## Slide 1: Performance Study of a Prototype Modular RICH Detector for EIC Experiments
Cheuk-Ping Wong
Georgia State University
For eRD14 Collaboration

## Slide 2: Outline
Electron Ion Collider
Prototype and Beam test
  Detector Design
  Beam Test Setup
Result
  Ring Finder Algorithm
  Cherenkov Ring Radius
  Number of Cherenkov Photons
Future Works
Accumulated hit map from simulation (left) and beam test (right) results

## Slide 3: Electron Ion Collider (EIC)
Advance the knowledge of nucleon structure
Final kaon and pion products
  SIDIS
  3D tomography of nucleon
  Gluon Saturation
  Gluon distribution inside proton

## Slide 4: Hadron Products Kinematic in EIC
rapidity
Final hadron energy (GeV)
Modular RICH
Notes: 10 GeV e- vs 100 GeV proton
Thick radiator become a problem when there are fringe field

## Slide 5
Prototype and Beam Test

## Slide 6: Design of 1st Modular RICH Prototype
Aerogel
Acrylic box
Hollow space
Fresnel lens
Sensor and readout
mirror
mirror
Aerogel | Thickness = 3.3cm Refractive index n = 1.03
Fresnel Lens | 262 grooves Focal length f = 7.62cm
Mirror set | On four sides: top, bottom, left and right
Sensor plane | Effective area = 9.6cm x 9.6cm Pixel size = 6mm x 6mm
Notes: Design of the 1st prototype

## Slide 7: Lens Based Design
Advantages of lens-based design:
  Transform circle plane image to a ring image  Sharper signal
  For all incident particles that move parallel to the z axis of the detector, the ring which is off center will be shifted toward to the center of the sensor plane
lens
Focal plane
Cherenkov photons
θ
θ
r
f
w/ Fresnel lens
w/o Fresnel lens
Incident particle
lens
Focal plane
Cherenkov photons
θ
θ
r
f
w/ Fresnel lens
w/o Fresnel lens
Incident particle

## Slide 8: 1st Prototype
Aerogel
Fresnel Lens
&
Mirror Set
Photon Sensor
&
Readout Electronics
Front
Back
Notes: Hamamatsu mutianode pmt.
Cover sensor plane

## Slide 9: Beam Test Setup at Fermilab
MTest facility at Fermilab
  120 GeV primary proton beam
  Low energy (down to 1 GeV) secondary pions, muons and electrons
Beam pipe
mRICH
M6 facility
Mtest facility
Beam test setup
Notes: Verify working principle of modular RICH detector
  Ring Radius
  Number of Cherenkov Photons

## Slide 10: Beam Test Setup
Beam direction
triggers
Hodoscope
Hodoscope
mRICH

## Slide 11: Beam Test Configurations
 | 120 GeV Proton | 8 GeV pion | 4 GeV pion
Full Setup with n=1.03 Aerogel | ✓ | ✓ | ✓
Full Setup with n=1.02 Aerogel | ✓ |  | 
Without Mirror | ✓ |  | 
Small beam size  quick tool for detector alignment

## Slide 12
Result

## Slide 13: Ring Finder Analysis
Ring Center Position
Accumulated Data of Entire Run
Hough Transform Algorithm

## Slide 14: Cherenkov Ring Image Reconstruction
Simulation
Beam test
Pixel amplitude
Num. of photon
Notes: Example of typical rings

## Slide 15: Cherenkov Ring Radius
Incident particle
Cherenkov photons
lens
Focal plane
θ’
θ
r
f
Aerogel
Air
θ
θ’
Ring size is independent on thickness of the aerogel or air gap
Proportional to focal length
Theoretical value of Cherenkov ring radius in modular RICH detector:
mm (120GeV/c proton)
Sensor plane setup

## Slide 16: Cherenkov Ring Radius
Simulation
Beam Test
Good ring:
radius is within expected range
Distance from the sensor center to the ring center is within 3mm
Notes: Since the Ring Finder algorithm will always give a a ring. We have to evaluate the found rings properties.

## Slide 17: Number of Cherenkov Photons per Event
(with n=1.03)
Fresnel lens transmission
Glass window transmission
Sensor quantum efficiency
Aerogel transmission
Estimated number of Cherenkov photons in modular RICH detector:
Maximum number of Cherenkov photons:
Fine structure const.
Thickness of radiator
β=v/c
Refractive index of radiator

## Slide 18: Number of Cherenkov Photons per Event
Simulation
Beam Test
Only consider the events that give good rings
Notes: Agree with theoretical number

## Slide 19: Summary
 | Theoretical number | Simulation | Beam Test
Cherenkov Ring Radius | 15.9mm | 15.5±0.1 mm | 15.7±0.4 mm
Num. of Cherenkov Photons | 10.33 | 11.0±2.8 | 12.8±3.2
Efficiency | / | 74.0% | 69.0%
Beam test result agrees with simulation result

## Slide 20
Future Work

## Slide 21: Simulation Study
Implement Pythyia simulation data to modular RICH detector
Integrate modular rich detector in EIC
mRICH wall on electron endcap in GEMC simulation

## Slide 22: Next Prototype
1st prototype | 2nd prototype
Acrylic box | Aluminum box
Including readout electronics | Decouple optical and electronics section to prevent overheating
Sensor pixel size = 6x6mm2 | Sensor size
Multianode PMT | PMT / MPPC array
Fresnel lens focal length =3” | Fresnel lens focal length =6”
Notes: opaque

## Slide 23: eRD14 Collaborators
Abilene Christian University
Argonne National Lab
Brookhaven National Lab
Catholic University of America
College of William & Mary
Duke University
Georgia State University
GSI Helmholtzzentrum für Schwerionenforschung GmbH
Howard University
INFN, Sezione di Ferrara
INFN, Sezione di Roma
Istituto Superiore di Sanità
Jefferson Lab
Los Alamos National Lab
Old Dominion University
Universidad Técnica Federico Santa María
University of Illinois
University of New Mexico
University of South Carolina
Yale University

## Slide 24
Back Up

## Slide 25: Cherenkov Ring Size from Simulation

## Slide 26: Cherenkov ring radius from different refractive indice of aerogel
Refractive index=1.02
Refractive index=1.047
-- Pion
-- Kaon

## Slide 27: Desired Pixel Size
Aerogel n=1.03
Naive case :
required pixel size = Difference in diameter between Cherenkov rings emitted by pion and kaon
1 pixel size
Ring from pion
Ring from kaon
Notes: GSU_NP_GrpMeeting 20160520

## Slide 28: Details of Detector Setup
4 sensors
4 glass windows
Side view
sensor
Glass window
Sensor plane viewed from the back
1 mm
1 mm
2mm
2mm
52 mm
48 mm
sensor

## Slide 29: Internal Reflection inside Glass Window
Material | Pyrex glass (Borosilicate glass)
Density | 2.23 g/cm3
Refractive index | 1.47
transmittance | 92% in 400-700nm wavelength region

## Slide 30: Event Display Comparison
Simulation (1,000 events)
Beam test result (1,214 events)
Pixel amplitude
Num. of photon
Notes: Accumulated Hit from the e

## Slide 31: Event Display Comparison
Simulation
Beam Test

## Slide 32: Ring Finder Analysis Procedure
Accumulated Data of Entire Run
Hough Transform Algorithm

## Slide 33: Radius (in each event) Distribution
rexpected
3.54mm
rexpected =18.7-3.54 (gap) ±0.60 ±3 (half of single pixel size)
=15.2 ±3.6mm
Radius of each photon hit from simulation result.
No Q.E. applied
r≈18.7±0.60 mm
Sensor 1
Sensor 2
Sensor 4
Sensor 3
Not on scale

## Slide 34: Weight Functions
√(a2+b2) (mm) / r (mm)

## Slide 35: Center Position (a,b)
Simulation
Beam Test