## Slide 1: SiPM Noise Simulation
y
HENRY KLEST
P
All copyright infringement is my own ☺
Aug. 9, 2024

## Slide 2: The Challenge
SiPMs are noisy
  Single-photon signals at O(MHz)
  Even worse once irradiated
Since the SciFi readout is longitudinally segmented, calibration of individual channels can be challenging
The MIP peak provides an ideal signal to use for a channel-by-channel calibration
Want to keep the signal amplitude of the MIP above the noise floor from the SiPMs

## Slide 3: The Mitigation Strategies
Reduce the SiPM noise per channel, or increase the MIP signal per channel
Noise Reduction Option | Pro | Con
S13 vs. S14 | Easy integration | Less Noise = Worse PDE
Reduce Temperature | Strong noise reduction | Hard integration
Replace SiPMs | Fresh sensors | $$$
Anneal SiPMs | Undo radiation damage | Hard integration(?)
Smaller readout channels | Better granularity | MIP shrinks too
MIP Improvement Option | Pro | Con
S13 vs. S14 | Easy integration | More PDE = More Noise
Silicone Cookie | Easy integration | ?
Better SciFis | Less attenuation, more light | $$$$$$$
Larger readout channels | More light | Noise SiPM Area
MIP Improvement Option | Pro | Con
S13 vs. S14 | Easy integration | More PDE = More Noise
Silicone Cookie | Easy integration | ?
Better SciFis | Less attenuation, more light | $$$$$$$
Larger readout channels | More light | 
For more detail on these, see our session in the Jan. collaboration meeting

## Slide 4: The Mitigation Strategies
Reduce the SiPM noise per channel, or increase the MIP signal per channel
Noise Reduction Option | Pro | Con
S13 vs. S14 | Easy integration | Less Noise = Worse PDE
Reduce Temperature | Strong noise reduction | Hard integration
Replace SiPMs | Fresh sensors | $$$
Anneal SiPMs | Undo radiation damage | Hard integration(?)
Smaller readout channels | Better granularity | MIP shrinks too
MIP Improvement Option | Pro | Con
S13 vs. S14 | Easy integration | More PDE = More Noise
Silicone Cookie | Easy integration | ?
Better SciFis | Less attenuation, more light | $$$$$$$
Larger readout channels | More light | Noise SiPM Area
MIP Improvement Option | Pro | Con
S13 vs. S14 | Easy integration | More PDE = More Noise
Silicone Cookie | Easy integration | ?
Better SciFis | Less attenuation, more light | $$$$$$$
Larger readout channels | More light | 
Let’s investigate these options a bit more…

## Slide 5: Readout Channel Splitting
Investigate the effect of splitting our current 1.2 x 1.2 cm2 channels into 2 or 4
12 mm
12 mm
DCR scales as SiPM area while MIP signal scales as path length
  Splitting in four reduces DCR by a factor of 4, signal by a factor of 2
  Splitting in two reduces DCR by a factor of 2, keeps MIP signal ~ the same
DCR is not linearly proportional to where can you set your threshold, needs to be simulated!
  DCR proportional to mean of pedestal, but we need to know the sigma!
Additional benefits of smaller channels:
  Reduces pulse size going into HGCROC
  Improves granularity for e/pi separation
  Reduces needed light guide length (?)
Splitting in two = sum orange + blue and green+purple

## Slide 6: Readout Channel Splitting
Investigate the effect of splitting our current 1.2 x 1.2 cm2 channels into 2 or 4
12 mm
12 mm
DCR scales as SiPM area while MIP signal scales as path length
  Splitting in four reduces DCR by a factor of 4, signal by a factor of 2
  Splitting in two reduces DCR by a factor of 2, keeps MIP signal ~ the same
DCR is not linearly proportional to where can you set your threshold, needs to be simulated!
  DCR proportional to mean of pedestal, but we need to know the sigma!
Additional benefits of smaller channels:
  Reduces pulse size going into HGCROC
  Improves granularity for e/pi separation
  Reduces needed light guide length (?)
Splitting in two = sum orange + blue and green+purple
This is probably worth a whole other talk…

## Slide 7: A word on annealing…
INFN Bologna successfully tested in-situ annealing via forward-bias of the SiPM
  Run a current through the diode until it heats to the desired temperature
This provides a convenient alternative to removing the SiPMs from the detector and putting them in an oven!
Achieved a factor ~50 (!!!) reduction in dark current after several days of heating at 150° C
  Very attractive option for us
  IF we can integrate it in the ESB
“Fraction of damage” =
Click here for Roberto's talk

## Slide 8: Simulation Technique
Throw waveforms at the dark count rates supplied to us by INFN Bologna for S14160-3050 SiPMs
  Various temperatures provided
  Both unirradiated and irradiated with 1E9 1 MeV neutron equivalent dose
Include the crosstalk numbers supplied by Hamamatsu
  This is important to determine the sigma of the noise!
Focus on irradiated sensors, since this is the concerning case for the MIP

## Slide 9: Baseline – 12 x 12 mm2
12x12 mm2
S14, 5°C, 1E9 Irradiated, No annealing
Strawman MIP
<Npe> = 8

## Slide 10: Baseline – 12 x 12 mm2
Strawman MIP
<Npe> = 8
12x12 mm2
S14, 5°C, 1E9 Irradiated, annealing factor 10

## Slide 11
6x6 mm2
S14, 5°C, 1E9 Irradiated, No annealing
6x12 mm2
S14, 5°C, 1E9 Irradiated, No annealing
Strawman MIP
<Npe> = 4
Strawman MIP
<Npe> = 8
MIP 2.5 “σ” above noise
MIP 1.7 “σ” above noise

## Slide 12
6x6 mm2
S14, 5°C, 1E9 Irradiated, annealing factor 10
6x12 mm2
S14, 5°C, 1E9 Irradiated, annealing factor 10
Strawman MIP
<Npe> = 4
Strawman MIP
<Npe> = 8
MIP 9.1 “σ” above noise
MIP 12.9 “σ” above noise

## Slide 13: To go even further…
3x12 mm2
S14, 5°C, 1E9 Irradiated, annealing factor 1
MIP 5.3 “σ” above noise
Strawman MIP
<Npe> = 8
12 mm
12 mm
Note that this case will only really be true for field-off runs of the collider
  Cosmics will rarely hit in the “aligned” orientation

## Slide 14: To go even further…
Note that this case will only really be true for field-off runs of the collider
  Cosmics will rarely hit in the “aligned” orientation
3x12 mm2
S14, 5°C, 1E9 Irradiated, annealing factor 10
MIP 18.9 “σ” above noise
Strawman MIP
<Npe> = 8
12 mm
12 mm

## Slide 15: Conclusions
If the annealing factor of 10 can be achieved, all schemes seem acceptable
  If not, the 12 mm x 12 mm and 6 mm x 6 mm are in trouble, 6 mm x 12 mm looks okay still
  The 6x12 mm option provides decent headroom at little cost
    Requires individual 6x6mm SiPMs and not arrays
Caveats
  We assumed as our strawman an average of 8 p.e. for the MIP
    Single-clad Kuraray was something like 6.4 p.e. on average in Maria’s previous sims, Luxium was 5.1 p.e.
    Tegan’s light guide studies suggest we gain more from the silicone cookie than we assumed at that time
    6.4 would be okay for the 2x1 split
  No investigation of splitting effect on signal shape!
    For fixed external circuitry, the smaller arrays will have faster signals (SiPM capacitance)
    This will reduce their sigma somewhat, but shorter signals will have fewer useful ADC samples in HGCROC

## Slide 16: Backup

## Slide 18: Backup Backup (January)

## Slide 19: Dark Currents from INFN Measurements
Scale currents by gain & qe to get a dark count rate
  This is a bit naïve, but Roberto indicated it should be alright
Order of magnitude increase after 1E9 1 MeV neq dose
  Our conservative estimate of dose for lifetime of experiment was 3E10

## Slide 20: HGCROC Signals
Pulse from charge injection tests on HGCROC
  Kindly supplied by Norbert
  Digitized much faster than HGCROC actually digitizes
  Landau fit
  Peak set to 1 photoelectron
For now, I just do the stupid thing and throw these distributions with the frequency of the DCR
The reality of how often we will see hits from noise will depend on what ADC value we call a “hit”

## Slide 21: Waveforms
Created by Monte Carlo which throws Landau distributions with parameters taken from the HGCROC charge injection signal at different time slices with probability defined by the DCR
Crosstalk produces pulses 2x or 3x as high as the standard single-photon pulse
  Here a 7% crosstalk probability is assumed for both S14160 and S13360
  Final crosstalk numbers will depend on the optical coupling to the lightguide

## Slide 22: Temperature Dependence
Both sensors look reasonably good before irradiation, could easily set a threshold at 4 or 5 p.e.

## Slide 23: Radiation Damage
0 °C not cool enough to save the MIP for either SiPM after 1E9 1 MeV neq dose
This assumes that the dark current produced by irradiation translates directly into dark counts, which is the worst case scenario
Keep in mind that this represents only ~1/30th of the 10-year expected dose

## Slide 24: -30 °C
Looks acceptable, as expected since -30C is the nominal temperature for the single-photon counting in the dRICH
DCR is an exponential function of temperature
Integration of sub-zero cooling would likely be very challenging, but in principle possible since the dRICH is already doing it
Sub-Zero

## Slide 25: Threshold
HGCROC will report information whenever the analog input is above a threshold
Given HGCROC pulse shapes, seems that something like ~15 MHz could be a reasonable goal for maximum DCR
  In 100 μs, expect analog signal above a 5 Npe threshold ~0.05% of the time

## Slide 26: Summing Channels
How can we reach 15 MHz?
  What matters for keeping the MIP is that there are less than 15 MHz of noise in the area that the MIP photons are hitting
Splitting the 4x4 array into four optically isolated 2x2 arrays could ~half the noise on the MIP
  Set thresholds at ~ ¼ the value of the 4x4 array
  Four light guides covering smaller areas
  Unlike a shower, the MIP energy deposit in the SciFi can be approximated as a line
    Will typically send all its photons to ~two of the four SiPMs!
  Half the surface area of active SiPM means half the noise

## Slide 27: Discussion
Even with splitting readout channels from 4x4 summed to 2x2 summed, can’t reach 15 MHz for irradiated SiPMs even at 0 °C
  1x1 channels? 5760*16 = 92k readout channels
Effects of annealing between runs not considered
  Time heals all wounds
  Some studies show 1 month of sitting at room temp. after proton irradiation can decrease dark current by a factor of 2
Or do as Craig Woody said and use the MIP to cross-calibrate in the early stages of the experiment, then trust that calibration once the MIP is below threshold
2
2

## Slide 28
Per channel, expect 0.6% of samples to be above a 5 p.e. threshold (0.24 MHz)
Fraction of time spent above a threshold of NSPE (1 ms simulated)
2
Per channel, expect 11% of samples to be above a 5 p.e. threshold (4.4 MHz)
Ignoring time binning effects

## Slide 29: HGCROC Bandwidth
2x2 array in 100 μs
HGCROC sends 32 bits/hit
Currently each HGCROC has 2 x 1.28 Gbps links
Max hit rate above threshold: 80 MHz for all channels on that HGCROC
Anticipate 60 Channels/HGCROC
Max hit rate of ~1.3 MHz/channel can be passed on by HGCROC
  For irradiated S13360 with readout split into 2x2, expect total DCR/channel of 12.7 MHz, want a threshold at ~2-3 SPE
    Above 2 PE 10% of the time ~ 4 MHz
    above 3 PE 2% of the time ~ 0.8 MHz
    Cross-talk has much larger effect on operation at lower thresholds
  Rate/channel situation is slightly worse for split readout due to cross-talk

## Slide 30: Conclusion
With measurements from INFN and HGCROC signals, made some first estimates for what waveforms will look like
Irradiated sensors very likely to lose the MIP without intervention
  Additional cooling
  Annealing
  Further splitting of channels
Caveats:
  Dark Current to DCR conversion
  Pulse shapes will depend on how many SiPMs are ganged together
  No room-temperature annealing effect

## Slide 31: BACKUP

## Slide 32: HGCROC ADC Resolution
Resolution of 0.4 fC ~ 2500 electrons
Much smaller than the signal from a single SPAD firing in the SiPM
  S13360 Gain 1.7E6
  S14160 Gain 2.5E6

## Slide 35: CONSIDERATIONS
Photon detection efficiency
Noise
  Low dark count rate necessary to see small signals from e.g. MIPs
  Low crosstalk & afterpulsing preferable
Pulse shape
  Fast rise time for z-position resolution
    Time-projection Calorimeter (TPC)
  Short tail to reduce signal pileup
  Consistent over time
  Proportional to Npe
Consider the performance in the BIC of Hamamatsu S13660 and S14160 Series
  Biggest challenge is seeing the MIP at midrapidity, use this as a benchmark

## Slide 36: PDE
PDE important to minimize statistical error on energy measurement & maximize efficiency for small signals
50 micron pixel size chosen
  Trade off between geometric efficiency & saturation point
Relevant wavelengths determined by emission spectrum of scintillating fibers
  Both SiPMs peak in PDE near the emission peak around 450 nm
S14160 peaks at ~50% PDE
S13360 peaks at ~40% PDE
In PDE, S14160 series wins
S14160
S13360
Kuraray Fiber

## Slide 37: NOISE
Dark count rate (DCR) determines threshold
  MIPs at midrapidity will generate 3-6 Npe on average
    Would be good to have threshold slightly below MIP
DCR above a few 10s of MHz will endanger the MIP
Specification | S13360-3050 (3x3 mm) | S14160-3050 (3x3 mm)
DCR (Typ.) | 500 kHz | 1 MHz***
Crosstalk (%) | 3 | 7
*** Estimated, differing values in literature
Signal will gang 1.2 cm x 1.2 cm area (16 3x3 mm or 4 6x6 mm)
  DCR for one BIC channel will be ~16x value in table
Plan to test S14160 SiPMs at ANL & Regina

## Slide 38: PULSE SHAPE
Fast rise time improves position resolution in z-direction
  If not limited by other factors like readout or scintillation decay
Fast fall time reduces pileup of signals (and dark counts)
  Shape will depend heavily on the readout circuit
Appears that S14160 has fast rise time, slower fall time than S13360
  Challenging to compare between papers due to differences in readout
  Will soon compare the two in an identical setup at ANL
Should converge on a reasonable target for these parameters based on physics
  Keeping the MIP, low energy ɣ
“Nominal” fall time
“long” fall time
“Short” fall time
Similar to HGCROC Default

## Slide 39
S13360 S14160
✅
✅
✅
✅
✅
✅
✅
✅
❌
✅
~
✅
✅
❌❓
❌
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅
✅

## Slide 40: OPEN/DISCUSSION QUESTIONS
What DCR can we really tolerate?
  Depends on signal shape, shorter fall time better
  With HGCROC-length signals, 10 MHz too large if threshold is 3 Npe
Do we want to actively temperature control the SiPMs?
  Maintain a constant DCR by decreasing temp as rad damage accumulates
  More effective with S13360 series than S14160
If we go with the S13360 series, how can we compensate the loss in PDE?
Does the lower operating voltage of the S14160 series benefit us?

## Slide 42: PDE: GlueX SiPM Parameters
The Hamamatsu specification sheets provide the recommended operating voltage for a nominal gain of 7.5 × 105 , although our measurements indicate lower gains (Fig. 4a). We determined that this operational voltage on average corresponds to 0.9 V above breakdown; to obtain our setting at an overvoltage of 1.4 V, we added 0.5 V and then adjusted for temperature.
PDE ~33%
https://arxiv.org/abs/1801.03088
Hamamatsu Multi-Pixel Photon Counter (MPPC) S12045(X):
16 x 3600 pixels (50 um)

## Slide 43: Pixel Size and Number of Pixels
Defined by photoelectron statistics and energy range to be measured
Energy measurement ranges in BECal:
Shall provide photon measurements up to 10 GeV (F-DET-ECAL-BAR.2) and down to 100 MeV (F-DET-ECAL.9)
Shall provide electron ID up to 50 GeV and down to 1 GeV and below (F-DET-ECAL-BAR.1)
  Electron energy measurement needed for e/π separation only (straightforward at high energies)
Reasonable performance for MIPs needed for calibration and for muon ID
Largest energy deposit occurs for particles at large η (steep angle) where the pathlength in a cell is maximal and the attenuation is minimal.
13.5 GeV
4.3 GeV
7.1 GeV
ePIC GEANT4 simulation 10 GeV photons at η ~ -1.7
ePIC GEANT4 simulation 19 GeV electrons at η ~ -1.7
ePIC GEANT4 simulation 50 GeV electrons at η ~ 1.4
extreme case

## Slide 44: Photoelectron statistics
2023 Hall D, Baby BCal, 3.9 GeV e+
1000 phe/GeV
per side
not corrected
for 29 cm
atten.
From our 2023 Hall D tests using GlueX SiPMs and double-clad Kuraray fibers: 1000 phe/GeV per side for showers at the center of the Baby BCAL prototype
Corrected for attenuation: 1077 phe/GeV* per side
We can scale these results for the ePIC Barrel ECal*:
x 1.5 factor improvement in SiPM photon detection efficiency
x 1.16 factor to account for better optical coupling
x 0.69 reduction accounting for single-clad Kuraray fibers
This gives ~ 1239 phe/GeV per side (fully corrected for attenuation)
10 GeV ɣ at η ~ -1.7: 5560 phe → 9.8 % max SiPM occupancy
19 GeV e- at η ~ -1.7: 9181 phe → 16.1 % max SiPM occupancy
50 GeV e- at η ~ 1.4 (most extreme case): 17456 phe → 30.1% max SiPM occupancy
* See backup slide for the attenuation length measurement and
extraction of those factors
2008 Hall B beam test, photons
660 phe/GeV
per side
not corrected
for 195 cm atten.
Well below the region where large nonlinearities in the SiPM response are expected in almost all cases.
Small non-linear effects possible for some ultra-high energy electrons, which is acceptable (e-π separation straightforward).

## Slide 46: NOISE
Dark count rate (DCR) determines threshold
  MIPs at midrapidity will generate 3-6 Npe on average
    Would be good to have threshold slightly below MIP
DCR above a few 10s of MHz will endanger the MIP
Specification | S13360-3050 (3x3 mm) | S14160-3050 (3x3 mm)
DCR (Typ.) | 500 kHz | 1 MHz***
Crosstalk (%) | 3 | 7
*** Differing values in literature
Signal will gang 1.2 cm x 1.2 cm area (16 3x3 mm or 4 6x6 mm)
  DCR for one BIC channel will be ~16x value in table
Plan to test S14160 SiPMs at ANL & Regina

## Slide 47
S13360-3050 (3x3 mm)
S14160-3050 (3x3 mm)

## Slide 48: PULSE SHAPE
Pulse shape strongly defined by how signals are handled
S14160 has faster rise time, slower fall time
Larger SiPMs (6x6 mm) have ~2x longer fall times due to capacitance
  Can we mitigate this in our ganging scheme?

## Slide 49: NOISE
Dark count rate (DCR) determines threshold
  MIPs at midrapidity will generate 3-6 Npe on average
    Would be good to have threshold slightly below MIP
DCR above a few 10s of MHz at the readout will swamp the MIP
Literature seems divided on noise characteristics of S14160 series
  Plan to test S14160 SiPMs at ANL & Regina

## Slide 50: WAVEFORMS
Parameterize S14161 waveform based on presentation from AMS-100 (here)
Exponential rise and exponential fall
  Different time constants
Pulse height around 0.045 mV
  Take this as 1 Npe

## Slide 51: WAVEFORMS
Agreement not good but also not so terrible
Tail a bit wider in the data
Good enough for now

## Slide 52: WAVEFORMS
Agreement not good but also not so terrible
Tail a bit wider in the data
Good enough for now

## Slide 53: WAVEFORMS
Agreement not good but also not so terrible
Tail a bit wider in the data
Good enough for now

## Slide 55: WAVEFORMS
Monte Carlo throwing signals with expected rate
  32 MHz
  1 microsecond
Crosstalk probability of 7% included (should it be, or is it included in the number from Hamamatsu?)
  Up to two crosstalk hits
    3 and greater is a less than 1% effect
Line drawn at 3 * single photoelectron peak

## Slide 56: HITS IN HGCROC WINDOW
Take 25 ns window of HGCROC
Poissonian distribution with a mean of 0.8
  25 ns * 32 MHz
If threshold is set to 3 * SPE pulse height, 4% of time bins will be triggered
  4% of the channels of the detector will be active in ToT mode at any given time

## Slide 57
Threshold of 3 p.e. likely excluded if DCR reaches 100 MHz
  This also poses an issue because we can’t get around it with timing cuts in the same way as the dRICH, the detector could have a signal at any time
    Bunch crossings every 10 ns, shorter than light propagation time

## Slide 58
Threshold (p.e.) | Prob. Above threshold @ 1 MHz | Prob. Above threshold @ 10 MHz | Prob. Above threshold @ 30 MHz | Prob. Above threshold @ 50 MHz | Prob. Above threshold @ 100 MHz
2 | 0.01% | 2% | 29% | 69% | 99%
3 | 0.0005% | 0.3% | 8% | 36% | 94%
4 | 0% | 0.04% | 1.7% | 14% | 79%
5 | 0% | 0.005% | 0.2% | 4% | 57%
6 | 0% | 0%* | 0.03% | 1.1% | 35%
7 | 0% | 0%* | 0.005% | 0.4% | 17%
Numerical uncertainty of 0.03%

## Slide 60: TEMPERATURE DEPENDENCE
Conventional wisdom is that DCR is halved for every decrease of 10° C
“Single-channel” here refers to 1/16 of a 4x4 array (S14161-6050HS-04)
  DCR numbers for ganged array should be 16x higher
To reach the ~4 MHz of GlueX with S14161-6050HS-04, need to go to -20° C or lower
Proton irradiation of SiPM arrays for POLAR-2

## Slide 61: TEMPERATURE DEPENDENCE
The authors of this paper report that DCR of the S14161 is 60% higher than S13361 at 25° C, and a factor of 5 higher at -20° C
  The DCR of the S14161 is apparently a much slower function of temperature
  This is bad, because it renders less effective the only handle we have over the DCR
  On the flip side, probably the DCR increases less if we go above 25° C…
On such a critical point, should consult an expert (Hamamatsu directly?) to see if this behavior is expected or not

## Slide 62: RADIATION DAMAGE
Pre-radiation DCR around 3 MHz (single channel)
  At 3V overvoltage
After ~200 Rad of proton radiation (and two months of waiting), DCR larger by factor of 4
  Half our expected dose
Proton irradiation of SiPM arrays for POLAR-2

## Slide 63: RADIATION DAMAGE
If we take the numbers provided in this paper seriously, expect 192 MHz of DCR after 200 Rad of radiation damage at room temperature
This is clearly too large, likely would swamp the MIP
  Threshold would need to be set at something like 9 Npe or higher

## Slide 64
S14161
S13361