## Slide 1: Machine Protection
October 7th 2024
Michael Costanzo

## Slide 2: Machine Protection
October 7th 2024
Michael Costanzo

## Slide 3: Overview
What is machine protection?
Hazard sources
Human Operators
Protection Approaches
Relation to ML / AI

## Slide 4: What Machine Protection Isn’t
It is not personnel protection
  Personnel protection is a credited control system, distinct from machine protection
  At RHIC this is the Particle Accelerator Safety System (PASS)
  The primary role of PASS is to control and manage human access to beam areas
  A mutex between beam and humans

## Slide 5: What Machine Protection Is
System(s) to prevent damage to machine components that:
Are expensive
Cause down time
Take a long time to repair
Could have programmatic impacts

## Slide 6: Protection From What?
The general themes are stored energy and energy density
  Energy of a particle beam
  Highly focused beam incident on a surface
  Current in superconducting systems
  Protect the machine from itself

## Slide 7: Human Operators
Operators and specialists issue control inputs
  There’s an enormous parameter space
  Sequencing for many operations is crucial
  Contexts are often changing:
    Different beams
    Different modes
    Non-continuous measurements
  A waterfall of statuses, readbacks, and alarms

## Slide 8: Timescale
Machine configuration can evolve rapidly and unexpectedly
  Beams travel on the order of c
  Time budget to prevent damage often in microseconds
  A significant amount of alarms occur after the fact
  No room for humans in the loop
CONDITION
DETECTION
LOGIC &
PROPAGATION
MITIGATION
RESPONSE
Total Response Budget

## Slide 9: A Layered View
Hardware
Device Limits
Application Level
Administrative Control
Elevated privileges
Required to change limits

## Slide 10: Beam Permit System
Key Inputs:
  BPMs
  Loss Monitors
  Quench Detection
Mitigation
  Abort Kickers
  Beamstops
  Altering permit configuration requires elevated privileges

## Slide 11: MPS, Largely Independent of Operators
Operators need not intervene for MPS to take action
Beam Permit is an operating constraint
Within the ‘permit envelope’, operators exercise their discretion
Altering the Permit system is under administrative control

## Slide 12: AI / ML as an operating agent
Does not bypass the protection layers
Must stay within the ‘Permit envelope’, just like human operators
No privilege to alter Permit configuration
Functionally comparable to existing feedback systems

## Slide 13: AI / ML as a Detection Source
Possible early warning / preventative agent
Potentially able to synthesize large, heterogeneous data streams
May find subtle correlations and precursors
Need training data
Beam aborts are sparse (relative to the volume of data)

## Slide 14: Summary
Machine Protection is fundamental to operational accelerators
Machine Protection is intentionally autonomous
Operators work within the MPS ‘envelope’
AI/ML agents must also work within the MPS ‘envelope’
AI/ML also offers the prospect of enhanced protection

## Slide 15: Questions?
Comments?