## Slide 1: Introduction of sPHENIX & INTT
RIKEN/RBRC
Itaru Nakagawa

## Slide 2: Basics of Particle Interaction
RIKEN/RBRC
Itaru Nakagawa

## Slide 3
Accelerator
Detector
QGP
Notes: What is this object made of?

## Slide 4
sPHENIX detector
  General concept of the modern particle collider
    Particle flow algorithm
    The technologies
      Calorimeter: sampling (SciFi, Sandwiched, Cherenkov light detection) and homogeneous (CMS ECal made of Lead Tungstate scintillating crystal). The PMT, SiPM
      Tracker: TPC, wire chamber, silicon, etc
      Magnet: charged particle curvature by Solenoid, etc
    What is difference between Electromagnetic and Hadronic calorimeters (interaction length and radiation length)?
    The particle identification (dE/dx of TPC, TOF, AC-LGAD, etc)
  Each subsystem of sPHENIX
    Geometry, technology, specification and performance, and the role of each subsystem
  Review of the sPHENIX construction
  Some physics projections
INTT
  Introduction to silicon detector, the technology
  The detail specifications of INTT
  Role of INTT in more detail
    The (out-time) pile-up suppression
      What is pile-up?
    How the single-bunch-crossing relevant to tracking (which is important to spin program, but why?)
  The story of INTT (from scratch to ladder production to detector installation to data taking)
    Some achievements of INTT (may have some overlaps with the INTT review talk, but should be fine)

## Slide 5: Basics
~particle interactions in matter~

## Slide 6
P Ra

## Slide 8
I am exhausted !
You’ve lost energy by interacting with people …

## Slide 9: Interaction of particles with matter
Bernd Surrow
NEPPSRIII
Overview of interaction processes
Particles created in the collision of high- energy particle beams experience electromagnetic and/or nuclear interactions in the detector material they pass through
Understanding these processes are vital for the design of any detector system!
Main processes for charged particles:
  Ionization
  Cherenkov radiation
  Bremsstrahlung
Photoelectric effect
Compton scattering
Pair production
Main processes for photons:
Lead (Z=82)
Craigville, Cape Cod, 08/23/2004
Lead (Z=82)
C. Fabjan, 1987
C. Fabjan, 1987
Depending on mass, momentum, species…

## Slide 10: Ionization Energy Loss

## Slide 11: Bethe-Bloch Formula
Bernd Surrow
NEPPSRIII
loss
Ionization
  Bethe-Bloch equation: Mean energy (or stopping power)
-dE/dx in units of:
(MeV/cm)/(g/cm3)=(MeV cm2/g)
-dE/x for charged particles: M » me
with:
Note:
Density () and shell (C) corrections at high and low energies, respectively
-dE/dx for electrons modified due to the kinematics, spin and identity of the incident electron with the medium electrons
Minimum at approx.:
(-dE/dx of relativistic particles: Close to minimum-ionizing particle (MIP)
PDG, 2004
Craigville, Cape Cod, 08/23/2004

## Slide 12: Bethe-Block Formula
https://pdg.lbl.gov/2006/reviews/passagerpp.pdf

## Slide 13: dE/dx for Various Elements
Bernd Su
NEPPSRIII
Ionization
Medium dependence
  Weak dependence on the medium, since Z/A ≈ 0.5:
Craigville, Cape Cod, 08/23/2004
PDG, 2004
Scintillator: dE/dx|min ≈ 2MeV/cm
Tungsten: dE/dx|min ≈ 22MeV/cm
Material | Z | A | Z/A | dE/dx min (MeVcm2/g) | Density (g/cm3)
H2 (liquid) | 1 | 1.008 | 0.992 | 4.034 | 0.0708
He | 2 | 4.002 | 0.500 | 1.937 | 0.125
C | 6 | 12.01 | 0.500 | 1.745 | 2.27
Al | 13 | 26.98 | 0.482 | 1.615 | 2.70
Cu | 29 | 63.55 | 0.456 | 1.403 | 8.96
Pb | 82 | 207.2 | 0.396 | 1.123 | 11.4
W | 74 | 183.8 | 0.403 | 1.145 | 19.3
U | 92 | 238.0 | 0.387 | 1.082 | 19.0
Scint. |  |  | 0.538 | 1.936 | 1.03
BGO |  |  | 0.421 | 1.251 | 7.10
CsI |  |  | 0.416 | 1.243 | 4.53
NaI |  |  | 0.427 | 1.305 | 3.67

## Slide 14: What do you drop?
https://www.photo-ac.com/main/search?q=この先急カーブ&srt=dlrank

## Slide 15: Radiative Energy Loss
https://www.cloudylabs.fr/wp/les-processus-de-pertes-denergie-des-particules/
Attractive Force by Coulomb Field
Nucleus

## Slide 16: Bremsstrahlung : electromagnetic radiative energy loss
A decelerated or accelerated charged particle radiates photons. The mean radiative energy loss is given by :
−
dE rad
dx
(
MeV g/ cm2
)=
0.3071
A (g) π
m
α 2 2 e
Z z ( )
2
m me
E 183
Z1/ 3
ln( )
medium atomic number
incoming particle energy
incoming particle mass
incoming particle charge state
fine structure constant = 1/137
m
m
( z ,m)=( e ) z2
dx
dE rad dErad
dx
(e−)
The mean radiative energy loss of a particle of charge z and mass m is a function of the mean radiative energy loss of an electron :
2
Electrons are much more sensitive to this effect.
http://lpsc.in2p3.fr/collot

## Slide 17: Radiation Length X0
induced by atomic electrons :
dx
rad
−dE (
e−)=4 α N A
Z ( Z +1) A
e
2
r E ln
Z
1/ 3
( 183 )
classical radius of electron : r e=α / me
e
rad
−dE ( −)= E
dx X
0
which can be rewritten as :
0
where X is the medium radiation length
then over a path x in the medium, the mean radiated energy of an electron reads :
Erad (e−)=E (1−e−x / X 0)
where x is expressed in cm or g/cm2
0
2
X ( g / cm )=
716.4 A ( g )
Z1/2
Z ( Z +1) ln ( 287 )
and :
http://lpsc.in2p3.fr/collot

## Slide 18
0
2
X ( g / cm )=
716.4 A ( g )
Z1/2
Z ( Z +1) ln ( 287 )
Radiation Length X0 for Various Elements
Bremsstrahlung
  Material dependence in radiation length X0
  Critical energy:
Material | Z | A | Z/A | X0 (cm) | Density (g/cm3)
H2 (liquid) | 1 | 1.008 | 0.992 | 866 | 0.0708
He | 2 | 4.002 | 0.500 | 756 | 0.125
C | 6 | 12.01 | 0.500 | 18.8 | 2.27
Al | 13 | 26.98 | 0.482 | 8.9 | 2.70
Cu | 29 | 63.55 | 0.456 | 1.43 | 8.96
Pb | 82 | 207.2 | 0.396 | 0.56 | 11.4
W | 74 | 183.8 | 0.403 | 0.35 | 19.3
U | 92 | 238.0 | 0.387 | 0.32 | 19.0
Scint. |  |  | 0.538 | 42.4 | 1.03
BGO |  |  | 0.421 | 1.12 | 7.10
CsI |  |  | 0.416 | 1.85 | 4.53
NaI |  |  | 0.427 | 2.59 | 3.67

## Slide 19: Cherenkov Radiation
Cherenkov radiation
  Definition: Cherenkov radiation arises when a charged particle in a material moves faster than the speed of light in that same medium:
Condition for Cherenkov radiation to occur:
Energy emitted per unit path length:
Example: Lead-glass (Passive absorber material = Active detector
material) calorimeter (Type SF5):
Density:  = 4.08g/cm
 Index of refraction: n = 1.67
Radiation length: X0 = 2.54cm
Bernd Surrow
NEPPSRIII
Craigville, Cape Cod, 08/23/2004

## Slide 20: Stopping Power of Minimum Ionazation Particle
https://pdg.lbl.gov/2006/reviews/passagerpp.pdf
https://link.springer.com/referenceworkentry/10.1007/978-1-4419-0720-2_8/figures/3_8
MIP

## Slide 21: Stopping Power of Minimum Ionazation Particle
MIP
https://www.researchgate.net/figure/Average-energy-loss-of-muons-in-iron_fig2_4154863

## Slide 22: Photon induced Electrons

## Slide 23: Interaction of photon with matter
Interactions of photons with matter
  Photoelectric effect
For E « mec2 and the fact that for E above the K shell, almost only K electrons are involved one finds:
(Klein-Nishina)
Atomic Compton cross-section:
Compton scattering
Assume electrons as quasi-free and E » mec2
:
PDG, 2004

## Slide 24: Interaction of photon with matter
Interactions of photons with matter
  Pair production
Absorption coefficient
Total probability for  inter- action in matter:
Probability per unit length or total absorption coefficient (Inverse of absorption length  of ):
X0 (Pb) = 6.4 g/cm2
PDG, 2004

## Slide 25
Thickness
Transverse Size
…
Eventually original energy is absorbed in the matter

## Slide 26: Electro-Magnetic Shower
Ends up with multiple particles and the primary particle may stop in the material
https://www.physi.uni-heidelberg.de/~sma/teaching/GraduateDays2017/sma_Detectors_4_Calorimeters.pdf

## Slide 27: Nuclear Interaction
Excitation and finally breakup of nucleus: nuclear fragments and production of secondary particles
For high energies (> 1GeV) the cross-sections depend only little on the energy and on the type of the incident particle (p, , K, …)
Define in analogy to X0 a hadronic interaction length I:
Nuclear interactions
  The interaction of energetic hadrons (charged or neutral) is determined by various nuclear processes:
Multiplicity  ln(E) Pt < 1 GeV/c

## Slide 28
Comparison of nuclear interaction length (in cm) and radiation length (in cm)
Material | Z | A | Z/A | X0 (cm) | I (cm) | Density (g/cm3)
H2 (liquid) | 1 | 1.008 | 0.992 | 866 | 718 | 0.0708
He | 2 | 4.002 | 0.500 | 756 | 520 | 0.125
C | 6 | 12.01 | 0.500 | 18.8 | 38.1 | 2.27
Al | 13 | 26.98 | 0.482 | 8.9 | 39.4 | 2.70
Cu | 29 | 63.55 | 0.456 | 1.43 | 15.1 | 8.96
Pb | 82 | 207.2 | 0.396 | 0.56 | 17.1 | 11.4
W | 74 | 183.8 | 0.403 | 0.35 | 9.58 | 19.3
U | 92 | 238.0 | 0.387 | 0.32 | 10.5 | 19.0
Scint. |  |  | 0.538 | 42.4 | 81.5 | 1.03
BGO |  |  | 0.421 | 1.12 | 22.1 | 7.10
CsI |  |  | 0.416 | 1.85 | 36.9 | 4.53
NaI |  |  | 0.427 | 2.59 | 41.1 | 3.67
I
X0
Z
Nuclear Interaction Length in Various Elements
X0, 0 [cm]

## Slide 29: EM vs Hadron showers
Shower profile
C. Fabjan, 1987
D. Wegener, 2001
6GeV electrons in different materials:
C. Fabjan, 1987
MC simulation:

## Slide 30
sPHENIX Detectors
Calorimetry
Minimum Bias Detector (MBD)
Event Plane (sEPD) (not shown)
Time Projection Chamber (TPC)
(TPOT not shown)
Intermediate Tracker (INTT)
MicroVertex Detector (MVTX)
Hadronic Calorimeters
Outer
Inner
Electromagnetic Calorimeter
Tracking
Trigger/event characterization:

## Slide 31: sPHENIX Detector
Calorimeter system
oHCal
iHCal
Tracking
system
oHCal
MAGNET
MVTX
INTT
TPC
EMCal
iHCal
oHCal
sEPD
MBD
◙ 1.4T Solenoid from BaBar
◙ Hermetic coverage:
|η|<1.1, 2π in φ
◙ Large-acceptance EM+H calorimeters: brings first full jet reconstruction & b-jet tagging at RHIC!!
◙ High data rates: 15 kHz for
all subdetectors
◙ Precise tracking with tracking system in stream readout
2023 : Commissioning Au+Au
2024 : p+p, Au+Au
2025 : Au+Au … p+A?
200GeV
TPOT

## Slide 32: Modern Experimental Detector Layout