## Slide 1: Bonding Geometries in the Current Stave/Tooling Design
Adam Huddart
ePIC F2F - 03/10/2024

## Slide 2: Introduction
3 Bonding Locations
  ASIC to EIC-LAS LEC
  ASIC to bridge FPC (or carrier if integrated)
  Bridge FPC (or carrier) to Primary FPC

## Slide 3: Conceptual FPC Layout
Traces on the top wing of the FPC (approx. 7mm wide)
  Majority covered by carbon fibre skin
  Cutouts in carbon fibre skin for access to bonding locations
FPC

## Slide 4: Bridge FPC to Primary FPC
Tab Bond
  Curvature of stave ends before bond location
    Flat surface (at angle)
  Bonding surface fully backed by K9 foam
K9 Foam Block
Bridge FPC
Primary FPC
Bond Location

## Slide 5: Bridge FPC to Primary FPC
Curvature Display (Black is flat)
Tab Bond
  Curvature of stave ends before bond location
    Flat surface (at angle)
  Bonding surface fully backed by K9 foam
Bond Region

## Slide 6: ASIC to Bridge FPC
Wire Bond
  Bond connection made on module assembly tooling
    ASIC is adhesively mounted to Kapton carrier
    Assembled Flat

## Slide 7: ASIC to Bridge FPC
Wire Bond
  Bond connection made on module assembly tooling
    ASIC is adhesively mounted to Kapton carrier
    Assembled Flat

## Slide 8: ASIC to Bridge FPC
Wire Bond
  Bond connection made on module assembly tooling
    ASIC is adhesively mounted to Kapton carrier
    Assembled Flat
    Kapton carrier held against module tooling with vacuum pad

## Slide 9: ASIC to Bridge FPC
Wire Bond
  Bond connection made on module assembly tooling
    ASIC is adhesively mounted to Kapton carrier
    Assembled Flat
    Kapton carrier held against module tooling with vacuum pad
    Bonding surfaces are flat but at an angle
    Supported on Aluminium
      (2 glue layers, ASIC and Kapton carrier)

## Slide 10: ASIC to EIC-LAS LEC
Wire bond on module assembly tool
LEC well constrained by EIC-LAS vacuum chuck
Wire Bond
  Surface of the ASIC flat
  LEC curved with 180mm diameter
Only shown wire bond parallel to the ASIC, width of pads on LEC unknown
Curvature Display (Black is flat)

## Slide 11: ASIC to EIC-LAS LEC
Alternatively, we could wire bond once adhesively mounted to the stave
Pros
  ASIC will be in its final resting position, less likely to damage bond during module installation
Cons
  Access more limited
  Less rigid mounting surface
  Module can’t be tested on assembly tooling

## Slide 12: Conclusions
2 out of 3 bonding operation are flat even with curved stave
Flat stave would remove the odd angle (current setup requires tooling to provide a horizontal bonding surface)
ASIC to EIC-LAS LEC wire bond would be a flat interface