## Slide 1: B0 tasks overview: vacuum
Vacuum
    Free space in front is currently < 5cm
      Gate-valve: bellows servicing the B0 will be on the IP side of the beampipe, between the valve and endcap. Vertical placement is preferred.
      Z-thickness of AC-LGAD layers ( needs to be <5cm). Readout boards/VTRX+
  Stay-clear area near the beam-pipe:
      2mm spacing needed between calorimeter/tracking layers and the beampipe. Depending on the bake-out procedure this distance could be ca 5mm ( temperature tolerance of AC-LGADs needs to be checked)
      Fernando/Christophe: The operating temperature for the ASICs is limited to 70 degree C (not guaranteed above this). Un-powered, the ASICs survive to about 120 degree C. However, the limitation is then determined by other components, such as PCB, solder, etc.
      Bake-out temperature?
Caption

## Slide 2: B0 tasks overview: tracker
AC-LGAD tracker
      Z-thickness of AC-LGAD layers ( needs to be <5cm).
      Location for Readout boards
        FTOF layout - min RD3 ( 3x4 =12 EICROCS per board)
        Decouple Modules ( AC-LGAD+ EICROC and Readout Boards) => cable length < 2m ( Fernando/Christophe: The HGCROC and ALTIROC ASICs -similar to the EICROC - were tested with 2 m long cables on the outputs and they worked well at 1.28 Gbps. )
        PCB board for HV/LV, etc distribution ?
      Cooling
      Geant4 simulation with actual sensor layout
      Installation
Yellow Module== 4EICROCs

## Slide 3: B0 tasks overview: EMCAL
EMCAL and integration with B0-magnet:
    Mechanical support from the back-side of B0 ( heavy weight)
  Assembly/installation sequence:
        B0-EMCAL assembly: glue or a frame for individual crystals?
        B0-EMCAL how to attach SiPM boards
        The mechanical structure and calorimeter modules without electronics will be installed in the assembly hall ( need to know B0-magnet availability, lab space for assembly) :
          Installation of crystals inside B0. B0 magnet with crystals will be transported to the hall (crane?)
          Beam commissioning
          Installation of SiPMs/readout on calorimeters
          Installation of AC-LGAD tracking layers
    Balcony: space for readout/DAQ, shielding?
    Mockup

## Slide 4: Mockup
India Krehbiel