## Slide 1
1. Overall Hardware Design
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
ePIC
EIC
Common
Platform
Online computer
4
FEB
FEB
FEB
System Clock: 98.5 MHz (100MHz nominal)

## Slide 2
2. DAM FLX155 interface
Dedicated Clock input,
up to three MGT lanes (Tx/Rx)
MTP multimode 850um optical

## Slide 3
7
Beam synced Clock, orbit
EIC common platform
Online computer
GTU
3. GTU design: Inputs and Outputs
GBE
Run Control
CLOCK distribution
MTP
DAM
Clock, Control, status
MTP
DAM
Clock, Control, status
MTP
DAM
Clock, Control, status
~150
LC
TOF_RDO
Clock
LC
TOF_RDO
Clock
LC
TOF_RDO
Clock
~200
Risk mitigation for extremely stringent requirement by TOF
Beam monitor
RDO clock phase
MTP fibers, ~10 meters
LC fibers, ~100 meters
Clock @ 98.5 MHz
GTU_CONTROL
DAM/RDO Status
Optional/extra
MTP: 4 Tx/4 Rx

## Slide 4
7
3. GTU design: DAM connection
GTU
DAM
Clock @ 98.5 MHz
GTU_CONTROL, min. 8-bits (+ 1 k_bit) @ 98.5 MHz
DAM/RDO Status, min. 8-bits (+ 1 k_bit) @ 98.5 MHz
To fully use the DAM connection
Receivers
Transmitters
Receivers
Transmitters
Downlink
Uplink
Transceivers
Transceivers
Available on DAM:
  4 MGT (MultiGigabit Transceivers) (One Rx for Clock)
Design on GTU:
  Clock,
  1 Tx and 1 Rx using MGT;
  1 Tx and 1 Rx using FPGA’s regular IO

## Slide 5
7
3. GTU design: FPGA selection
Enough GigabitTransceivers (~150)
Enough General IOs, (~600)
FPGA lifetime
 | Versal Primium |  |  | AI Edge | Versal Prime |  | Versal HBM |  | UltraScale (plus) | 
FPGA | VP1552 | VP1502 VP2502 | VP1802 VP2802 | VE2802 | VM1802 | VM2302 VM2902 | VH1522, 42, 82 | VH1742 VH1782 | VU9P | VU190
GTY/XH | 68 | 28 | 28 | 32 | 44 | 8 | 68 | 68 | 120 | 60+60
GTM | 20 | 60 | 140 | 0 | 0 | 36 | 20 | 60 | 0 | 
Gen_IO | 570 | 570 | 570 | 300 | 506 | 192 | 570 | 570 | 832 | 702
Eval kits | FLX155 |  | VPK180 $18K | VEK280 $7K | VMK180 $9,345 |  | VHK158 $15K |  | VCU118 $9K | VCU110 $21K
The GTM can be used similarly as GTY, but the RxFIFO, and TxFIFO can NOT be bypassed  Delay uncertainly;
GTM internal data width 64/80, minimum 9.5 Gbps  better for faster data throughput (trick: doulble counting, “01011…” @5Gbps is the same as “0011001111……” @10Gbps, or “000111000111111………” @15 Gbps) ;

## Slide 6
7
3. GTU design: FPGA selection: PROs and CONs of three preferred FPGA candidate
FPGA | PRO | CON
Versal VP1802 VSVA5601, 570 XPIO, 28 GTY, 140 GTM | Dual core Arm® Cortex-A72; 1:1 GT with DAM | 1:2 Tx to DAM, 1:1 Rx from DAM on XPIO; GTM, harder to control
Versal VH1582 VSVA3697, 570XPIO, 68 GTY, 20 GTM | Dual core Arm® Cortex-A72; Large on-die memory | 1:2 Tx to DAM, 1:1 Rx from DAM on XPIO; 1:3 with DAM on MGT
UltraScale+ VU9P B2104, 702 HPIO, 76 GTY | 1:1 HPIO with DAM Compatible with VU5P, VU7P | No Arm® CPU; 1:2 GTY Older FPGA,
Prefer: AMD Versal Primium VP1802 ACAP
Two (or three) smaller FPGAs are easier for the PCB design (less risk).

## Slide 7
3. GTU design: functional diagram
EIC
COMMON PLATFORM
EIC/ePIC clock & beam orbit info
jitter cleaner & phase adjustment
FPGA
Beam vs clock phase monitoring
Clock phase adjustment
1:400
fanout
XPIO_1
MGT_1
XPIO_2
MGT_2
XPIO_150
MGT_150
Optic transceivers
DAM_150
DAM_1
DAM_2
Optic transmitter
TOF_RDO_1
TOF_RDO_1
TOF_RDO_200
Run Control computer
Run Control
Synchronous
User interface
DAM/RDO status configure
GTU
~200
~150

## Slide 8
3. GTU design: If the optical transceivers are on the GTU PCB
12* 12-port transmitter for Clock
12* 12-port transmitter for XPIO
12* 12-port receiver for XPIO
12* 12-port transmitter for MGT
12* 12-port receiver for MGT
144* MTP to DAM
12-port transmitter for Clock
12-port transmitter for XPIO
12-port receiver for XPIO
12-port transmitter for MGT
12-port receiver for MGT
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
MTP to DAM
12*

## Slide 9
3. GTU design: modular design
GTU base board
Optic transceiver plugin modules (to DAM)
FPGA
Power
supplies
Clock
Receiver, control, distribution
Run Control
Memory
‘services’
GTU base board
Optic Transceiver plugin module
Clock fanout
Possible TX fanout
Quad optic TRX
Power
regulators
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Fits in a 19U wide rack
Takes 4U high space
MTP fiber ports to DAM
19 U wide
4 U high
All the electrical signals are differential signals (PCB and connector)
The FPGA can be a single piece, or two pieces with fast interconnect.

## Slide 10
Clock phase monitoring:
Beam pickup, and digital feedback to GTU
Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)
Optic Transceiver plugin module
Clock fanout
Optic transmiter
Power
regulators
4 U high
Optic transmiter
Optic transmiter
Optic transmiter
Optic transmiter
Optic transmiter
Optic Transmitter plugin modules
Clock only, to TOF_RDO (optional)
3. GTU design: risk mitigation