## Slide 1: “Injectors” RHIC Retreat 2024
11/15/2024
V. Schoefer

## Slide 2: Talk that is
Talks that are not
Polarized protons
  Polarization performance
  Skew quad resonance correction commissioning
  Split/merge user commissioning
Comments about operation in the injectors
No dedicated talks for
  Separated discussion of proton/heavy ion performance
  OPPIS status/performance
  Skew quads (a major new system)
  Substantial reliability “challenges”

## Slide 3: Startup Timeline
Nominal plan was for 6 weeks AGS startup time prior to RHIC cooldown (normally 3 weeks for p^)
  Extra time planned to allow for additional skew quad commissioning time
  Difficulties with OPPIS and cold snake delays polarized operation (and ops with nominal p^ optics) by 3-4 weeks
March: unpolarized beam commissioning.
  Split/merge and dual pulse Linac user development
  Skew quad installation, power supply hookup and beam-based polarity checks
April: 2 weeks polarized proton setup in AGS (in actuality less than normally planned)
Cumulative time with beam at AGS extraction for each user
P^ ops (tune jump)
P^ ops (skew quad)
End p-p
P^ ops (skew quad)
P^ dev (skew quads)
Au
“Beam days” = (# of supercycles with beam in AGS) * (supercycle length in days)

## Slide 4: Beam time breakdown
(user number) in parenthesis

## Slide 5: Run 24 Polarization Performance
EIC target region
Dashed line is previously established good operation
Mean polarization performance Run 24: 95% of established optimum, with a sigma of +/-7%

## Slide 6: Source performance/stability
Intensity
Polarization
Source intensity comparable to Run 22.
Periodic ~1 wk variation due to Rb fills in Run 24, not in Run 22
Polarization both lower in average (~5% rel) and larger in variation in Run 24, relative to 22
 | Run 22 | Run 24
Pol (mean) | 82.4 | 78.7
Pol (σ) | 2.3 | 2.8

## Slide 7: AGS Polarization efficiency AGS Extraction/Source
AGS Polarization/Pol(200 MeV) by Fill
Polarization transmission through AGS slightly better than Run 22 over most intensities
Skew quad fills not obviously different from tune jump at the highest intensities

## Slide 8: Energy stability
Arrival time at GƔ = 45
Change in GƔ during acceleration, fill by fill
Slow drift of the energy as a function of time during the ramp
  For tune jump 100 us is significant, 200 us is bad
  Tolerance is better with skew quads, but would still prefer stability
  Injection matching
Change during a fill is small (drift is ~hours)
Deviation is often linearly increasing during ramp
ML project to improve calibration precision, make online continuous calibration and quantify uncertainty
Conventional analysis of the MM field contribution to this drift
  We have a slow software feedback for RHIC energy matching
  Consider developing a system for the whole cycle

## Slide 9: Skew quad commissioning
Spin tune gap
Hor resonance crossings
Tune
jump
(pause tune jump near transition)
15 skew quads in AGS
Designed to replace and improve upon the tune jump for correction of horizontal depolarizing resonances
Nov 2023: Magnets #13,14 installed. Final magnet held at power supply vendor for testing
Nov-Apr 8th: Power supplies delivered and connected in phases
  Significant ”after market” modifications to each one, mostly to improve p.s. heating
Mar 5th : First 6 magnets powered, ready for testing
Mar-Apr: Beam based polarity checks (zero polarity errors), orbit correction
May 4th: Proof of principle test!
May-Jun: beam-based tests, interleaved with a lot of RHIC setup
July 29th: First demonstration of ramp effect
Sep 9th: RHIC operations with skew quad user
~About 20 shifts of commissioning time over many calendar weeks

## Slide 10: Skew quad commissioning
Spin tune gap
Hor resonance crossings
Tune
jump
(pause tune jump near transition)
15 skew quads in AGS
Designed to replace and improve upon the tune jump for correction of horizontal depolarizing resonances
Nov 2023: Magnets #13,14 installed. Final magnet held at power supply vendor for testing
Nov-Apr 8th: Power supplies delivered and connected in phases
  Significant ”after market” modifications to each one, mostly to improve p.s. heating
Mar 5th : First 6 magnets powered, ready for testing
Mar-Apr: Beam based polarity checks, orbit correction
May 4th: Proof of principle test!
May-Jun: beam-based tests, interleaved with a lot of RHIC setup
July 29th: First demonstration of ramp effect
Sep 9th: RHIC operations with skew quad user
Many thanks to Ioannis, Ed, Chirag and others
Fast development and implementation of changes to the p.s. switching.
ZERO problems operating even in August.

## Slide 11: Commissioning: Proof of principle single resonance crossing
At nominal acceleration rate (dGɣ/dθ =4.7 x 10-5), max polarization loss from a single resonance is 0.1-0.5%
  too small to to measure individually
Configure a crossing at fixed energy: just above nominal extraction, with ramped horizontal tune and very slow ramp rate (>100x longer)
11
Parameter | Value
Gɣ | 45.74
dp/p (full base) | 1x10-3
Chrom ξx | 4
ΔQx | 0.08
Tune ramp length [ms] | 200
Crossing rate (⍺) | 1.7 x 10-7
Resonance crossing
Slow crossing gives measurable 20-25% relative polarization loss

## Slide 12: Commissioning: Proof of principle single resonance crossing
Select three skew quads with good relative phasing
K07 in phase with snakes
E05 180o from K07
B07 orthogonal to snake drives
Skew quad arrow length is full current range of supply (arrow head is positive)
B07
K07
E05
Snake drive
Resonance ‘portrait’ at Gɣ = 45.74
Polarization response to skew strength
Phasing of skew quads is as expected
Demonstration of total correction
In anti-correcting phase, expect more loss from simple Froissart-Stora estimate
  May be multiple crossings from synchtron motion during long crossing
  To be investigated in simulation

## Slide 13: Skew quad during acceleration: Orbit effects
Large horizontal orbit excursions in AGS
High vertical tune (8.985 – 8.991)
Horizontal off-centering in skew quads leads to large vertical orbit changes and beam loss.
Beam-based orbit offsets measured and corrected
  Skew quads pulsed, infer offset from vertical orbit change + model
  Correction limited by weak steering dipoles
13
Sample horizontal orbits (at BPMs)
Horizontal position at skew quads, inferred from orbit differences
Before correction
After correction
Low energy
High energy

## Slide 14: Skew quad during acceleration: Orbit effects
Large horizontal orbit excursions in AGS
High vertical tune (8.985 – 8.991)
Horizontal off-centering in skew quads leads to large vertical orbit changes and beam loss.
Beam-based orbit offsets measured and corrected
  Skew quads pulsed, infer offset from vertical orbit change + model
  Correction limited by weak steering dipoles
14
Sample horizontal orbits (at BPMs)
Horizontal position at skew quads, inferred from orbit differences
Before correction
After correction
Low energy
High energy
First generalized orbit correction in AGS
Thanks to Jon Laster and Leve Hajdu for Controls support!

## Slide 15: Orbit corrector currents
Centering in skew quads requires maxing out some orbit correctors and nearly maxing others
Global correction would require more than factor of 2 higher currents
High currents make each corrector less reliable, more likely to be single point failure.
Motivates:
Survey realignment
Investigating possibility of upgrades:
  Stronger correctors
  Additional correctors (possibly 50% more if adding on at each remaining PUE location is possible)
  Model/controls work toward global orbit correction
AGS Hor Orbit Corrector Currents

## Slide 16: Skew quadrupole commissioning: ramp and polarization
Enabling more pulses via
  Incremental orbit improvements
  Fixing bug in resonance calculation for low energy resonances when Qy not in spin tune gap
  Included model-predicted orbit response of the skew quads in the optimization to minimize resulting vertical rms
    Resonance strength, |ε| = 0
    Tune shift from coupling, ΔQy< 0.005
    Vertical |Morm*(kskew*xskew)|max < 1 mm
Skew quad currents
16
Skew quads ON
Skew quads OFF
Polarization ratio
Skew Quads ON/OFF
Polarization comparison
Mysterious decline in base polarization

## Slide 17: Correction scaling measurements
Overall scaling of the correction currents from zero to full correction
Agreement with the model is better if only the higher energy (after transition) resonances are corrected
Implies errors in resonance calculation at low energy are still significant
Near 0+ easier to do more harm than good
Correcting only resonance
above transition
Correcting only resonance
above and below transition

## Slide 18: Skew quad status
Commissioning tasks all successful
Successful demonstration of principle and practical implementation on ramp
Polarization gain over base is 12-15%.
  To be compared to 8-10% from the tune jump
Operation is robust enough to replace the tune jump as the default system
Where is the rest of the polarization from the skew quads (goal gain factor is 15-20% over base)
  1% in the transition ‘gap’
  Beta beat likely a small contribution
  Next likely culprit is residual coupling
    Survey, realignment of AGS magnets planned for next two shutdowns (no alignment before Run 25)
    Main magnet roll and vertical sextupole offsets of principal concern
Resonance calculations with 2010 main magnet rolls
Small impact at high energy
Working on the low energy model

## Slide 19: Split/merge setup
Aimed at reducing space charge at AGS injection
Chart: 95% Normalized Emittance vs. Intensity for AU4
Chart: 95% Normalized Emittance vs. Intensity for AU3 (Split-Merge)
Vertical 2 | 15.3 | 20.2533 | 16.92 | 14.5933 | 11.8767 | 14.9067 | 12.9433 | 17.48 | 12.8733 | 14.8133
Value @ 3x1011 | Single bunch | Split/ merge
Pol (%) | 66.4 | 67.3
Emit hor | 3.1 | 2.6
Emit vert | 3.2 | 2.7
(emit is rms, norm, urad)
Slope dP/dI is less
Emittance is 15% smaller
Polarization is only slightly changed (?!)
Seem associated with the P(0) offset: normally associated with Booster or source
  Not so sure this interpretation holds up
Long emit is ~1.2 eVs (+20% from nominal)
Nominal user (single bunch)
Split/merge

## Slide 20: LtB Injection Optimization with ML (Lucy Lin)
Demo on intentionally detuned LtB
Bayesian Optimization algorithm automatically maximizes Booster beam intensity using LtB optics
Higher intensity after fixed scrapers smaller beam size higher luminosity
Beam size decrease observed in both planes in the BtA line corresponds to intensity increase
Similar algorithm under development for AGS injection
Minimal model inputs
Likely to help better maintain previously achieved optimum
Intensity Booster extraction
Beam sigma (BtA)
Not an explicit objective, consequence of improving scrape efficiency

## Slide 21: Injector physics and operations
The number of people who can work independently with beam in the injectors is small
Run 11/12: Commissioning of the tune jump (last major commissioning effort)
  Leif (Gg-meter), Woody (power supplies), Yann (physics/simulation), Haixin (polarimeter analysis/data)
  Nick T, Kip, Mei, Steve T, Francois, Thomas Roser, Vahid, Vincent, Keith Z
  13 people (11 shifters, Keith and Thomas)
Run 24:
  Vincent (skew quad commissioning)
  Keith (entire split/merge and dual pulse configurations, little/no physics involvement)
  Kiel (Run coordinator), Haixin (polarimeter scans/data)
  4 people
Limited expertise has consequences:
  Beam time in injectors is ‘opportunistic’, with a broad field someone can use it when it arrives (not true if half the injector group is the run coordinator)
  Limited attention: Every small “fire” stalls the main efforts
  Have not raised levels of automation/robustness commensurately with decrease in personnel (many systems that ran on continuous attention and good will now don’t) (e.g. I did not commission the two new AtR cameras) “The inheritance problem”
  The Run 24 operation+development effort really strained our abilities to keep up
    Is the current level of support really sufficient to commission an entirely new polarized species? (3He, ~5-6 beam months of 24/7 work identified).

## Slide 22: Reliabilities and Capabilities
OPPIS
  Periods with unpolarized beam tolerable this year because so sPHENIX priorities
  Need to re-establish lines of communication
    Used to have agreements with ops about Intensity/Rb temp control to smooth out intensity
AGS Cold snake
  Similar: periods with unpolarized beam not counted as ‘failure’ because of unique operating concerns
  Example of Injector group comfortably accepting reduced capability
    Ramp down now significantly longer: impacts p-Au operation and development efforts (we fill Au first at least….)
AGS Extraction bumps
  Workaround for one failed supply
  These supplies specifically identified several years ago by operations as a weak point for diagnosis of problems
AGS Tune Meter
  1 week failure
  On the short list for RHIC->EIC “Middle Ages” overhaul
  Example of getting a capability back after >10 years (independent plane control of kick strength)
Multiple multi-hour repair accesses one weekends
  Not counted as failure, so largely unnoticed
  Not indicative of general reliability

## Slide 23: Bottom lines and outlook
Injectors delivered physics for RHIC operation together with two commissioning efforts
Skew quadrupole resonance correction
  mature enough to replace the tune jump in future operation
  Better gain factor relative to tune jump
  Improvements
    understanding residual coupling in AGS important
    Model of realistic AGS (with errors) , especially low energy
    Correcting near transition energy
    Survey and alignment of AGS (not for Run 25)
Split/merge
  Demonstrated -15% transverse emittances at 3x1011
  Small improvement in polarization (might be offset from other sources)
  We still don’t understand the emittance evolution in the injectors
    Space charge/emittance evolution needs a fairly sustained campaign of physics simulations/measurements
    Including everything one would do for a new machine: magnet errors, impedance models etc.
Future operation could start day 1 with a split/merge + skew quad correction setup
Gold is fine. See EBIS talk.

## Slide 24: Skew Quad Special Thanks!
Engineering,Design and Installation Team
George Mahler, Ioannis Marneris, Nicholaos Tsoupas, Richard Lynch, Viorel Badea, Dan Lehn, Jimmy Meier
Equipment all worked 100% as expected!
“Making it Happen” Award
Leve Hajdu and Chirag Birla
for excellence in operational support with rapid and continuous on-the-fly solutions!