## Slide 1
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; iFAST, grant agreement 101004730, FCCIS, grant agreement 951754; E-JADE, contract no. 645479; EAJADE, contract number 101086276; and by the Swiss CHART program
http://cern.ch/fcc
Michael Benedikt, Frank Zimmermann, CERN
on behalf of FCC collaboration & FCCIS DS team
The FCC Integrated Program
Strategic Joint Meeting of the HFCC, New York, 8 November 2024

## Slide 2
FCC integrated program
FCC-ee
FCC-hh
comprehensive long-term program maximizing physics opportunities
stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities
stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, pp & AA collisions; e-h option
highly synergetic and complementary programme boosting the physics reach of both colliders
common civil engineering and technical infrastructures, building on and reusing CERN’s existing infrastructure
FCC integrated project allows the start of a new, major facility at CERN within a few years of the end of HL-LHC
2020 - 2045
2045 - 2065
2070 -

## Slide 3
FCC integrated program - timeline
Note: FCC Conceptual Design Study
started in 2014 leading to CDR
in 2018
Ambitious schedule taking into account:
past experience in building colliders at CERN
approval timeline: ESPP, Council decision
that HL-LHC will run until 2041
project preparatory phase with adequate
resources immediately after Feasibility Study
~2033
~2070
~2046
2027/28

## Slide 4
European Strategy for Particle Physics
2013 Update of European Strategy for Particle Physics:
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines.”
→ FCC Conceptual Design Reports (2018/19)
2020 Update of European Strategy for Particle Physics:
“Europe, together with its international partners, should investigate technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage.”
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  CDRs published in European Physical Journal C (Vol 1) and ST (Vol 2 – 4)
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 , EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382

## Slide 5
FCC FS Council Documents, June ‘21
Organisational Structure of the FCC Feasibility Study
http://cds.cern.ch/record/2774006/files/English.pdf
Main Deliverables and Timeline of the FCC Feasibility Study
http://cds.cern.ch/record/2774007/files/English.pdf

## Slide 6
demonstration of the geological, technical, environmental and administrative feasibility of the tunnel and surface areas and optimisation of placement and layout of the ring and related infrastructure;
pursuit, together with the Host States, of the preparatory administrative processes required for a potential project approval to identify and remove any showstopper;
optimisation of the design of the colliders and their injector chains, supported by R&D to develop the needed key technologies;
consolidation of the physics case and detector concepts for both colliders
elaboration of a sustainable operational model for the colliders and experiments in terms of human and financial resource needs, as well as environmental aspects and energy efficiency;
development of a consolidated cost estimate, as well as the funding and organisational models needed to enable the project’s technical design completion, implementation and operation;
identification of substantial resources from outside CERN’s budget for the implementation of the first stage of a possible future project (tunnel and FCC-ee);
Results will be summarised in a Feasibility Study Report to be released in March 2025
FCC Feasibility Study (2021-2025): high-level objectives
F. Gianotti

## Slide 7
FCC FS mid-term review
the scientific and technical results be reviewed by the FCC FS Scientific Advisory Committee, augmented by additional experts as needed;
the cost and financial feasibility, which will focus on the first-stage project (tunnel, technical infrastructure, FCC-ee machine and injectors), be reviewed by a committee including external experts, as proposed in CERN/3588;
Mid-term review setup and deliverables are defined in CERN/SPC/1183/Rev.2:
FCC Scientific Advisory Committee
Riccardo Bartolini (DESY), Alain Chabert (Société Française du Tunnel Routier Fréjus),
Heinz Ehrbar (HEP), Brigitte Fargevieille (Électricité de France), Belen Gavela Legazpi (UAM), Gudrun Hiller (Dortmund), Srinivas Krishnagopal (BARC), Peter Krizan (Ljubljana), Philippe Lebrun (CERN, retired), Peter McIntosh (STFC), Michiko Minty (BNL),
Andrew Parker (Chair, Cambridge), Kyo Shibata (KEK), Roberto Tenchini (Pisa)
FCC Cost Review Panel
Carlos Alejaldre (Fusion for Energy), Austin Ball (CERN, retired), Umberto Dosselli (INFN), Heinz Ehrbar (HEP)
Vincent Gorgues (CEA), Norbert Holtkamp (Chair, Stanford), Christa Laurila (National Audit Office, Finland), Ursula Weyrich (German Cancer Research Centre), Jim Yeck (BNL), Thomas Zurbuchen (ETH Zürich)

## Slide 8
Feasibility Study Mid-Term Review passed !
The goal of the FCC FS mid-term review is to assess the progress of the Study towards the final report.
Deliverables approved by the Council in September 2022:
https://indico.cern.ch/event/1197445/contributions/5034859/attachments/2510649/4315140/spc-e-1183-Rev2-c-e-3654-Rev2_FCC_Mid_Term_Review.pdf
Documents:
Mid-term report (all deliverables except D7)
Executive Summary of mid-term report
Updated cost assessment (D7)
Funding model (D7)
Review process:
Oct 2023: Scientific Advisory Committee (scientific and technical aspects)
and Cost Review Panel (ad hoc committee; cost and financial aspects)
Nov 2023: SPC and FC
2 Feb 2024: Council
Many thanks to the SAC, CRP, SPC, FC and the Council for the very useful reviews!
Deliverables:
D1 : Definition of the baseline scenario
D2 : Civil engineering
D3 : Processes and implementation studies with the Host States
D4 : Technical infrastructure
D5 : FCC-ee accelerator
D6: FCC-hh accelerator
D7: Project cost and financial feasibility
D8: Physics, experiments and detectors
Full Report
8 Chapters/Deliverables
~ 700pp document
~ 16 editors
~ 500 contributors
→70-80 recommendations
All deliverables met, no technical showstoppers

## Slide 9
Structure:Three Volumes
Vol. 1: Physics, Experiments and Detectors (~200 pages)
Vol. 2: Accelerators, Technical Infrastructures, Safety Concepts (~400 pages)
Vol. 3: Civil Engineering, Implementation & Sustainability (~200 pages)
- Executive Summary of the FCC Feasibility Study: ~40 pages
In addition: a. Documentation on Cost Estimate – Funding Models
b. Environmental Report
Feasibility Study Report for March 2025
to be prepared with Overleaf & published by EPJ (Springer-Nature) – FCCIS members
Input for Update of European Strategy for Particle Physics

## Slide 10
10
PA: Experiment
PB: technical
PD: experiment
PF: technical
PG: experiment
PH: technical
PJ: experiment
PL: technical
Layout chosen out of ~ 100 initial variants, based on geology and
surface constraints (land availability, access to roads, etc.), environment, (protected zones), infrastructure (water, electricity, transport), machine performance etc.
“Avoid-reduce-compensate” principle of EU and French regulations
Overall lowest-risk baseline: 90.7 km ring, 8 surface points,
4-fold symmetry
Number of surface sites | 8
Surface requirements | ~40 ha
LSS@IP (PA, PD, PG, PJ) | 1400 m
LSS@TECH (PB, PF, PH, PL) | 2032 m
Arc length | 9.6 km
Sum of arc lengths | 76.9 m
Total length | 90.7 km
V. Mertens,
J. Gutleber
Reference layout and implementation: PA31 - 90.7 km
4 experiments

## Slide 11
Integration with regional infrastructures
Road accesses developed for all 8 surface sites
Four possible highway connections defined
Less than 4 km of new roads required
Electrical connection concept developed with RTE (French electricity grid operator)
Three HV supply points, two new stations & CERN Prevessin
 requested loads have no significant impact on grid
R&D efforts aiming at reduction of the energy consumption of FCC-ee and FCC-hh
Connections to
French electricity grid
connections with
highway network

## Slide 12
Regional implementation activities
Meetings with municipalities concerned
in France (31) and Switzerland (10)
PA – Ferney Voltaire (FR) – experiment site
PB – Présinge/Choulex (CH) – technical site
PD – Nangy (FR) – experiment site
PF – Roche sur Foron/Etaux (FR) – technical site
PG – Charvonnex/Groisy (FR) – experiment site
PH – Cercier (FR) – technical site
PJ – Vulbens/Dingy en Vuache (FR) experiment site
PL – Challex (FR) – technical site
Detailed work with municipalities and host states
identify land plots for surface sites
understand specific aspects for design
identify opportunities (waste heat, tec.)
reserve land plots until project decision
The support of the host states is greatly appreciated and essential for the study progress!
Status 1 June 2024

## Slide 13
FCC tunnel implementation- geological conditions
FCC passes below Lake Geneva moraines
FCC above limestone
FCC inclined at 0.5% gradient to minimise depth of point F
Limestone unavoidable between G-H
  Tunneling mainly in moraine layer (soft rock), well suited for fast, low-risk TBM construction.
  6 million m3 excavated volume  8.5 million m3 excavation material on surface
  CE Designs of all underground structures developed
  To fix the vertical position of the tunnel, interfaces between geological layers have to be known

## Slide 14
First series of site investigations
Site investigations to identify exact location of geological interfaces:
Molasse layer vs moraines/limestone
~30 drillings and ~90 km seismic lines
 Vertical position and inclination of tunnel
example of drilling works on a lake the lake

## Slide 15
Start of site investigations – seismic investigations
Seismic line SL_USSES_02 :
Acquisition date : 01/10/2024
Length : 480 meters
Method(s) : Explosive and Seismic gun
Geophones : 96 units (5 meters of spacing)
Shot points : 13 shot points in total
Seismic line SL_USSES_01 :
Acquisition date : 02/10/2024
Length : 300 meters
Method(s) : Weight drop
Geophones : 60 units (5 meters of spacing)
Shot points : 15 shot points in total
First seismic line :
Second seismic line :

## Slide 16
Status of site investigations – drilings
  Drilling for first borehole has commenced on 14/10/2024
  The drilling (USSES 2) is within the commune of Marlioz
  The drill site is located within the storage yard of a private construction company (Besson).
  Drilling Depth = 70m
  Fully cored recovery
  Drill time should be about 2 weeks
  Equipped with Piezometer

## Slide 17
CE underground and surface progress
Full 3D model of all underground structures as basis for costing and scheduling exercises with external consultant.
Experiment Site (PA)
Generic study of experiment site and technical site done by FNAL
bills of quantities extracted from FNAL designs
basis for cost estimate by consultant with experience on industrial constructions in CH-FR area.

## Slide 18
Studies on excavation strategy and material quantities
2 TBMs from each experimental point Alternative with no TBMs from PA

## Slide 19
Development of excavation material re-use opportunities
OpenSkyLab: academic and industrial collaboration @LHC P5 CMS
Transformation of Molasse (FCC ~8 Mm3 volume) into fertile soil for agricultural and other uses
Materials: Molasse from the HL-LHC construction
Duration: 4+ years (2024 - )
Trials with 5 000 t molasse
  Soil fertilisation process (micro-organisms, mixing with fertile soil, etc.)
  Development of ferilisation mix products
  Development of quality managed processes
  Experimental phase with scientific protocol and field monitoring and control system support

## Slide 20
OpenSkyLab status and progress

## Slide 21
Environmental studies to document
present status of potential FCC surface site areas
Short term goals for FCC Feasibility Study:
Establish a state of the current environmental conditions at the surface site locations based on the actual situation, complementing the map and database investigations.
Confirm the territorial feasibility in principle.
Support the environmental impact studies for the geotechnical and geophysical investigations (i.e. boreholes and seismic lines).
Long term goals anticipating impact assessment works:
Comply with the regulatory reporting requirements in the frame of the authorisation process.
Identify and document the environmental stakes exhaustively.
Definition of environmental strategy and guiding principles for Ecodesign to be considered by infrastructure and equipment designers in technical design phase.

## Slide 22
Environmental studies around surface areas
PA
PB
PD
PF
PG
PH
PJ
PL
Total area investigated in 2023/24: 585 ha over 4 seasons

## Slide 23
On 15 May, RTS (Radio Télévision Suisse) broadcasted a special program celebrating CERN’s 70th anniversary and hosted at CERN’s Science Gateway.
The event featured a comprehensive look at CERN's illustrious history, groundbreaking achievements, and future ambitions, including the prominently featured Future Circular Collider (FCC) project with study experts interacting with the audience.
La Roche-sur-Foron - Haute Savoie international fare April 27 to May 6
CERN’s participation in the International Fair of Haute-Savoie/Mont Blanc, enhanced by the valuable help of volunteers from the FCC team, resulted in meaningful discussions with more than 2000 members of the local community on topics ranging from the required technological advancements to sustainability measures.
Start of public information & engagement sessions
First public information and discussion meeting at the Science Gateway on the 24th April at CERN.
The meeting was organised for the local community of our Host States, France and Switzerland, in the Science Gateway. The "Progress of the feasibility study of the Future FCC circular collider" was followed by a discussion with the participants.

## Slide 24
Commission Nationale de Debat Public (CNDP)
mission and public information meetings
The CNDP, created in 1995, is an independent French authority that ensures public participation in the definition and decision process of major projects in France, impacting the environment by providing a neutral and transparent framework for discussions between decision-makers and citizens.
On July 2, 2024, the CERN DG requested the CNDP to undertake an advisory mission on public participation for the FCC. On July 3, the president of the CNDP appointed two guarantors to:
Assist CERN in preparing the first information meetings on the ongoing studies in the region.
Provide non-binding advice to CERN on the next steps for public participation regarding the FCC.
CNDP decision for the Advisory Mission

## Slide 25
FCC-ee basic design choices
K. Oide,
J. Gutleber
et al.
Double ring e+ e- collider
Common footprint with FCC-hh,
Asymmetric IR layout and optics to limit synchrotron radiation towards the detector
Perfect 4-fold superperiodicity allowing 2 or 4 IPs; large horizontal crossing angle 30 mrad, crab-waist collision optics
Synchrotron radiation power 50 MW/beam at all beam energies.
Top-up injection scheme for high luminosity Requires booster synchrotron in collider tunnel

## Slide 26
FCC-ee main machine parameters
F. Gianotti
3 years
> 2 x 106 H
5 years
2 x 106 tt pairs
2 years
> 108 WW
LEP x 104
4 years
5 x 1012 Z
LEP x 105
x 100 improvements on all EW observables
up to x 10 improvement on Higgs coupling (model-indep.) measurements over HL-LHC
x10 Belle II statistics for b, c, τ
indirect discovery potential up to ~ 100 TeV
direct discovery potential for feebly-interacting particles over 5-100 GeV mass range
Up to 4 interaction points  robustness,
statistics, possibility of specialised detectors
to maximise physics output
Design and parameters to maximise luminosity at all working points:
allow for 50 MW synchrotron radiation per beam.
Independent vacuum systems for electrons and positrons
full energy booster ring with top-up injection, collider permanent in collision mode
Parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1283 | 135 | 26.8 | 5.0
number bunches/beam | 11200 | 1852 | 300 | 64
bunch intensity [1011] | 2.16 | 1.38 | 1.69 | 1.48
SR energy loss / turn [GeV] | 0.0390 | 0.369 | 1.86 | 9.94
total RF voltage 400/800 MHz [GV] | 0.079/0 | 1.0/0 | 2.09/0 | 2.1/9.2
long. damping time [turns] | 1171 | 218 | 65.4 | 19.4
horizontal beta* [m] | 0.11 | 0.22 | 0.24 | 0.9
vertical beta* [mm] | 0.7 | 1.0 | 1.0 | 1.4
horizontal geometric emittance [nm] | 0.7 | 2.16 | 0.66 | 1.51
vertical geom. emittance [pm] | 1.9 | 2.0 | 1.0 | 1.36
vertical rms IP spot size [nm] | 36 | 47 | 40 | 51
beam-beam parameter xx / xy | 0.0022/0.0977 | 0.013/0.129 | 0.0108/0.130 | 0.065/0.136
rms bunch length with SR / BS [mm] | 5.57 / 15.6 | 3.46 / 5.28 | 3.26 / 5.59 | 1.91 / 2.32
luminosity per IP [1034 cm-2s-1] | 143 | 20 | 7.5 | 1.38
total integrated luminosity / IP / year [ab-1/yr] | 17 | 2.4 | 0.9 | 0.17
beam lifetime rad Bhabha + BS [min] | 15 | 12 | 12 | 11

## Slide 27
FCC-ee optics baseline & further evolution(s)
regular arc
interaction region
FODO lattice, many -I sext pairs; periodic unit cell length 260 m
hybrid FODO lattice,
with few sext. families,
periodic unit cell length300 m
5 sext.s per final focus, modular
“1.5” sext.s per final focus,
asymmetric
K. Oide
K. Oide
P. Raimondi
P. Raimondi
C. Garcia,
R. Tomas, et al.
optimisation goals:
reduced power consumption
lower SR energy loss
increased momentum acceptance
relaxed tolerances
larger dynamic aperture
simplified powering schemes

## Slide 28
Optimisation for operation: 400 MHz SRF and beam switchyard
Beam switching between (Z, W) and ZH operation
2-cell 400 MHz cavities for all three working points, identical configuration
ES separators + magnetic field for switching beams
Allows quasi “instantaneous” switching between Z, W, ZH
33 CM
Beam 1
Beam 2
33 CM
33 CM
33 CM
400 MHz
400 MHz
400 MHz
400 MHz
ZH
Z, W
E&M
sep.1
E&M
sep. 2a
E& M
sep. 2b
Collider RF integration at point H
(Z, WW and ZH operation)
extra year of operation thanks to single RF system
Beam crossing and combination
at RF section in point H
 | Energy (GeV) | Current (mA) | RF voltage (GV)
Z | 45.6 | 1280 | 0.08
W | 80 | 135 | 1
H | 120 | 26.7 | 2.08
ttb | 182.5 | 5 | 11.67

## Slide 29
RF R&D activities
RF system R&D is key for increasing energy efficiency of FCC-ee
Nb on Cu 400 MHz cavities (KEK as R&D partner), seamless cavity production, coating techniques
Bulk Nb 800 MHz cavities and cryomodule, surface treatment techniques (JLAB, FNAL as R&D partners)
RF power source R&D in synergy with HL-LHC.
400 MHz
monoblock prototype
high-efficiency klystron R&D
5-cell 800 MHz cavity development collaboration with JLAB

## Slide 30
Optimized injector concept and parameters
Mid-term review recommendations to reduce gradients and repetition rate  new linac optimization in terms of cost and power density
  Overall power consumption (for linacs) is reduced by more than a factor 3 by means of:
    new accelerating structures with higher shunt impedance;
    lower gradient (29.5 MV/m  22.5/20.5 MV/m);
    lower repetition rate (200/400 Hz  100 Hz).
  Repetition rate of 100 Hz with 4 bunches per rf pulse
  New layout: Damping Ring at higher energy 2.86 GeV, no common linac with 2x repetition rate.

## Slide 31
Optimised injector implementation at Prevessin site
CERN Fenced Area
Damping
Ring
High Energy LINAC
Good integration with existing CERN Prevessin Site and strongly reduced visibility from outside.
Ideal connection to existing experimental halls.
Good conditions for construction.
Entrance CERN Prevessin Site

## Slide 32
FCC-hh main machine parameters
F. Gianotti
Formidable challenges:
high-field superconducting magnets: 14 - 20 T
power load in arcs from synchrotron radiation: 4 MW  cryogenics, vacuum
stored beam energy: ~ 9 GJ  machine protection
pile-up in the detectors: ~1000 events/xing
optimization of energy consumption:  R&D on cryo, HTS, beam current, …
Formidable physics reach, including:
Direct discovery potential up to ~ 40 TeV
Measurement of Higgs self to ~ 5% and ttH to ~ 1%
High-precision and model-indep (with FCC-ee input)
measurements of rare Higgs decays (𝛄𝛄, Z𝛄, µµ)
Final word about WIMP dark matter
parameter | FCC-hh | HL-LHC | LHC
collision energy cms [TeV] | 81 - 115 | 14 | 
dipole field [T] | 14 - 20 | 8.33 | 
circumference [km] | 90.7 | 26.7 | 
arc length [km] | 76.9 | 22.5 | 
beam current [A] | 0.5 | 1.1 | 0.58
bunch intensity [1011] | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 
synchr. rad. power / ring [kW] | 1020 - 4250 | 7.3 | 3.6
SR power / length [W/m/ap.] | 13 - 54 | 0.33 | 0.17
long. emit. damping time [h] | 0.77 – 0.26 | 12.9 | 
peak luminosity [1034 cm-2s-1] | ~30 | 5 (lev.) | 1
events/bunch crossing | ~1000 | 132 | 27
stored energy/beam [GJ] | 6.1 - 8.9 | 0.7 | 0.36
Integrated luminosity/main IP [fb-1] | 20000 | 3000 | 300
With FCC-hh after FCC-ee: significant amount of time for high-field magnet R&D,
aiming at highest possible collision energies
Target field range for cryo-magnet R&D

## Slide 33
Key activities on FCC-hh: cryo magnet system, optics design
Optics design activities:
adaptation to new layout and geometry
shrink b collimation & extraction by ~30%
optics optimisation (filling factor etc.)
betatron collimation straight
experimental straight
Collider Center
F. Valchkova
M. Giovannozzi. G. Perez, T. Risselada
High-field cryo-magnet system design
Conceptual study of cryogenics concept and temperature layout for LTS and HTS based magnets, in view of electrical consumption.
Update of integration study for the ongoing HFM designs and scaling to preliminary HTS design.
   Confirmation of tunnel diameter!
HFM R&D (LTS and HTS) on technology and magnet design, aiming also at bridging the TRL gap between HTS and Nb3Sn.

## Slide 34
Possible time line till start of construction
2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 2028 |  |  |  | 2029 |  |  |  | 2030 |  |  |  | 2031 |  |  |  | 2032 |  |  |  | 2033 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FS Report
cost update
Pre-TDR Phase
TDR Phase
Feasibility Study
Project Decision
CE Concept Design update
Start construction
Detector EOI submissions
FC3 formation, call for CDRs
Detector CDRs submitted to FC3
ESPPU
2025/26
Construction 
Construction Design
TDR
cost update
CE Tender Design
engineering design 
Phase 1 Site Investigations
Environmental Impact study & Authorization Process
Phase 2 Site Investigations
accelerator design, technical infrastructure design, R&D, towards TDR
pre TDR
cost update

## Slide 35
Construction and installation planning stage 1
Baseline stage 1 FCC-ee schedule
Q1 2033, Start of CE construction work
Q2 2041, Completion of last lot of CE construction
Q2 2043, Overall completion of TI installation
Q4 2044, Accelerator installation completed
Q4 2045, HW commissioning completed
Q1 2046, First beams
Q1 2048, Start of nominal operation
Q3 2041 – Q3 2044, Experiment installation
Q1 2046, Start beam commissioning
Civil eng. works
Shaft works
TI installation
Experiment. install.
Geodetic install.
Machine install.
Accelerator HWC
TI HWC
Shaft release
First alcove release

## Slide 36
Status of FCC global collaboration
141 Institutes
32 countries
+
CERN
Increasing international collaboration as a prerequisite for success: links with science, research & development and high-tech industry will be essential to further advance and prepare the implementation of FCC
FCC Feasibility Study:
Aim is to increase further the collaboration,
on all aspects, in particular on
Accelerator and Particle/Experiments/Detectors

## Slide 37
FCC Week 2024 - San Francisco – 10 to 14 June
449 participants, 50 public sessions, 216 oral presentations, 32 posters
US efforts getting organized, towards completing the FS by March 2025

## Slide 38
Progress on international collaboration
26 April 2024
White House Office of Science and Technology Policy Principal Deputy U.S. Chief Technology Officer Deirdre Mulligan signed for the United States while Director-General Fabiola Gianotti signed for CERN.

## Slide 39
EU Competitiveness Report
“One of CERN’s most promising current projects, with significant scientific potential, is the construction of the Future Circular Collider (FCC): a 90-km ring designed initially for an electron collider and later for a hadron collider..
Refinancing CERN and ensuring its continued global leadership in frontier research should be regarded as a top EU priority, given the objective of maintaining European prominence in this critical area of fundamental research, which is expected to generate significant business spillovers in the coming years.”
https://commission.europa.eu/topics/strengthening-european-competitiveness/eu-competitiveness-looking-ahead_en
edited by Mario Draghi, and officially handed over to Ursula von der Leyen in September 2024

## Slide 40
Supporting statements at CERN’s 70 anniversary
“….No European country alone could have built the world’s largest particle collider. CERN has become a global hub because it rallied Europe and this is even more crucial today.
I am proud that we have financed the feasibility study for CERN’s Future Circular Collider (FCC). This could preserve Europe's scientific edge and could push the boundaries of human knowledge even further. And as the global science race is on, I want Europe to switch gears. To do so, European unity is our greatest asset. ….”
Ursula von der Leyen, President of the European Commission

## Slide 41
Summary from Feasibility Study
CERN Council launched in 2021 the feasibility study for FCC FS to provide input by 2025, required for further discussion, and in view of a potential project decision by end 2027/begin 2028.
Focus on implementation scenario developed with host state authorities
  Surface site areas identified and individual landplots reserved
  Electrical supply concept developed with FR and CH grid operators
  Road and highway connections identified and designs established
  Environmental initial state analysis for all surface sites completed
Colliders and technical infrastructures
  Two collider lattice variants established, optimization ongoing
  R&D activites started on main technologies (RF for FCC-ee, HFM for FCC-hh)
  Injector design optimized and implementation at CERN Prevessin site developed
  Technical infrastructures (EL, CV) system layouts developed
Cost estimate (by FCC FS) and funding model (CERN Council and Directorate)

## Slide 42
FCC Main Goals for Coming Years
Upcoming milestone for FCC is the completion of the Feasibility Study by March 2025 as input for the Update of the ESPP.
The following pre-TDR phase should prepare for a possible project approval by 2027-2028 and enable the subsequent start of CE design contract:
  Updated cost and schedule studies
  specifications to enable CE tender design by mid 2027
  refined input for environmental evaluation and project authorisation process
  requires overall integration study and designs based on technical pre-design of accelerators, technical infrastructure and detectors
Possible start of CE construction would then be 2032-33:
  CE groundbreaking
  TDR to enable prototyping, industrialization towards component production
Strong international collaboration is essential for success!

## Slide 43
Venue: Hofburg Palace, a historical and cultural landmark in Vienna, Austria.
Dates: Monday 19 to Friday 23 May 2025
Presentation of the Feasibility Study Report and review of its findings and opportunities for future R&D projects
Please save the date and join us in Vienna
FCC Week 2025 - Vienna