## Slide 1
Dave Gaskell
Jefferson Lab
November 6, 2024
RCS Compton Update

## Slide 2: Simple rate, measurement time estimates
Ebeam | Aavg | Tavg | Aenergy | Tenergy | Adiff | Tdiff
5 | 4.51% | 243 s | 5.78% | 148 s | 5.48% | 164 s
10 | 7.79% | 92 s | 10.15% | 54 s | 9.56% | 61 s
18 | 11.29% | 51 s | 14.91% | 29 s | 13.96% | 33 s
Average analyzing power:
 Average value of asymmetry over acceptance
Energy-weighted:
Differential:
 Energy deposited in detector for each helicity state
 Measurement of asymmetry bin-by-bin vs. energy, etc.
Assuming 80% polarization, <Plaser>= 6mW, 300 mm beam spot size…,  time for 1% measurement

## Slide 3: GEANT3 Simulations
Originally assumed a Cherenkov-style detector with number of photoelectrons proportional to number of particles incident on detector
Not easy to build such a detector with needed granularity
Switched to diamond detector – record total energy deposited in each strip for a single laser strip
Detector components:
1 mm W converter
500 strip diamond detector, 1 x 5 cm
W/SciFI calorimeter (not really relevant here)
Simulation = 100,000 backscattered photons
Assuming 10,000 photons/laser pulse = 10 laser pulses

## Slide 4: Energy deposited in Photon Detector
Assuming ~10,000 backscattered photons per laser pulse, large amount of energy deposited in photon calorimeter:
5 GeV  3.7 TeV
10 GeV  13.4
18 GeV  37.8 TeV
18 GeV
Energy per laser pulse
10 GeV
5 GeV

## Slide 5: Energy Deposited in Diamond Strips
18 GeV
5 GeV
10 GeV
2 cm

## Slide 6: Energy Asymmetry
Transverse polarization will be extracted using asymmetry in energy deposited in each strip
18 GeV
10 GeV
5 GeV

## Slide 7: RCS to-do list (still)
Get realistic beam parameters for RCS laser IP
  Due to RCS design questions, this will probably not be soon
Add 5 GeV, 10 GeV
Perform robust estimates of measurement times using this technique
Add another plane for measurement of out in-plane polarization
Check sensitivity to residual longitudinal polarization