## Slide 1
Agenda
Announcements
  Pre-TDR review process
  Next week lpGBT in FEB/RDO?
Issues That came up preparing for pre-TDR Draft
  More descriptive FEB / RDO Labeling System
  FEB / RDO distinctions and part in protocol
    lpGBT vs FPGA
    Clock’s
  Readout Cartoons and counts
  Positions of Electronics for Radiation Estimates
Electronics and DAQ WG Meeting 10/10/2024

## Slide 2
Pre-TDR Review Process:
In Zenodo:
  "EIC preTDR - Chapters 2 and 8, DRAFT, Version0.1".
Directions for getting into the ePIC “Community” on Zenodo are listed in the general meeting talk:
  (https://indico.bnl.gov/event/22602/contributions/88353/attachments/55269/94564/ePIC%20Collaboration%20News%2014%20June%202024%20rev2.pptx ),
  slides 10 and 11.
There are internal reviewers, but everyone is encouraged to read and give feedback to the collaboration at:
  https://forms.gle/iBtcGrFCbdRaRuuF9
Feedback deadline is October 20th

## Slide 3
Issues That came up preparing for pre-TDR Draft
  More descriptive FEB / RDO Labeling System
RDO
A) FEB/RDO names?

## Slide 4
Should we make a more descriptive naming scheme for FEB/RDOs?
Type |  | Technology | Clock |  | #In |  | Down BW (gbs) |  | #Out |  | UP BW (gbs) |  | Version | Total
AGG | - | L | 40 | : | 16 | / | 1.28 | - | 1 | / | 4.18 | - | 1 | AGG-L-40:16/1.28-1/4.18-1
AGG | - | F | 100 | : | 32 | / | 0.08 | - | 1 | / | 10 | - | 1 | AGG-F-100:32/0.08-1/10-1
 |  | L=lpGBT F=FPGA |  |  |  |  |  |  |  |  |  |  |  | 
Is this something we should do? Are there any existing schemes? opinions about what to encode?
CMS
Jermiah Mans’
Presentation to TIC:
Detector Database
(Construction
planning DB)
A) FEB/RDO names?

## Slide 5
B) Protocol Impact of lpGBT
V0.1 Data frames: Downlink: 64bits – 10.15ns
uplink: 64bits – 10.15ns (Frame definition TBD ~6.4 Gb/s) (8 Gb/s raw)
V0.1 ALCOR (VTRX+) Downlink: 32bits – 10.15ns (Frame definition TBD ~3.2 Gb/s) (4 Gb/s raw)
uplink: 64bits – 10.15ns (Frame definition TBD ~6.4 Gb/s) (8 Gb/s raw)
lpGBT: Downlink: 64bits – 25.375ns
uplink: 256bits – 25.375ns
Positional # of bits x 40MHz  Translated to serial line bits/sec
On each elink
(2  80 Mb/sec, 32  1.28 Gb/sec)

## Slide 6
B) Protocol Impact of lpGBT
100 Mhz Frames
40MHz Frames
100Mhz Frames
GTU
100 Mhz Frames
40MHz Frames
100Mhz Frames
Periodic Sync
CMD
Periodic Sync
CMD
RDO
100MHz Frames
RDO
40MHz Frames
FEB
100MHz Frames
FEB
40MHz Frames
Time Tag in 40 MHz based units
Relative to Last Sync
Time Tag in100 MHz based units
Relative to Last Sync
Offset + scaling to BX based units
Offset to BX based units
lpGBT
is always
“FEB”
“FEB” -> “RDO”
Positional bit fields is wasteful (lots of NOP) So must be different from RDO/DAM link protocol
Need to rethink commands. Ex. no BX needed/ or even defined here
Handle as much messaging in DAM as possible,
Lighten the protocol to the RDO.

## Slide 7
Service Hybrid
How many Sensors?
Staves?
BPOL?
Heat/cooling
C) Readout Cartoons
AC-LGAD Sensors
ETOF
EICROC
Bump Bonded to Sensor
Up to 2xlpGBT
Power?
Cooling?
Connector on Stave
To connector on Service
Hybrid
(differential serial 160Mhzx28 up)
(differential serial 80Mhzx28 down)
Up to 28 ASICs / Service Hybrid
Sensor Plane
Flat over Sensor
Plane
VTRX+
RDO
UltraScale+
FPGA
South Platform
SFP+
VTRX+
Pigtails
X(cm)
Power Supply
Power
Cables
DAM
DAQ Room
Fiber. up to 48 RDO / DAM
A Powerpoint Slide for each detector
An excel sheet with the total number of each component
An excel tab for each component / spec etc…
DSCs should supply info – but either Electronics and DAQ or TIC should organize it.
X,Y,Z positions of each type of electronics (or a specified range of values)
Come up with a format
On Det
Patch
Fiber
(XX)

## Slide 8
D) Positions of Electronics
Possibly related to previous. We need x,y,z positions for electronics…