Dual-radiator RICH: update
EIC PID consortium meeting
Alessio Del Dotto for the EIC PID/RICH collaboration
November 9, 2016

---
Outline
- Why a dual-radiator RICH (dRICH) in the h-endcup
- Some detail on the simulation:
  - established baseline
  - recent results and developments
- Future developments

---
Why a dRICH in the hadron side
We want to study several processes where the capability of PID is extremely important.
Common configuration Jlab/BNL (e 10 GeV x p 100 GeV)
- The high momentum region contains important physics (i.e. SIDIS)
- We want to have hadron-PID capability in the range [~3,50]

---
dRICH in the JLab EIC detector
dRICH

---
Mirror focused aerogel & gas
aerogel
gas
Goal: pi/K/p ID from 2.5 to 50 GeV/c
e/pi ID up to 20 GeV/c
polar angular coverage [5°,25°]
- Aerogel
  - 4 cm thickness
  - index of refraction 1.02 (lower than the usual 1.03)
- Gas (C2F6 or CF4) about 160 cm
  - C2F6 guarantee a good momentum matching with the aerogel
  - CF4 a larger momentum coverage
The dRICH is in magnetic field (3T central field in the simulation)
GEANT4/GEMC
simulation
mirror R = 2.8 m
Photo-detector:
spherical shape
8500 cm2 (per sector)
6 sectors of
60° in azimuthal
angle

---
Single p.e. error contributions
The Idirect Ray Tracing alghoritm has been used as an analysis tool!
 Photons coming from aerogel with wavelength below 300 nm cut by software.
Aerogel & C2F6
Aerogel & CF4
Assumed angular error on the track:
\Delta\theta=\Delta\phi=0.5~mrad

---
PID at 15° (polar angle)
Aerogel & C2F6
Aerogel & CF4
- Aerogel & C2F6 can be considered the optimal solution for our momentum range!
- QE curve - H12700

---
C2F6 & Aerogel PID table (15°)

---
PID at 5° polar angle
- Similar behaviour for a polar angle of 25°
- The dominant error for the gas is the emission error
\pi/K
K/p
e/\pi
{\color{blue} \bullet ~ C_2F_6}
{\color{red} \bullet ~ aerogel}

---
FY17 – proposed activities
- Study of the background, and acrylic shield between aerogel and gas [under study]
- Reconstruction algorithm improvement and comparison
- GEMC based digitalization of the photon-detector
- Formulation of requirements (magnetic field, track reconstruction, etc …) [essentially carried out]
- Study of the feasibility of the dRICH to fit the BNL version of EIC detector
Toward the first dRICH prototype:
- Identification of the baseline candidate as photo-detector (in magnetic field)
- Study and definition of the prototype

---
Study of the acrylic shield
Aerogel and C2F6 dual-radiator RICH with a shield to separate the aerogel from the gas, and to filter photons below about 300 nm
acrilic shield
thickness 3 mm

---
Transmittance and Absorption length
Transmittance is defined by a sigmoid function, and the Absorbtion length is with d = 0.3 cm
Implemented
in GEMC
A={d}/{\ln T}

---
Filtered spectrum
This is the effect of the shield on a beam of photons of E = [2,6.2] eV
With the shield there is an additional absorption of photons, even in the good range!
A trade off is needed!

---
Shield & background for aerogel
S/B % estimated reconstructing
the angular distributions with the
Indirect Ray Tracing alghoritm
The background increase at polar
angles higher than 20°!
Optical alignment?
Photons produced in the acrylic
escape the edge?

---
S/B at 25° (polar angle)
The background can be eliminated
with a selection cut!
Selection cut
Signnal
Background
\theta_{Ch}

---
To do next
- Study of the background, and acrylic shield between [continue the study: 1p.e. errors and PID performances ]
- Reconstruction algorithm improvement and comparison
- GEMC based digitalization of the photon-detector
- Formulation of requirements (magnetic field, track reconstruction, etc …) [essentially carried out]
- Study of the feasibility of the dRICH to fit the BNL version of EIC detector [to be addressed in the next month ]
Toward the first dRICH prototype:
- Identification of the baseline candidate as photo-detector (in magnetic field)
- Study and definition of the prototype

---
Backup: Momentum and angular uncertainties of the tracks
Traks generated in GEMC in this way, i.e. at 31 GeV/c :
<option name="BEAM_P" value="pi+, 31*GeV, 15*deg, 0*deg"/>
<option name="SPREAD_P" value="1.16*GeV,0*deg,180*deg"/>
<option name="SPREAD_P" value="3.48*GeV,0*deg,180*deg"/>
In addition an angular smearing has been added to the versor of the track entering
the RICH, in both polar and azimuthal angle
\Delta\theta=\Delta\phi=0.5~mrad
p = <p> \pm \Delta p