## Slide 2: Current Layout
Does not work
5.8 deg MPGD coverage angle
ToF:
  Inner Face Z: 1675mm
  Thickness Z: 75mm
  Outer Radius: 600mm
MPGD:
  Inner Face Z: 1500mm
  Thickness Z: 150mm
  Outer Radius: 500mm

## Slide 3: Option 1: Smaller Dia. Disks
Both disks shrink in diameter, MPGD disk would be attached to PST, unsure where ToF would be attached to.
7.4 deg MPGD coverage angle
ToF:
  Inner Face Z: 1675mm
  Thickness Z: 75mm
  Outer Radius: 450mm
MPGD:
  Inner Face Z: 1500mm
  Thickness Z: 150mm
  Outer Radius: 450mm

## Slide 4: Option 2: Removable Disks
Both disks would be removable, would need to figure out where to support them from. Disks will need wither space in X to move out or larger inner diameters to fit around flange (Flange doesn’t exist yet)
3.4 deg MPGD coverage angle
ToF:
  Inner Face Z: 1825mm
  Thickness Z: 75mm
  Outer Radius: 630mm
MPGD:
  Inner Face Z: 1650mm
  Thickness Z: 150mm
  Outer Radius: 630mm

## Slide 5: Option 3: MPGD goes Backwards
Requires moving the SVT disks around, need to figure out where we would support ToF from. ToF would still need to be removable.
4.9 deg MPGD coverage angle
ToF:
  Inner Face Z: 1750mm
  Thickness Z: 75mm
  Outer Radius: 630mm
MPGD:
  Inner Face Z: 1255mm
  Thickness Z: 150mm
  Outer Radius: 450mm

## Slide 6: Option 3: MPGD goes Backwards

## Slide 7: Option 3: MPGD goes Backwards

## Slide 8: Backup Slides