## Slide 1: SVT power estimates

## Slide 2: Introduction
Take Iain’s numbers (https://indico.bnl.gov/event/25211/contributions/98063/attachments/58158/99918/SLDO_Considerations_v13.pptx)
Do some scaling of the numbers there
Include AncASIC and FPC power loss
Multiply with numbers of chips
Use nominal and max categories as Iain

## Slide 3: Scaling
Iain gives power numbers for the 6-RSU LAS and the AncASIC in this case
I have scaled this for a 5-RSU LAS by using the current estimates given in another slide in his talk
For the AncASIC in the 6-RSU LAS case Iain gets 35% of the LAS power in the AncASIC for nominal and 45% of the LAS power for max
  I use the same 35%/45% for the case of the 5-RSU LAS for both cases
For the power loss in the FPC (200 mΩ/LAS) he shows distributions for the power loss with and without the FPC
  The resistance scales with number of LAS because of serial powering, assumption is that each LAS adds a trace corresponding to its own length
    More complex (long) FPC geometries will increase this)
  I eyeballed an additional power loss from the FPC of 20% in the nominal case, and 30% for max
I don’t have a number for MOSAIX for IB, so I scaled Iain’s 6-RSU LAS number
  I am sure that there are better numbers, and I am happy to substitute if you send them to me
  In any case, this is a small fraction of the overall power

## Slide 4: Numbers used
Power [mW] | 5 RSU |  |  | 6 RSU |  | 
 | LAS | AncASIC | FPC | LAS | AncASIC | FPC
Nominal | 1092 | 382 (35% of LAS) | 218 (20% of LAS) | 1224 | 428 (35% of LAS) | 245 (20% of LAS)
Max | 1689 (+55%) | 759 (45% of LAS) | 507 (30% of LAS) | 1897 (+55%) | 853 (45% of LAS) | 569 (30% of LAS)
OB |  | # of LAS/stave | # of staves | Total # of LAS
L4 | 5-RSU LAS | 16 | 70 | 1120
L3 | 6-RSU LAS | 8 | 46 | 368
OB and disks
disks | Total # of LAS
5-RSU LAS | 1104
6-RSU LAS | 1312
IB
Power [mW] | Power per 12-RSU row (incl. LEC & REC)
Nominal | 2014
Max | 3145 (+56%)
IB | # of sensors | Rows per sensor | Total # of rows
L0 | 4 | 3 | 12
L1 | 4 | 4 | 16
L2 | 8 | 5 | 40
Under review

## Slide 5: System power numbers
 | nominal |  |  |  | max |  |  | 
 | Power/stave [W] | Air flow per stave |  | Total power/system [W] | Power/stave [W] | Air flow per stave |  | Total power/system [W]
 |  | Volume [l/s] | Speed [m/s] |  |  | Volume [l/s] | Speed [m/s] | 
L0 |  |  |  | 24 |  |  |  | 38
L1 |  |  |  | 32 |  |  |  | 50
L2 |  |  |  | 81 |  |  |  | 126
L3 | 13.2 | 1.0 | 4.2 | 608 | 22.0 | 1.7 | 7.1 | 1012
L4 | 27.1 | 2.1 | 8.7 | 1896 | 47.3 | 3.6 | 15.2 | 3310
Disks |  |  |  | 5669 |  |  |  | 8929
Total power [kW] |  |  |  | 8.31 |  |  |  | 13.47
Total flow [l/s] |  |  |  | 641 |  |  |  | 1038
Volume flow is for cp,v = 0.00129 J/Kcm3
ΔT = 10°C, fully efficient
Stave air speed is for cross-section of 240 mm2
Total volume flow is at atmospheric pressure
641 l/s = 1358 cfm and 1038 l/s = 2199 cfm

## Slide 6: Further material
Slides from Iain

## Slide 7
LAS Current and Power Consumption
 | Voltage(V) | Typ Current Consumption (mA) |  |  | Max Current Consumption (mA) |  | 
 |  | RSU | LEC | EIC-LAS | RSU | LEC | EIC-LAS
GAVDD | 1.32 | 28 |  | 168 | 45 |  | 270
GDVDD | 1.32 | 71 | 100 | 526 | 111 | 150 | 816
GSVDD | 1.32 | 1.6 | 30 | 40 | 2.4 | 45 | 59.4
TXVDD | 1.2 |  | 200 | 200 |  | 300 | 300
Total |  |  |  | 934 |  |  | 1445
Converting to EIC-LAS
  Assume 6 RSU LAS
  Numbers in red do not have “Max” estimates in the previous slide, so assumed +50% on typ number (since this is true for supplies that do have it)
  EIC-LAS is one LEC and 6 RSU
  To calculate power for a LAS with Length L RSUs, use the formula below for each of the 4 supplies and add the results
    PLAS = V(IRSU * L + ILEC)
  To include the AncASIC power, use the power fractions (fPOWER) on this slide
    PANCASIC = fPOWER * PLAS

## Slide 8
AncASIC Performance
EIC-LAS, AncASIC and Total Power (mW) | MODE 0 |  |  |  |  |  |  |  |  |  | 
 | Typ |  |  |  | Max |  |  |  | Total |  | 
 | EIC-LAS | AncASIC |  |  | EIC-LAS | AncASIC |  |  | Min | Nom | Max
 |  | Min | Nom | Max |  | Min | Nom | Max |  |  | 
Global Digital | 701 | 131 | 210 | 238 | 1088 | 193 | 341 | 394 | 832 | 911 | 1482
Global Analog | 224 | 61 | 71 | 83 | 360 | 88 | 111 | 147 | 285 | 295 | 507
Services | 53 | 28 | 32 | 44 | 80 | 18 | 41 | 66 | 81 | 85 | 146
Serialiser | 246 | 47 | 115 | 128 | 369 | 37 | 172 | 246 | 293 | 361 | 615
Total | 1224 | 267 | 428 | 493 | 1897 | 336 | 665 | 853 | 1491 | 1652 | 2750
AncASIC Power Fraction |  | 21.81% | 34.97% | 40.28% |  | 17.71% | 35.06% | 44.97% |  |  | 
N.B. FPC traces add another 200mW
1702
2581
Prev values:
Overall Power Consumption

## Slide 9
Chart: PWR_Additional_TOT
| 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70
Typ - Mode 0 Shunt | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 3 | 12 | 6 | 21 | 36 | 46 | 54 | 108 | 68 | 78 | 63 | 30 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Max - Mode 0 Shunt | 0 | 0 | 0 | 0 | 0 | 7 | 6 | 9 | 6 | 24 | 24 | 39 | 45 | 56 | 83 | 66 | 71 | 55 | 31 | 13 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Typ - Mode 0 Tot | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 6 | 3 | 9 | 6 | 15 | 30 | 24 | 68 | 56 | 74 | 75 | 66 | 51 | 39 | 12 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Max - Mode 0 Tot | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7 | 3 | 6 | 9 | 3 | 18 | 12 | 18 | 33 | 30 | 36 | 60 | 48 | 72 | 57 | 37 | 44 | 24 | 17 | 4 | 4 | 0
FPC Consumption
  FPC traces consume considerable power
  Increase from ~35% to 50-60% of LAS
  Due to >1A through 200mohm
  Varies with Typ and Max corner due to current increase
  Cooling problem or not? To be included in model?
AncASIC Performance
Total Power Variation in Corners

## Slide 10
Power Caveats…
Caveats to the numbers
  Best estimate from MOSAIX. Not a warranty.
  Possibility that LEC value will rise (additional functions)
  For GAVDD, it is likely that EIC-LAS will be in the Max case, since we want the fastest frontend speed
  We may be able to reduce TXVDD consumption if we don’t need all the transmitters (or can run slower)
  Need to add consumption of non-SLDO AncASIC
  Mis-match in GAVDD, GDVDD consumption may require different input voltages (waste of power in serial powering chain)
  Irradiation
Future Updates
  May be future releases from MOSAIX
  AncASIC will need to be updated once porting to XT011 is completed
  Test results from ER2