## Slide 1
Clocks In the ASICs:
The question discussed on 10/9/24 referred to changing the clock on the CALOROC from 200 MHz to 320 MHz to support the lpGBT operation.
I think this was confusing to some of us because the we have talked about the ASIC clocks as being either the EIC/Synced CERN bunch clock (39.4 MHz) or the EIC clock (98.5 MHz). The 200 MHz, 320 MHz are the potential source clocks for the CALOROC, but in any case there are multiple internal clocks.
The reason for a 200 MHz input clock was that (pre-lpGBT) the EIC RDO was going to provide a multiple of the EIC clock and leave the clocking issues to the ASICs, so this was one of the changes the CALOROC was going to make for us. With the lpGBT based detectors, though, we will provide 39.4 MHz clocks from the RDOs. This makes the 200 MHz unneeded so it gets rid of one of the complicating changes that would need to be implemented!
The following pages describe the various clocks and how they are related:

## Slide 2
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
Digitization clocks:
Sensor Digitization:
  This clock is only relevant for time-binned ADC data. The digitization clock is built into sensor/ASIC. For the most part, these numbers are not under current discussion.
  EICROC: 39.4 MHz, CALOROC: 39.4 MHz, ALCOR: N/A, SALSA: 49.75MHz, FCFD: ?(N/A) MHz
Ramifications:
  For TOA/TOT the time is defined by discriminating the input voltage, not from integrated ADC values, so this clock is not directly related to time resolution for CALOROC/EICROC… but for mixed TOA/TOT + ADC modes the ADC part is relevant
  If the shaping time is longer than the digitization clock the time resolution comes from an average(fit) of ADCs, and can be much better than the time step, so a clock slower than 98.5 Mhz can still resolve times to a bunch crossing level using ADCs
  A clock different from the EIC Clock prevents the use of timing windows to separate collision data from backgrounds (as expected for ALCOR)
  When the clock edges start at a different time with respect to the collision, there could be subtle effects (the shape of the pulses, slewing, etc…) So there might need to be 5 different calibrations one for each potential collision phase for sampled ADCs @ 40MHz

## Slide 3
RDO
lpGBT based FEB
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
ASIC downlink connections:
Supplied Downlink Clock:
  The supplied clock also doubles as the bit rate for the serial communication, so it is correlated to the fast commands available.
  Typically, there is 1 downlink per ASIC and 1 or more uplinks per ASIC. The uplink/downlink are not necessarily at the same speed.
lpGBT supports: 80 MHz, 160 MHz, or 320 MHz downlinks
downlink supplied: EICROC: ? , CALOROC: (old 200 MHz, new 320 MHz), ALCOR: 394 MHz, SALSA: ?, FCFD: ?
    Downlink frame rate: EICROC 39.4 MHz, CALOROC 39.4MHz, ALCOR 98.5MHz, SALSA: 98.5MHz, FCFD: ?
Ramifications:
  The relationship between the internal ASIC clocks and supplied clocks is complex but not critical to the interfaces. They might affect the external specs, but the external specs are what matters, not the internal clocks.
  The downlink serial interfaces use this clock, so it defines bandwidth of synchronous commands available
  lpGBT only supports specific rates and the number of distinct connections allowed depends upon the rates
    Downlinks:
    The only clocks provided to the ASICs by lpGBT are the uplink/downlink clocks, so the ASIC must derive any internal/digitization clocks from the uplink or downlink clock. For ASIC based RDOs one could imagine separate clocks for the ASIC supply and the serial link rates.
  When we are talking about the RDO clock we usually mean the frame rate for this clock. This clock/number of bits per synchronous command. This is always going to be 40 MHz for lpGBT.
  We should consider the idea of ALL synchronous command delivery to be oriented towards 50.76 ns (5 x BX time) (Note that 1260 BX / revolution including abort gaps, divides 5)

## Slide 4
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
ASIC uplink connections:
Uplink Clock : The electrical connections to/from ASICs:
  Typically, there is 1 downlink per ASIC and 1 or more uplinks per ASIC. The clocks here are bit rates and define the data transfer rates. The uplink/downlink are not necessarily at the same speed.
lpGBT supports: 80MHz, 160MHz, 320 MHz, 640MHz, or 1.28GHz for uplink
uplink: EICROC: (1.28 GHz perhaps lower), CALOROC: 1.28 GHz, ALCOR: 788 MHz, SALSA: ?, FCFD: ?
Ramifications:
  The relationship between the internal ASIC clocks and the uplink/downlink and sensor digitization is complex but not critical to the interfaces. They might affect the external specs, but the external specs are what matters, not the internal clocks.
  lpGBT only supports the specific rates and the number of connections allowed per lpGBT depends upon the rate used
    Uplinks:

## Slide 5
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
lpGBT optical protocol:
lpGBT optical links:
  The optical links of the lpGBT are the serial drivers/receivers that connect the VTRX+ fibers. The optical part is a serial protocol, but this is translated automagically and presented as parallel frames with n bits transferred on a 39.4 MHz clock.
  Downlink Frame Format: (Serial rate 64 x 39.4 MHz= 2.5 Gb/s)
    40 bits are available for data
    2 bits (80 MB/s) for controlling internal registers
    2 bits (80 Mb/s) exported to “EC” pins
    32 bits (1.2 Gb/s) exported to directly to ASIC downlinks
  Uplink Frame Format: (Serial rate 256 x 39.4 MHz = 10 Gb/s)
    As Downlink frame but 224 bits available for data
    Bits still grouped according to their respective ASIC serial lines (8 bits per 320 Mb/s rate)
Ramifications:
  lpGBT doesn’t support any mode other than direct fiber access to the ASIC serial uplinks and downlinks. Only specific clocks are supported (at multiplies of 39.4 MHz)

## Slide 6
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
ASIC Slow Control connections (I2C or Programable logic port (PIO)):
Slow control links: these are effectively unlimited (in lpGBT 16 I/O ports, 3 I2C Masters capable of addressing multiple ASICS)
  lpGBT: There is an 80 MHz (39.4 MHz x 2 bits) “internal command” bit. This allows the setting of registers which control the slow I2C &/or PIO interfaces. The information is read/write. Sending/receiving data over these lines is going to be much slower. (I’m guessing 500Kb/s or so, but we’d have to gather information from experts)
  FPGA based RDO: This isn’t specified yet but expected to be similar.

## Slide 7
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
DAQ Optical Protocol:
DAQ Optical Protocol: Serial Clock Assumed ~10 GHz
  Pre-lpGBT:
    64 Bit frames @ 98.5 MHz
    RDO has knowledge of actual BX
    Fast commands are sent to the RDO which has the internal intelligence to distribute (by copies) to particular ASICs
    Unlike lpGBT aggregation protocol “zero-suppressed” rather than purely positional with all bits transferred to fiber.
Issues to resolve:
  3 different tech: 39.4 MHz @ 2.5Gb/s downlink, 98.4 MHz @ 2.5 Gb/s downlink, 98.5 MHz @ 10 Gb/s downlink
    Option 1: All RDO use 100 MHz. RDO converts 39.4 MHz -> 100 MHz
    Option 2: Some RDO at 100 MHz, some at 39.4 MHz. DAM converts 39.4 -> 100 MHz
  Exact protocol for ASIC communications is different. How does this affect proposed command protocols?

## Slide 8
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
Summary
ASIC | Downlink (baud) (Mhz) | Downlink frame frequency (MHz) | Uplink (baud) (MHz) | Uplink frame frequency (MHz) | FEB (baud) (MHz) | FEB frame freq (MHz) | RDO (baud) (MHz) | RDO Frame freq (MHz) | Digi clock (MHz) | RDO UP baud (MHz) | RDO UP Frame (MHz) | Intern clock (MHz) | Chain Type | Optics Type
EICROC | ?lpBGT? | 39.4 | ?lpGBT? | 39.4? | 2521 | 39.4 | - | - | 39.4 | 9850 | 39.4 |  | A (B?) | VTRX+
CALOROC | 315.2 | 39.4 | 1260x4 | 39.4 | 2500 | 39.4 | 7880 | 39.4 | 39.4 | 9850 | 39.4 | 315.2 | B | Com
ALCOR | 788 | 98.5 | 788 | 98.5 |  |  | 3152 | 98.5 | n/a | 9850 | 98.5 | 394 | C | VTRX+
SALSA | ? | ? | 1000 x 4 | 98.5 | 2462 | 98.5 | 3152 | 98.5 | 49.25 | 9850 | 98.5 |  | B | VTRX+
FCFD | ?(80) | 39.4 | 1260 | 39.4 | 2521 | 39.4 | - | - | n/a | 9850 | 39.4 | 39.4 | A (B?) | VTRX+
Discrete |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Astropix |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ITS-3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(…) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(B)
(C)
FEB
(lpGBT)
ASIC
Sensors
(A)
DAM
DAM
DAM
RDO

## Slide 9
RDO
FEB
(lpGBT)
ASIC
Sensors
RDO
ASIC
Sensors
FEB
(Stave)
(Module)
Summary
ASIC | Downlink (bits) (Mhz) | Downlink frame frequency (MHz) | Uplink (bits) (MHz) | Uplink frame frequency (MHz) | FEB (bits) (MHz) | FEB frame freq (MHz) | RDO (bits) (MHz) | RDO Frame freq (MHz) | Digi clock (MHz) | RDO UP bits (MHz) | RDO UP Frame (MHz) | Intern ASIC clock (MHz) | Chain Type | Optics Type
EICROC | ?lpBGT? | 39.4 | ?lpGBT? | 39.4? | 2521 | 39.4 | - | - | 39.4 | 9850 | 39.4 |  | A (B?) | VTRX+
CALOROC | 315.2 | 39.4 | 1260x4 | 39.4 | 2521 | 39.4 | 7880 | 39.4 | 39.4 | 9850 | 39.4 | 315.2 | B | Com
ALCOR | 788 | 98.5 | 788 | 98.5 |  |  | 3152 | 98.5 | n/a | 9850 | 98.5 | 394 | C | VTRX+
SALSA | ? | ? | 1000 x 4 | 98.5 | 3152 | 98.5 | 7880 | 98.5 | 49.25 | 9850 | 98.5 |  | B | VTRX+
FCFD | ?(80) | 39.4 | 1260 | 39.4 | 2521 | 39.4 | - | - | n/a | 9850 | 39.4 | 39.4 | A (B?) | VTRX+
Discrete |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Astropix |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ITS-3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(…) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(B)
(C)
FEB
(lpGBT)
ASIC
Sensors
(A)
DAM
DAM
DAM
Assume ~10 Gb/s
Assume:
7880 = 80 bits x 98.5 (William Gu)
3152 = 32 x 98.5 (VTRX+ max DL)
2521 = 64 x 39.4 (lpGBT DL)
3152 = 32 x 98.5 (VTRX max DL)