## Slide 1: Clustering for SBND To build a full SigProc (DNN) – Imaging – Clustering Chain for SBND
Haiwang Yu, Nov. 12

## Slide 2: Outline
Xin, Brett and I have finished the initial translation of the uboone clustering to WCT.
  runs but not validated yet
Next:
  validation – Xin, Haiwang
  adaptation to more experiment
    SBND – Haiwang, Ewerton

## Slide 3: Clustering steps/configuration
merging:
para, prol, dead, regular
separate, accidental crossing tracks
separate
merging, dotted line
separate
separate, remove ghost
merging, neutrino
merging, merge small to large
Imaging: clustering based on blob overlapping
Clustering:
  to combat various failure cases (parallel, prolonged, dead, imaging failure)
  specific scenarios (neutrino, small activities, boundaries, over-clustering)

## Slide 4: Configurable knobs
Parameters already extracted
  length_cut – expected gap size to jump
  num_try – try and optimize
TPC geom:
  wire pitch, angle
  boundaries
Many hard-coded numbers on distance, angle cuts
  treat them like human-made NN
    given the wire LArTPCs are similar in sense of wire pitch, those numbers may be fine?

## Slide 5: SigProc (DNN) – Imaging – Clustering for SBND
As part of QL-Matching for SBND
  Show some progress at the coming SBND CM (Dec. 10)
DNN – Moon, Avinay
  status: production workflow available
  WIP: passing though “summary” for imaging
  validation - matching the charge – check the uncertainty
Imaging - Ewerton
  status: Ewerton has something working locally
  WIP: more general purposed coding needed; refactoring on going
  validation:
    geometry: projection of imaging vs. SigProc result
    check some of the equation solving cases
Clustering
  status: placeholder available, need to replace with real devs.
  make sure the APA boundaries are configured correctly for SBND

## Slide 6: Previous development
larwirecell
OpFlashSource
larwirecell
FrameSource
(ADC/SigProc)
charge-pipe
(SigProc)-Img-Clus
TensorFileSink (dump)
QLMatching
(larwirecell)
Fanout
larwirecell
OpFlashSource
charge-pipe
(SigProc)-Img-Clus
TensorFileSink (dump)
QLMatching
(larwirecell)
0
1
Bee.json
Bee.json
Bee.json
stand-alone python

## Slide 7: Planned workflow
larwirecell
OpFlashSource
larwirecell
CookedFrameSource
charge-pipe
Clustering
TensorFileSink (dump)
QLMatching
(larwirecell)
Fanout
TensorFileSink (dump)
QLMatching
(larwirecell)
0
1
Bee.json
Bee.json
Bee.json
stand-alone python
charge-pipe
ChSel-Imaging
live
dead
charge-pipe
Clustering
charge-pipe
ChSel-Imaging
live
dead
larwirecell
OpFlashSource

## Slide 8: Input/Output
Input: Need to match the staged production: start from recob::wire
  all information need to be available: trace; cmm; summary
  traces need to be dense after reading in
Output: BEE for now
  ITensorSet output available?
  Need optional ICluster output?
  Future IO for AI/ML

## Slide 9: Tasks to make the chain running
wire-cell-toolkit: apply-pointcloud [porting] → master
larwirecell: merge Ewerton and Haiwang’s branches
  CookedFrameSouce
  QLMatching
jsonnet: merge Ewerton and Haiwang’s branches

## Slide 10: Backups

## Slide 11
Fanout
ChannelSelector
ChannelSelector
img-active
img-masked
PointTreeBuilding
MABC
dump
CookedFrameSource

## Slide 12: Separate_2 does not break clusters
Separate_2 -> b2id
add function calculate length from list of blobs

## Slide 13: Event
wcsimsp_g4_gen_prodgenie_bnb_nu_cosmic_sbnd_nskip6.root

## Slide 14: Nov. 7

## Slide 15
Deghosting: Projection2D::get_projection
DNNROIFInding: no trace summary

## Slide 16: DNNROIFInding: no trace summary
indices, summary: two arrays with same length with indexing corresponding to traces
irow -> index
ch = m_chlist[irow]

## Slide 17: Oct. 31

## Slide 18: Building the SP(DNN)-Img-Clus workflow
SigProc with DNN-ROI: https://github.com/LArSoft/larsoft/releases/tag/v10_00_03
wire-cell-toolkit
  DNNROIFinding: passing through summary/RMS to dnnsp frame
  ChannelSelector
larwirecell
  CookedFrameSource
Imaging (ICluster):
I had issues running imaging on data, but Ewerton has a working version, incorporating his local devs
  wire-cell-toolkit, larwirecell, cfg
using dnn-roi in imaging
  synergy with PDHD
Clustering (ITensorSet, PointCloud::Facade):
Configurable clustering_function to run in MultiAlgBlobClustering
  json -> c++