## Slide 1: Addressing the Needs of WG#2 Laser-Plasma Interactions
Igor Pogorelsky

## Slide 2: Charge to WG#2

## Slide 3: Community input
What Mid-IR (10 mm) means for plasma accelerators
  Electron acceleration – larger “bubbles” for external injection, staging, ultra-low emittance
  Ion acceleration – gas targets, monoenergetic regimes such as shock wave, possibility to access energies of cancer therapy interest
Power requirements
  LWFA milestones: self-modulation (2 TW, a0~1), blow-out (5-10TW a0~2), bubble (25-30TW, a0~4)
  Ion acceleration – energy scaling ~a02, next milestone 20 MeV with 10-20 TW, need a0~10, ~100 TW for 100 MeV/nu
Pulse duration
  Sub-picoseconds (~500 fs) for LWFA blowout/bubble
  1-3 ps for other applications, including ions
Pulse structuring
  Controlled pre-pulse for ion acceleration

## Slide 4: Community input (continues)
Polarization
  Linear
  Circular
Pulse stability, contrast, repetition rate
  <10%
  Important for going forward to applications
High-quality electron beam from RF linac
  10 fs, 10 mm,100 pC, 1 mm.mrad
  Essential for suggested LWFA studies (external injection, staging, emittance preservation, etc.)
  Wake field imaging
NIR lasers
  ~10 TW, ~100 fs
  Ionization injection
  Plasma diagnostics
  Synchronization requirements

## Slide 5: Alignment of ATF/ATF-II plans with community needs
Power requirements
  ATF will support near-term needs with up to 4 TW
  ATFII milestones co-aligned with long-term needs (10, 25, 100 TW)
Pulse duration
  2 ps for near-term applications
  Attempt to speed up development of sub-ps regime concentrating on efficient and reproducible ~500 fs pulses
Pulse structuring
  Pre-pulse provided
Polarization
  Linear and circular can be provided with direct amplification (no CPA)
  ATF-II plan does not (presently) include technology development for circular polarization of high power pulses
Pulse stability, contrast, repetition rate
  Work on improving, pulse stability of a high priority
High-quality electron beam from RF linac
  Provide at ATF
  In a core plan for ATF-II
NIR lasers
  Looking for collaborative support to refurbish and put on line to make available at ATF and ATF-II

## Slide 6
Seed pulse generator
Regenerative amplifier
ATF-II laser facility in making

## Slide 7: Impact from ATF-hosted laser/plasma research
Ion Acceleration
  Cancer therapy
  Spin-off to deuteron, neutron, and THz sources
LWFA
  Compact light sources based on combination of a high-charge LWFA and high-yield Compton scattering
  Test bed for R&D towards the next linear collider

## Slide 8: Roadmap to plasma colliders
  100 pC ~10 GeV demonstration
  Matched laser guiding in plasma
  Improve stability, reproducibility and tenability, to enable near-term applications as well
  LWFA-based positron source
  Staging with >90% capture and emittance preservation, understanding emittance growth mechanisms and mitigation
  Optimize efficiency from laser to beam, including bunch shaping and wake energy dumping by additional pulses
  New diagnostics development and testing
  Experimental validation of new simulation tools

## Slide 9: ATF diversity in addressing community needs
PWFA
LWFA
Two-color/low e
all-optical Trojan Horse
Matched guiding
Ion Acceleration
Shock Wave
RPA, BOA, RITA, …
Seeded LWFA
LWFA stability study
LWFA staging study
Wakefield probing with e-beam
Compton sources
Positron sources
ICS Conversion for gg colliders
LWFA

## Slide 10: Laser/plasma R&D enabled by CO2 Capabilities
2TW/3ps | 4TW/2ps | 10TW/2ps | 20TW/0.5ps | 40TW/0.25ps | 100TW/0.1ps
Self-modulated LWFA |  | Blowout and Bubble |  |  | 
Seeding
Staging
Two-color, low-
Probing, diagnostics, codes benchmarking
Shock wave acceleration
RPA, BOA
5 GeV
Deuterons, neutrons, THz
Biological tests
Medical application
3
Laser channeling
LWFA
Ions
Program would benefit from:
Large-scale plasma structures
Available well-controlled fs electron linac bunches
Access to low-density SWA technique

## Slide 11: Thank you for attention

## Slide 12: LWFA and Compton R&D Enabled by CO2 Capabilities
2TW/3ps | 4TW/2ps | 10TW/2ps | 20TW/0.5ps | 40TW/0.25ps | 100TW/0.1ps
Self-modulated LWFA |  | Blowout and Bubble |  |  | 
Seeding
Staging
Two-color, low-
Probing, diagnostics, codes benchmarking
High-charge regime
All-Optical Trojan Horse
5 GeV
All-Optical Compton
All-Optical Compton FEL
Positron source
3
Laser channeling
LWFA
+Compton
Program would benefit from:
Large-scale plasma structures
High-charge LWFA electron bunches
High photon fluxes per laser energy
Available well-controlled fs electron linac bunches

## Slide 13: 3-D simulations of multi-GeV LWFA stage
Propagation in
a matched channel
400 fs 60 TW CO2 laser focused to w0=262.5 mm at the entrance to a 3.2x1015cm-3 matched parabolic plasma channel.
Courtesy of Wei Lu
Bubble charge
Notes: PIC simulations show that a Cow laser can produce a really nice bubble, several GeV acceleration per stage, considering channeling. But we really need a subpicosecond pulse. Our best result so far was 2 ps. With such a pulse, the bubble conditions is very difficult to satisfy.

## Slide 15: Two optimum regimes for LWFA collider stage
Parameter | Ti:S | CO2
Laser wavelength (mm) | 0.8 | 9.2
Plasma density (×1016cm-3) | 11 | 0.35
Plasma wavelength (mm) | 99 | 560
Laser pulse duration (fs) | 130 | 700
Laser radius (mm) | 63 | 360
Laser peak power (TW) | 300 | 75
Laser energy per stage (J) | 40 | 52
Number per bunch (×109) | 4 | 23
Single stage interaction length (m) | 0.79 | 1.1
Accelerating field (GeV/m) | 12.6 | 2.2
Energy gain per stage (GeV) | 10 | 2.4
Number of stages | 50 | 208
Collision rate (kHz) | 10 | 0.3
Average laser power per stage (kW) | 400 | 16
Linac length (stages 0.5 m apart) (m) | 65 | 448
Total laser power (MW) | 20 | 2.6
limited by beamstrahlung
e- + e+ g
Beamstrahlung is irrelevant for gamma colliders
the number of beamstrahlung photons and
the induced beam energy spread both ~

## Slide 16
Power milestones? 20 MeV -10TW, neutron production
Pulse duration?
RPA: E~txI, need prepulse, pulse structuring 1 ps, short diagnostic

## Slide 17
CO2 laser beam channeling
No discharge
Discharge, no attenuation
Same with attenuation, shows 160 mm FWHM
17

## Slide 18: Short-term upgrade plan in progress
Building 820 CO2 Laser Configuration | Pulse Energy (J) | Peak Power (TW) | Pulse Width (ps) | Efficiency of utilization (%) | Power to Experiment (TW) | Target Date for Users
Current status | 6 | ~2 | 3-3.5 | ~25% | ~0.5 | FY16
Addition of Plasma Shutter | 6 | ~2 | 3-3.5 | 80-90% | ~1 | Mid FY17
CPA Reconfiguration (no Isotopes) | 6-10 | 2-3 | 3-3.5 | 80-90% | ~1.6-2.4 | Mid FY17
CPA Reconfiguration with Isotopes | 6-10 | 3-4.5 | 2-2.5 | 80-90% | ~2.4-4 | Early FY18
Non-linear Pulse Compression | >1 | >1 | <1 ps | 80-90% | ~1 | Late FY18
18

## Slide 19
Plasma shutter to eliminate harmful reflection from plasma at the experiment’s IP back into amplifier to allow full-scale operation in the present configuration, which is capable to 2TW, whereas we are limited to 0.5-1TW by this reflection.
CPA: Operating above 1TW in DA regime we see significant distortions in the beam due to nonlinear (high-intensity) effect on the amplifier’s output window. We eliminate it and extract much higher energy from amplifier using a stretched pulse that will be compressed with gratings after the amplifier. Telescopes will be installed to use bigger surface of compressor gratings.
Isotopes to increase the amplifier bandwidth to allow shorter pulses immediately in DA regime or upon compression in CPA regime.
NLPC: We will explore the possibility of productive use of the observed self-modulation of the laser pulse during DA through the second amplifier by selecting a self-focused beamlet, measuring its parameters and attempting to compress. This analysis is essential for designing a full-scale NLPC for 912 and may provide users at 820 with a sub-picosecond pulse.
Prime thrusts of the ATF CO2 laser short-term upgrade

## Slide 20
Layout of CO2 Laser System main components at ATF-II
Final
Amplifier
Seed Pulse
Generator
Regenerative
Amplifier
CPA
Compressor
IRS
NLPC
Laser
Experiment.
Systems
CO2 Laser Transport