## Slide 1: Dynamic Node Self-Organization
Bill Claycomb
Member of Technical Staff
Sandia National Laboratories
Albuquerque, New Mexico, USA
Sandia is a multiprogram laboratory operated by Sandia Corporation, a Lockheed Martin Company, for the United States Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
May 26, 2010

## Slide 2: What is Self-Organization?
Network nodes forming groups on their own
  No centralized component directing group formation
May be ordered or randomized
Group size may vary
Group may need to re-organize
  Times may vary
What about newly joined nodes?
What about nodes that disappear?
Very similar to network formation in wireless sensor networks
  Except the domain is potentially much larger

## Slide 3: Why Self-Organization?
Eliminates the need for centralized management
Randomized self-organization
  Unpredictable
  Exposes nodes to variety of different neighbors
  May allow communication/collaboration across network boundaries

## Slide 4: Dynamic Self-Organization Considerations
Nodes organize randomly across an entire network
Advantages
  Group membership cannot be predetermined
Disadvantages
  Communication is likely to be across subnets
    Network could be impacted
    Performance could be degraded

## Slide 5: Local Subnet Dynamic Self-Organization

## Slide 6: Local Subnet Self-Organization Protocol
Generate large random number, X
Determine number of groups per subnet, G
Determine index of group membership within the subnet, Z:
Use index to join the appropriate multicast group (i.e. 230.0.0.Z)

## Slide 7: Local Subnet Self-Organization Analysis
Advantages
  Easy to compute
  Communication likely to be fast
Disadvantages
  Communication is not across subnets
  Communication is limited to within an individual group

## Slide 8: Global Dynamic Self-Organization

## Slide 9: Global Self-Organization Protocol
Large random number, X
Total number of groups per network, T
Determine index of group membership within the network, Z:
Use index to join the appropriate multicast group (i.e. 230.0.Za.Zb)

## Slide 10: Global Self-Organization Analysis
Advantages
  Easy to compute
  Communication is across the entire network
  External collaboration exists
Disadvantages
  Communication may be slower
  Networks formed are randomized – no guarantee of distance between nodes
  Communication is limited to within an individual group

## Slide 11: Hybrid Dynamic Self-Organization

## Slide 12: Hybrid Dynamic Self-Organization Protocol
Large random numbers, X1, X2
Number of groups per subnet, G
Number of subnets, S
Total number of groups is
Percent of each group that should be “remote” nodes (outside local subnet), F
Calculate
If then the node is “remote”
  a. Use as subnet index
  b. Use as group index (within subnet)

## Slide 13: Hybrid Dynamic Self-Organization Protocol
If the node is “local”, determine index of group membership within the subnet,
Use index to join the appropriate multicast group (i.e. 230.0.0.Z)

## Slide 14: Hybrid Dynamic Self-Organization Analysis
Advantages
  Communication across subnets
Disadvantages
  Communication may not be as fast
  Need to be able to determine number of subnets in an organization
  Communication is limited to within an individual group

## Slide 15: Hierarchical Dynamic Self-Organization

## Slide 16: Hierarchical Dynamic Self-Organization Protocol
Large random number, X
Number of groups per subnet, G
Determine index of group membership within the subnet,
Use index to join the appropriate local multicast group (i.e. 230.0.0.Z)
Share X with group members, choose node with median value to be group leader

## Slide 17: Hierarchical Dynamic Self-Organization Protocol
Group leaders join local network multicast group
If the number of group leaders exceeds the average group size, form a secondary group using steps 1-5. Repeat as necessary
Subnet group leaders join a network-wide multicast group.
If number of subnet group leaders exceeds the average group size, form a higher-level group using steps 1-5. Repeat as necessary.
Top-level group does not need to choose group leader

## Slide 18: Hierarchical Dynamic Self-Organization Analysis
Advantages
  Communication across subnets
  Communication with all nodes in the network
  Group leaders may store/consolidate information from member nodes
  Allows collaboration with larger group using less communication overhead
Disadvantages
  Communication may not be as fast
  Need to be able to determine number of subnets in an organization
  Group leader failure could result in lack of communication with group members

## Slide 19: Performance Considerations
Is multicast enabled on the network?
Are necessary multicast addresses available?
Network communication is necessary to establish hierarchical groups
  Additional node overhead

## Slide 20: My Question to YOU
What are the potential applications?

## Slide 21: Future Directions
Hybrid-Hierarchical Dynamic Self-Organization
Simulation
Implementation and testing
Performance evaluation
Application to ongoing challenges

## Slide 22: Your Questions for Me
http://www.sandia.gov
wrclayc@sandia.gov