## Slide 1: Change in magnetic fields after flattening the roof of the High-Field Test return yoke ?
Kin YIP
Nov. 23, 2016
J. Hock (2016-11-18) : The reason for the change is that the original thicker steel planned to be used for the roof was found (after re-analyzing) to be contaminated with Co-60 and therefore cannot be sent out to Streck to be machined.
Notes: Just a title slides

## Slide 2
Original

## Slide 3
Flattened
N. Tsoupas helped make the change (in W. Meng’s preprocessor model) by changing the material in the relevant parts from “steel” to “air”.

## Slide 4: Any Major Change ?
original
Gauss
Gauss
flattened
Central Field (Bz) after flattening
  Bz(0,0,0) = 13734.4 G  13734.2 G

## Slide 5
Original

## Slide 6
Flattened

## Slide 7: Brett Parker confirmed (Nov. 22, 2016) …
Hello,
I confirm Kin's results. The change in central field is negligible (well within the error of having a different mesh) and the change in external field is less than 2 gauss.
While I am also using Opera3D, my model uses a different, more detailed, geometry that I got from John Cozzolino a while ago and can be considered an independent calculation.
I am trying to get several things done before the holiday time (after which I leave for a CERN visit) so I won't attend the meeting this week, but Kin can report these results. – Brett