## Slide 1
Gray Putnam (they/them)
SBN WG
Jan 9, 2025
Signal Processing + DNN ROI in ICARUS

## Slide 2: Introduction
I have been working on getting the WireCell 2D signal processing working in ICARUS
Main steps:
  Infrastructure adaptation (presented here previously, now done with work from Jacob C., Brett, others)
  Filter optimization
  DNN ROI
I’ll review what we have completed, and show progress on the DNN training (work by Avinay Bhat)

## Slide 3: What are the Goals?
My goal is to get the WireCell signal processing at parity in ICARUS with where SBND is at
My hope would be that we could explore combining publication of the signal processing work across SBN
I’m hoping to continue that conversation here (and in future WireCell meetings)
  Please let me know what you think, and what we need to do to get ICARUS to parity with SBND

## Slide 4
Filter Optimization

## Slide 5: Filter Optimization
WireCell has two filter stages:
  Wiener-like filter for ROI finding
  Gaussian filter for charge extraction

## Slide 6: Filter Optimization Parameters: ROI
There are three parameters in the ROI filter (which is intended to be Wiener-like):
  Time axis:
    : filter frequency
    : interpolates from Gaussian () to cutoff ()
  Wire axis:
    : wire filter frequency

## Slide 7
Efficiency x Purity comparison, Nominal 1D v Optimized 2D
Filter Optimization Results: Improvement in ROI Identification
See DocDB 38074
for details

## Slide 8: Filter Optimization Parameters: Charge
There are two parameters in the charge extraction filter (which is a Gaussian):
  Time axis:
    : filter frequency
  Wire axis:
    : wire filter frequency

## Slide 9: Charge Filter Optimization
Optimize for charge resolution, in space of Gaussian filter width

## Slide 10: Charge Filter Optimization
Optimize for charge resolution, in space of wire filter width

## Slide 11
Nominal 1D v Optimized 2D
Improvement in Charge reconstruction
The change in charge scale is due to a WireCell configuration parameter that we have since fixed

## Slide 12: Event Displays
S/N is much improved!
The low wire-frequency cutoff smears charge across wires on the induction planes
Is this bad? We’ll have to look at higher level variables
Plane 0
Plane 2
Plane 1

## Slide 13
DNN ROI Training

## Slide 14: Sample Generation: Gen types
We are generating samples for training the DNN
(Today): Corsika cosmic-only MC
(Future): Cocktail of:
  BNB neutrino + cosmic
  NuMI neutrino + cosmic
  Extended muons
Validation tests with HPS -> e+e- decays

## Slide 15: Sample Generation: Detector Simulation Types
Nominal detector simulation
“Opaque” detector simulation (middle induction signal shape with largest intransparency)
“Rand” detector simulation (Omnidetector)
Time
Arb. Amplitude
2nd Ind. Signal Shape. Most intransparency
Time
Arb. Amplitude
2nd Ind. Signal Shape. Least intransparency
SBN DocDB 32136

## Slide 16: Sample Generation: Detector Simulation Types
Nominal detector simulation
“Opaque” detector simulation (middle induction signal shape with largest intransparency)
“Rand” detector simulation (Omnidetector)
Baseline variations in “Rand”:
  Electron lifetime, uniform from 2-15 ms
  Channel gain, gaussian 10% variation
  Noise, gaussian 5% variation
  Electronics response width, gaussian 5% variation
  Middle induction signal shape, uniform from least to most transparent

## Slide 17: Training the DNN
Example training on front induction
Validation loss converges after a few epochs
Avinay Bhat

## Slide 18: Inference Results: Efficiency, Purity
Avinay Bhat

## Slide 19: Inference Results: Efficiency*Purity
Performance is stable, mostly independent of detector simulation
Not much difference in performance from different model trainings
Avinay Bhat

## Slide 20: How Precise are these Metrics?
Compare eff*pur computed between two halves of each dataset
Result: difference on order of ~1-2%
Avinay Bhat

## Slide 21: Inference Results: Compared to Traditional
Compared to traditional ROI performance (slightly different efficiency computation, nominal MC)
Signal Processing | Efficiency | Purity | Efficiency*purity
Plane 0, Nom. 1D | 0.87 | 0.74 | 0.65
Plane 1, Nom. 1D | 0.85 | 0.42 | 0.36
Plane 0, Trad. ROI 2D | 0.90 | 0.94 | 0.85
Plane 1, Trad. ROI 2D | 0.90 | 0.92 | 0.83
Avinay Bhat

## Slide 22
At first, running the DNN inference took ~30GB of memory
Running the DNN
Inference on ind 1
Inference on ind 0

## Slide 23
Improved this by:
  Separating operation of DNN into “chunks” along plane
    https://github.com/WireCell/wire-cell-toolkit/pull/340
  More aggressively dropping deconvolved arrays
Running the DNN
12 minutes/event
10GB memory

## Slide 24
Event display of DNN ROI’d waveform
Not running correctly, still some bugs to work out
Integration Back into LArSoft
Plane 0

## Slide 25: Integration Back into LArSoft
What do I need to configure to get DNN running correctly?
  input_scale (1/2000.)
  tick_per_slice (8)
  Does anything need to be different for chunking?

## Slide 26: Conclusion
The filter optimization and infrastructure adaptation to enable WireCell signal processing for ICARUS is now complete
DNN ROI training is ongoing
  So far, looks like it will provide further improvements
  Going to test a broader array of gen types and detector simulations
  Few bugs to work out for running inference in LArSoft