## Slide 1: BIC prototype test at CERN PS and plan for KEK
Jan 14th 2025
BIC System Testing Meeting
Jeongsu Bok (Pusan National University)

## Slide 2: Outline
Beam test at CERN PS in Aug. 2024
  Production
  Experimental Setup
  Results
Future beam test plan
  At KEK in Mar. 2025
  Future options

## Slide 3: Prototype
3x5 stacking of 32x3x3 cm3 unit modules
  32x9x15cm3
  Fiber is bundled, glued, and polished
  Connected to glass PMT
  Power supply in additional board, connected to DAQ module and trigger board using USB and LAN
Additional module with SiPM
Implemented geometry based on material composition of prototype
Previous Pb/SciFi - SiPM

## Slide 4: Beam Test Setup at CERN PS T10

## Slide 5: Beam Test Setup at CERN PS T10
DAQ: DRS4-DAQ 3x36ch from
30ch PMT(R11265-100)
DWC
Cherenkov
Trigger scintillator
Trigger
DWC

## Slide 6: Pulse Height Adjustment and Calibration
Starting from beam position confirmation
  Moving beam position (table) from end to end to confirm the beam position
  Pulse height drops at the edge
Pulse height adjustment
  Based on energy deposit in GEANT4 simulation
  Adjust PMT HV to make module response similar
  Also to prevent saturation at 5 GeV/c
Calibration
  2million events to center of prototype.
  Compare integrated ADC and energy deposit in simulation for each module
  After summing the signals from all modules, apply additional scale factor for the total energy deposit
PID using Cherenkov Counter
Beam position using Delay Wire Chamber
Electron selection using two Cherenkov counters
Determine integral range in time structure

## Slide 7: Beam profile at T10
After electron selection
Position using Delay Wire Chamber
Triggered area 10x10mm2 smaller than beam size
Almost straight, according to DWC1-2 correlation
3 GeV/c
depends on collimator setup
and beam energy
10mm

## Slide 8: Experimental Program
Energy response using 0.5, 1, 2, 3 GeV/c electron beam
Horizontal position scan for time resolution
SiPM module
Additional tests

## Slide 9: Result
Stochastic term: 11.5%
Constant term: 7.2%

## Slide 10: Result: Linearity
The result is linear within 4%
  Function: constant
  Band: 4%
However, little bit larger than energy deposit in simulation due to Gaussian fit.
EReco/EBeam
Ebeam [GeV/c]

## Slide 11: Result: Longitudinal shower profile
Energy deposit is maximum at
2nd module in 0.5,1 GeV/c
3rd module in 2,3 GeV/c
Beam
Beam
Energy Deposit [%]

## Slide 12: Result: Time resolution
𝜎 of Time(Left-Right)
Using constant fraction 30%
Most upstream module 𝜎 ~ 280ns
  Depends on module and light yield
  More energy deposit in downstream
SiPM module showed comparable performance in time resolution and energy resolution.

## Slide 13: Result: Effective Speed
-13,-10,-5,0,+5,+10,+13cm
Then, horizontal length difference: +26,+20,+10,0,-10,-20,-26 cm
Checked 𝜇(tL-R)
Most upstream module
Without reflection
  n = 1.59(core) 1.49(clad)
  v = c/n = 18.8 cm/ns
Data: 15.4 cm/ns
Checking simulation

## Slide 14: Future Testbeam Plan

## Slide 15: Schedule
KEK (1~5 GeV/c electron)
  March 2025: proposal submitted on Jan. 8th
    Beam period: March 6th ~ 24th
  May-June 2025
  Oct-Dec 2025
CERN PS (0.5~5 GeV/c electron, muon, pion)
  Submitted proposal on Oct. 21st, aiming August 2025
  0.5~5 GeV/c electron beam, muon possible
  https://ps-sps-coordination.web.cern.ch/ps-sps-coordination/

## Slide 16: KEK beam line
Counting Room
Trigger Counters
Beam Shutter

## Slide 17: KEK beam rate and profile
Rate: Overall rate is 2~2.5 kHz, Highest rate ~ 3 GeV. Δp/p: 10%
At 3 GeV, 𝜎~4mm, wide in x-direction, Beam rate with 8mm x 8mm: 350 Hz
Naive estimation for 8x8mm2 trigger area: 87,255,350,203,63 Hz at 1,2,3,4,5 GeV/c
At CERN PS using 10x10mm2 trigger area (+DWC,Cherenkov)
  0.73, 2.9, 5.6, 6 Hz at 0.5,1,2,3 GeV/c

## Slide 18: Plan for the KEK beamtest in March
If we get beam time, programs are
  Energy scan for 3x8 or larger
    95% energy deposit for 3 GeV electrons
  AstroPix test
  Calibration of separated Pb/SciFi
  Hodoscope operation
  If possible, AstroPix shower shape
Goals in intermediate term
  PMT  SiPM comparison
  Build a bulk sector (70cm)
  AstroPix+ Pb/SciFi

## Slide 19: backup

## Slide 20: Expected result in future measurements
Future measurements with larger volume, tail due to leakage will shrink
  If we narrow the fit range, it becomes 10.3%⊕5.1%

## Slide 21: Backup: expected stochastic term

## Slide 22: Backup: Fitting with Noise Term
In case of limited fitting range (not the official result)
3 parameters for 4 datapoints
For the fit with 3 parameters, 6.1% of stochastic term does not make sense in this setup
We will include more points in future testbeam
Stochastic: 11.5%
Constant: 7.2%
Stochastic: 6.1%
Constant: 9.2%
Noise: 6.9%

## Slide 23: Backup: Simulation of prototype

## Slide 24: Backup: simulation for various geometry

## Slide 25: Backup: fit result for PMT
beam
beam
M16
beam

## Slide 26: Backup: KEK Beam structure (2024 March)
2024 March setup using two triggers of SciFi-MPPC
Additional injection ~ms in every ~100s
  3 peaks in an additional injection
  VETO out is prepared in the control room.
    need to consider how to include veto in our DAQ and reject signal
Otherwise, rate seemed stable
1s
Unit: 109 ns = second
Unit: 109 ns = second
SciFi+MPPC trigger for Korea Alice telescope

## Slide 27: Backup: KEK Beam profile along beam axis
Beam width in sigma (gaussian fit) in beam axis direction
Z=0 is at the edge of the last quadrupole magnet.

## Slide 28: Table
Movable stool on the table
  Horizontal move: wheel counter
  Vertical move: tape ruler
  Table itself is movable
Table dimension
  Only one table: Aluminum profile should be prepared if we need more space.
  Stool size match to the Telescope
    550(x)×550(y)×700(z) mm3
A frame+stool, a desk for power supply and others.
If we need more ancillary detectors out of table, we have to consider Aluminum profile.