## Slide 1: Update on gas system and monitor
dRICH Office
January 5th, 2025
Silvia Dalla Torre and Fulvio Tessarotto

## Slide 2: Items for PID review
Radiator gas choice
Conceptual design of the gas system
Needed monitoring tools
Interferometer development
Studies of C2F6 – CO2 separation system
C2F6 fraction from sonar
Transparency in the visible
Previous review: July 2023
today
discussion

## Slide 3: Items for PID review
Studies of C2F6 – CO2 separation system

## Slide 4: Block diagram of the dRICH gas system

## Slide 5: Block diagram of the dRICH gas system
Studies for a possible separation system

## Slide 6: Separation possibilities
Phase separation by liquefying the radiator gas
 implies operating at very low temperatures
2) Phase separation by liquefying the other gas
 implies using CO2 as neutral gas instead of nitrogen
3) Separation by membrane filtering
implies developing a dedicated system
Chart: 
| -148 | -143 | -138 | -133 | -128 | -123 | -118 | -113 | -108 | -103 | -98 | -93 | -88 | -83
 | 0.0001747 | 0.00036445 | 0.00071136 | 0.0013103 | 0.0022944 | 0.003842 | 0.0061843 | 0.0096111 | 0.014475 | 0.021196 | 0.03026 | 0.042223 | 0.057704 | 0.077387
fraction of C2F6 in the vented-out gas
temperature (˚C)
Damiano Galassi (EP-DT chemical Engineer)
Is studying for us the behavior of C2F6-CO2
mixture and phase separation options:
partial condensation , crystallization, …
REMINDER

## Slide 7: Physical properties of C2F6
hexsafluoroethane
C2F6 molecular weight: 138.01 g/mol
boiling point: -78.1 °C
melting point: -100.6 °C
density: 5.734 kg/m3 at 24 °C
density: 16.08 kg/m3 at -78 °C
1 covalent bond
6 hydrogen bond
liquid
gas
Chart: Pressure (MPa) vs temperature (K)
REMINDER

## Slide 8: Physical properties of CO2
No liquid below
-56.6 ˚C

## Slide 9: An approach for vessel filling
Using CO2 as stand-by gas
  CO2 requires reasonable P, T conditions for liquefaction
Studies of CO2-C2F6 separation

## Slide 10: Separation of C2F6 from CO2
Preliminary Studies: CO2 – C2F6 Binary Mixture
Investigation performed by Damiano Galassi, chemical and process Engineer, EP-DT-FS Gas team, CERN, Nov. 2024
CO2
  Triple point -57 C and 5.2 bar
  Possible condensation point (T,P) = (-53, 6) expressed in C, bar
C2F6
  Triple point -100 C and 0.3 bar
  Possible condensation point (T,P) = (-37, 6) expressed in C, bar
Liquefaction Pressure (PL) versus temperature

## Slide 11: C2F6 - CO2 gas mixture
Experimental data from literature on Vapor-Liquid Equilibrium (VLE) versus CO2 fraction
Fraction of C2F6 in azeotropic composition
azeotropic behavior strong interaction between the two molecules

## Slide 12: C2F6 - CO2
Comparison with various models
NRTL-RK (Non-Random Two Liquids) to model liquid phase and its deviation from ideality coupled with Redlich-Kwong’s cubic equation of state to simulate the vapor phase.
PSRK (Predictive Soave Redlich-Kwong) which uses EOS (equation of state) both for the vapor and liquid phase and corrects the attractive forces by using Wong-Sandler mixing rules.
RK-ASPEN (Redlich-Kwong + Mathias-Copeman alpha function) which follows the same rules of PSRK but corrects the attraction with the MC alpha function.
PR (Peng-Robinson) which is another cubic EOS mostly suitable for hydrocarbons in extreme conditions (usually of high pressures)
Existing Models do not reproduce the data in the interesting region
-46 ˚C

## Slide 13: C2F6 - CO2
The model improved by Damiano Galassi
Allows for identification of optimal separation procedures
Improved Model obtained by fitting the parameters on the data

## Slide 14: Separation of C2F6 from CO2
10 bar
5 bar
2 bar
1 bar

## Slide 15: Separation of C2F6 from CO2
10 bar
5 bar
2 bar
1 bar

## Slide 16: Separation of C2F6 from CO2
10 bar
5 bar
2 bar
1 bar
CO2/C2F6 50/50 gas
CO2/C2F6 26/74 liquid

## Slide 17: Separation of C2F6 from CO2
10 bar
5 bar
2 bar
1 bar
CO2/C2F6 50/50 gas
CO2/C2F6 26/74 liquid
CO2/C2F6 26/74 gas
CO2/C2F6 12/88

## Slide 18: CERN setup
Elements of a setup for separation with distillation column at CERN
our sonar measurement

## Slide 19: C2F6 - CO2
The system is being prepared at CERN for a different application
Limited in maximum pressure up to 3.5 bar
Temperature down to -90 C
Could be used by us for a test of C2F6-CO2 separation:
an interesting option being explored.

## Slide 20: An approach for vessel filling
C2F6 fraction from sonar

## Slide 21: VUV Trasparency of C2F6
Exafluoroethane 5.0 at CERN
Used for a test-beam
transparency > 98%
for 170 nm < λ < 220 nm
Measured in the COMPASS setup
REMINDER

## Slide 22: C2F6 speed of sound
Thanks to this measurement we can state that we were very near to 100% C2F6
C2F6 flushed at 50 l/h for
40 minutes (~3 volumes)
Speed of sound: 139.7 m/s
our sonar measurement
Sonar in the system can be very useful

## Slide 23: Other separation options
Transparency in the visible range

## Slide 24: Strategy of measurements
In the visible range commercial devices can be used: spectrophotometers
This imposes short sample cell size, therefore pressurized gas cell
10 cm at 10 bar equivalent to 1 m long cell at 1 bar
A cell for transparency measurements of C2F6 is in preparation (designed by Ferrara)

## Slide 25: Purchase of Perkin Elmer 850+
Financed by INFN at the end of 2024
Selected: PE850+ by Perkin Elmer
PE 850+ installed in Trieste and commissioned by Perkin Elmer personnel on 30.01.25

## Slide 26: first measurement with Perkin Elmer 850+
We performed 3 consecutive measurements of a filter of OD=0.1
Great reproducibility!

## Slide 27: first measurement with Perkin Elmer 850+
Chart: 'Field2'
We performed 3 consecutive measurements of a filter of OD=0.1
Thorlabs datasheet
Superimposed (blue)

## Slide 28: Interferometer development
Bachelor thesis of Gabriele Furlani
(Trieste University), this summer