## Slide 1: TAKE FIVE for Safety- Lithium-Ion Battery Safety
September 23, 2025
Frank Craner

## Slide 3: Lithium-Ion Batteries
Because lithium-ion batteries combine a flammable electrolyte with a significant amount of stored energy, thermal runaway reactions are possible.
Thermal runaway is a chain reaction where the heat released from the failure of one cell damages nearby cells.
This can be initiated by internal short circuiting due to defects during manufacturing, mechanical damage to the battery, exposure to excessive heat or cold, and improper charging.

## Slide 4: Thermal Runaway and Fires
Thermal runaway can be identified by several indicators including: a rise in battery temperature, venting of gas, vapor, or smoke from the battery, or the presence of fire.
Fires caused by thermal runaway can produce additional chemical hazards that may include hydrogen fluoride (HF), hydrogen chloride (HCl), hydrogen cyanide (HCN), phosphoryl fluoride (POF3), carbon monoxide (CO), carbon dioxide (CO2), black carbon, and other potentially hazardous chemicals and particulates.

## Slide 5: OSHA Recommendations
Store lithium-ion batteries and devices in dry, cool locations
Follow manufacturer’s instructions for storage, use, charging, and maintenance of lithium-ion batteries
Limit the quantity of stored lithium-ion batteries
Dispose of lithium-ion batteries and devices containing these batteries, at designated recycling facilities and do not place them in municipal trash or recycling bins
Do not mix battery types (e.g. lithium-ion, alkaline, lead acid) in recycling facilities

## Slide 6: NFPA Safety Tips
• Purchase and use devices that are listed by a nationally recognized testing laboratory.
• Always follow the manufacturer’s instructions.
• Only use the battery that is designed for the device.
• Only use the charging cord that came with the device.
• Do not charge a device under your pillow, on your bed, or on a couch.
• Do not keep charging the device or device battery after it is fully charged.
• Keep batteries at room temperature when possible. Do not charge them at temperatures below 32°F (0°C) or above 105°F (40°C).
• Store batteries away from anything that can catch fire

## Slide 7: Signs of a Problem (per NFPA)
Stop using the battery if you notice these problems:
  odor,
  change in color,
  too much heat,
  change in shape,
  leaking, or
  odd noises.
If it is safe to do so, move the device away from anything that can catch fire. Call 9-1-1 (offsite) or x2222 (BNL).

## Slide 8: Recycle Batteries Responsibly
Don’t throw lithium-ion batteries in the trash or regular recycling bins because they could start a fire.
Recycle your device or battery at a safe battery recycling location.
NOTE– at BNL waste lithium-ion batteries are collected as “Universal Waste” in dedicated containers.