## Slide 1: ePIC Global Timing Unit (GTU)
The requirements
The ePIC designs
The GTU design
The current status

## Slide 2
Streaming Data
Time Frame M+5
Time Frame 1 …
Time Frame M+4
Time Frame M+3
Time Frame M+2
Time Frame M+1
Time Frame M
START
RE-START
RE-START
START
RE-START
RE-START
STOP
RE-START: STOP and START at the same Beam Crossing
Whole detector dead time
RE-START
1.1 Synchronized control
1.2 Jitter of the FEB/ASIC received clock: less than 5ps;
  1.3 For TOF detectors, the phase of the clock relative to the beam crossing center point is stable (less than 5ps);
  1.4 For dRICH detector, the phase of the clock relative to the beam crossing center point is stable (< ~100ps) for shutter implementation (zero suppression)
1. The requirements

## Slide 3
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750
2. The ePIC designs
2.1 The EIC beam crossing
 | Electron Storage Ring (ESR) | Hadron Storage Ring (HSR) (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [µs] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
        Beam crossing: 98.525 MHz or 10.150ns
        Orbit period: 12.7886 µs or 1260 Beam Crossing
Electron Beam Energy: 5 – 18 GeV
Proton Beam Energy: 41, 100 – 275 GeV
Luminosity: 1034 cm-2s-1

## Slide 4
2. The ePIC Designs
2.2 The ePIC clocks:
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
Streaming Data
Beam crossing ( * electron ion collision )
Time Slice M+5
Time Slice M-1
Time Slice M+4
Time Slice M+3
Time Slice M+2
Time Slice M+1
Time Slice M
SRO data header:
Packet number,
Data source ID,
Starting orbit count
Starting BX count
SRO data trailer:
Ending orbit count
Ending BX count
Sync/Error/buffer status
Total word count
* * * * * * * *
* * * * * * * *
* * * * * * * *
BX_Clock, 98.5 MHz
GTUDAM, 9.85 MHz
lpGBT_Clock, 39.4 MHz
Any other clocks
Nominal Time Slice: 65530 (~216) BX, ~0.6 ms, settable in GTU (Synchronization check)
All the clocks are phase aligned (fixed)
Single clock source, distributed to the whole system
GTUDAM, 19.7 MHz

## Slide 5
2. The ePIC designs
2.3 The ePIC Timing/Control distribution
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
(O)100
RDO
(O)1000
GTU (O)1
EIC
Common
Platform
Online computer
FEB
FEB
FEB
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEB:
  Detector dependent Front End / ASIC carrier boards.
System Clock: 9.85 MHz (or 19.7 MHz)
GTU distributes 9.85 (or 19.7) MHz clock, and DAM reconstructs the 98.5 MHz, (and) 39.4 MHz clock

## Slide 6
2.4: Synchronization
DAM/RDO to implement time measurement, so that RDOs can compensate the fiber length delay to within one clock period; but, it is easier to use same-length fibers.
GTU/DAM to keep a 11-bit beam crossing counter (terminates at 1260), synchronization check with streaming readout time slice (start/stop) commands; online/offline check with beam orbit structure (collision or no collision);
RDO to keep a 11-bit beam crossing counter (terminates at 1260), or a 9-bit beam crossing counter (terminate at 504 for lpGBT protocol), and a 6-bit (min. ~818 ms), 21-bit (preferred, ~26seconds), or 32-bit (over 15 hours) beam orbit counter;
GTU and DAM should keep a larger beam orbit counter;
RDO to keep a 16-bit (min), or 32-bit (preferred) time slice counter. This counter should not overflow for the maximum DAQ computer buffer.
RDO should assert buffer high_marker no later than one orbit period before it is full and starts to lose data.
RDO starts a new data packet upon receiving time-slice_start, and end the current packet upon receiving time-slice_end or upon receiving a new time-slice_start.
RDO to hold data if the DAM is busy (potential buffer full), and the DAM to hold data if the host computer/Network switch is busy.
The GTU can record dead time by sending TimeSlice_end, and holding TimeSlice_start in responding to RDO busy.
RDO should generate one packet on every readout time slice. The RDO can discard detector data to avoid buffer overflow, or out of synchronization, but this occurrence must be recorded in the data package/trailer.
GTU
RDO
DAM
DAQ
Data Buffer ‘FULL’ backpressure
Status accumulation:
Data Buffer conditions, Out of Sync, Reset_request, etc.
Run_control:
SRO_time_start/stop, RESETs, etc.
Data flow
2. The ePIC Designs

## Slide 7
3. The GTU Design
3.1 Clock distribution

## Slide 8
3. The GTU Design
3.2 Slow Control

## Slide 9
3. The GTU Design
3.3 GTU fast control

## Slide 10
3. The GTU Design
3.4 GTU partition (multiple run-control support)
Hardware: Each MGT transceiver corresponds to one DAM. It can be ‘controlled’ independently.
Each MGT is assigned an ID (corresponding to a sub-system);
Each Run_control_user_interface is also assigned an ID (corresponding to a sub-system);
* If we use BIT (instead of INTEGER) for the IDs, multiple sub-systems can be controlled by multiple User Interfaces.
RUN_CONTROL_USER_1
RUN_CONTROL_USER_2
RUN_CONTROL_USER_n
FPGA
command switch
MGT/DAM_1[1:a]
MGT/DAM_2[1:b]
MGT/DAM_m[1:c]
There is (should be) enough FPGA resources to implement a 24x24 (n=24, m=24) switch with broadcast option

## Slide 11
3. The GTU Design
3.5 the design
FPGA
Power
supplies
Clock
Receiver, control, distribution
Run Control
Memory
‘services’
GTU base board
Optic Transceiver plugin module
Clock fanout
Possible buffers
Quad optic TRX
Power
regulators
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
Quad optic TRX
16.8 inch wide (max)
4 U/7” high (max)
FPGA (SOM)
FPGA
Clock fanout
A 4U (high, 19 inch wide) rack mounted box consisting of one GTU base board (16.8 inch wide max), and many Optic transceiver plugin modules (4U high max, to DAM)

## Slide 12
4. The GTU status
262 mm
425 mm
Right now:
Schematics: 60%
PCB placement: 80%
PCB routing: 0%
This summer

## Slide 13
Up to 144
GTU
DAM
4. The GTU future

## Slide 14
4. The GTU future
lots of:
Firmware
Software

## Slide 15
Thank you

## Slide 16
2.4 The hardware design
  2.4.1 GTU
GTU required:
EIC common platform interface;
Run Control;
~150 DAM interface
Risk mitigation:
Beam vs clock phase monitoring;
Dedicated clock fanout to TOF
2. The ePIC Designs
Clock @ 9.85 MHz
GTU_CONTROL
DAM/RDO Status
Optional/extra
Between GTU and DAM
Same-length Multimode fibers: 4 Tx/4 Rx (inexpensive, standard, commercially available)
GTU
DAM

## Slide 17
2. The ePIC Designs
2.4 The hardware design
  2.4.2 DAM
DAM clock reconstruct,
98.5 MHz and 39.4 MHz,
Phase aligned with the 9.85 MHz clock,
Additive Jitter ~1ps;
Phase: fixed
The DAM will have one MTP fiber port connects to GTU, 48 ports (duplex) connect to 48 RDOs (one port each), and PCIexpress to host PC.
Run control
SYNC the run control from GTU and repack in lpGBT format at 39.4 MHz, or non-lpGBT format at 98.5 MHz
ASIC setup, and RDO/FEB monitoring

## Slide 18
2.6 The data format
2. The ePIC Designs
GTU
DAM
Clock @ 9.85 MHz
GTU_CONTROL, “(min) 8-bits (+ 1 k_bit) @ 98.5 MHz” & “480-bits @9.85 MHz”
DAM/RDO Status, “(min) 8-bits (+ 1 k_bit) @ 98.5 MHz” & “480-bits @9.85 MHz”
To fully use the DAM connection
FPGA MGT Transceivers
PCB Transmitters
PCB Receiver
FPGA_MGT Transceiver
Downlink
Uplink
FPGA IOB Transceivers
FPGA_MGT Transceiver
2.6.1 Between GTU and DAM
The 9.85 MHz clock is also used to align the DAM boards by using the same (length, type) fibers (Synchronization)
DAM
RDO
64-bit at 39.4 MHz for lpGBT, or 64-bit @ 98.5 MHz (for example) for non-lpGBT
256-bit at 39.4 MHz for lpGBT, or 64-bit @ 98.5 MHz (for example) for non-lpGBT
FPGA MGT Transceivers
lpGBT or FPGA_MGT Transceiver
Downlink
Uplink
2.6.2 Between DAM and RDO/FEB (one-pair of fibers)
DAM aligns and repacks the packet (from GTU), and sends the relevant information to the RDO at 39.4 MHz, or 98.5 MHz. The RDO receives the ‘downlink’ after a fixed (same) delay (relative to the GTU generation).

## Slide 19
2.5 The risk mitigation
3. The ePIC Designs
2.5.1 Clock phase (RDO/lpGBT recovered clock versus electron beam) monitoring:
e- Beam pickup
RDO(area) Clock
Phase#1
Phase#2
Phase#1160
Phase#1
PhaseOrbit (average)
GTU: Phase Correction
RF-SoC (?)
Optic Transceiver plugin module
Clock fanout
Optic transmitter
Power
regulators
4 U high
Optic transmitter
Optic transmitter
Optic transmitter
Optic transmitter
Optic transmitter
GTU_Optic Transmitter plugin modules
Clock only, to TOF_RDO (optional)
Possible choice of Optic Transmitters:
Samtec FireFly, 12 ch TX,
MTP_12 at GTU
LC at RDO
2.5.2 Dedicated clock from GTU to TOF_RDO

## Slide 20
2.4.1 GTU detailed design: clock ‘area’
EIC common platform interface
OSC
AD9510
Si5395
FPGA (SOM)
IN1
IN0
OUT0
IN0
Orbit
BXclock
98.5 MHz
9.85 MHz
SPI
Clock_Sync
OUT4
OUT5
Fanout
To FPGAs
I2C
OUT0
OUT1
OUT2
OUT3
OUT4
OUT9
IN3
ZDM
To plugin optic transceivers
To plugin optic transmitters
Beam Phase monitoring
Clock phase adjustment
AD5330x
AD5330x
2. The designs

## Slide 21
Used on the Jlab’s Trigger Interface (TI) modules to generate SYNCHRONIZED /2, /4, /6 and /8 lower frequency clocks.
Analog Devices AD9510
Additive output jitter (rms)
LVPECL: 225 fs
LVDS/CMOS: 275 fs
2.4.1 GTU detailed design: AD9510 synchronous clock divider (clk1 input)

## Slide 22
2.4.2 DAM (FLX155) clock interface
Dedicated Clock input,
up to three MGT lanes (Tx/Rx)
MTP multimode 850µm optical
* These two diagrams are from FLX155 presentations

## Slide 23
2.6.1 GTU  DAM communication (Downlink, example)
packet | One packet at 9.85 MHz, or 10 ( one word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(9:0) abcdeifghj- | K28.1_3C 0011111001 x0111110xx | K28.2_5C 0011110101 | K28.3_7C 0011110011 | K28.4_9C 0011110010 | K28.5_BC 0011111010 x0111110xx | K28.6_DC 0011110110 | K28.7_FC 0011111000 x0111110xx | K23.7_F7 1110101000 | K27.7_FB 1101101000 | K28.0_1C 0011110100
Bit(19:10) | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC | GTU_RC
Bit(29:20) | BX(7:0) | BX(15:8) | Obx(7:0) | Obx(15:8) | Orbit(47:0), BX(63:16), etc. |  |  |  |  | 
Bit(39:30) | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM | DAM
Bit(79:40) | USER | USER | USER | USER | USER | USER | USER | USER | USER | USER
packet | One packet at 9.85 MHz, or ten (single word at 98.5 MHz) |  |  |  |  |  |  |  |  | 
word | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Bit(9:0) abcdeifghj- | K28.1/3C 0011111001 x0111110xx | K28.2/5C 0011110101 | K28.3/7C 0011110011 | K28.4/9C 0011110010 | K28.5/BC 0011111010 x0111110xx | K28.6/DC 0011110110 | K28.7/FC 0011111000 x0111110xx | K23.7/F7 1110101000 | K27.7/FB 1101101000 | K28.0/1C 0011110100
Bit(39:10) | Status | Status | Status | Status | Status | Status | Status | Status | Status | Status
Bit(79:40) | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC | RDO/ASIC
2.6.1 DAM  GTU communication (uplink, for example)

## Slide 24
4. GTU optic Adaptor
100mm
170mm

## Slide 25
4. GTU base board
262 mm
425 mm