## Slide 1
Detector System | Channels | ASIC | FEB | RDO | Gb/s (RDO) | Gb/s (Tape) | DAM Boards | Readout Technology | Notes
Si Tracking: Inner Barrel (IB) Outer Barrel (OB) Backward Disks (EE) Forward Disks (HE) | 1.8B Pixels 5.0B Pixels 4.7B Pixels 4.7B Pixels | 160 495 462 462 | 592* 1870* 1744* 1744* | 24 55 52 52 | 2.36 3.52 4.68 4.68 | 2.36 3.52 4.68 4.68 | 1 2 2 2 | ITS-3 sensors & ITS-2 staves / w improvements | ASIC corresponds to VTRX+ counts FEB corresponds to detector fiber RDO is off detector Fiber aggregator
MPGD tracking: Electron Endcap Hadron Endcap Inner Barrel Outer Barrel | 16,384 16,384 32,768 98,304 | 256 256 512 1536 | 64 64 128 384 | 16 16 32 96 | 2.86 4.01 4.10 15.81 | 0.58 0.80 0.82 3.16 | 1 1 1 2 | uRWELL / SALSA uRWELL / SALSA MicroMegas / SALSA uRWELL / SALSA | VTRX+ based FEB
Forward Calorimeters: LFHCAL HCAL insert ECAL W/SciFi Barrel Calorimeters: HCAL ECAL SciFi/PB ECAL ASTROPIX Backward Calorimeters: NHCAL ECAL (PWO) | 63,280 8k 18,320 1,536 5,760 500M pixels 3,256 2,852 | 1130 142 28 102 58 | 1130 142 574 28 102 58 102 | 74 9 72 2 4 340 4 13 | 18.54 17.72 14.75 0.87 11.45 1.25 3.46 2.00 | 2.47 2.36 7.36 0.12 1.52 1.25 0.47 0.99 | 2 1 2 1 1 8 1 1 | SiPM / CALOROC SiPM / CALOROC SiPM / Discrete SiPM / CALOROC SiPM / CALOROC Astropix SiPM / CALOROC SiPM / Discrete | CALOROC: 56 Ch/CALOROC 16 CALOROC / RDO Discrete: 32 Ch/FEB, 8 FEB/RDO conservative (16 estimate).
Far Forward: B0: Crystal Calorimeter 4 AC-LGAD layer 2 Roman Pots 2 Off Momentum ZDC: Crystal Calorimeter HCAL | 135 688,128 524,288 294,912 900 9,216 | 672 512 288 165 | 5 168 128 72 30 165 | 1 42 32 18 4 11 | 2.3 12.75 14.53 3.53 2.30 0.22 | 2.3 2.1 2.1 0.7 4.5 .22 | 1 1 1 1 1 1 | SiPM/APD / Discrete AC-LGAD / EICROC AC-LGAD / EICROC AC-LGAD / EICROC SiPM/APD / Discrete CALOROC | 4 layer x 42 module x 4 EICROC x 1024 ch 2 stations x 2 layer x 32 module x 4 EICROC x 1024 ch 2 stations x 2 layer x 18 module x 4 EICROC x 1024 ch
Far Backward: 2 x Low Q Tagger 2 x Low Q Tagger Cal 2 x Lumi PS Calorimeter 2 x Lumi PS tracker Direct Photon Lumi Cal | 66M pixels 420 3,360 128k 100 | 3456 1000 | 288 250 24 | 24 1 1 64 24* | 37 - 19 45 200 | .3 - 7 2 7 | 10 1 1 2 1 | Timepix4 SiPM / CALOROC SiPM / Discrete AC-LGAD: FCFD or EICROCx SiPM / fADC250 | Firmware Trigger to reduce output rate Low Q Calorimeter doesn't run at high luminosity Direct Photon: commercial digitizer, no RDO
PID-TOF: Barrel Endcap | 2,359,296 3,719,168 | 18,432 3,632 | 288 212 | 288 212 | 15.95 33.92 | 4.79 7.34 | 8 6 | AC-LGAD: FCFD or EICROCx AC-LGAD: EICROC | bTOF 128 ch/ASIC, 64 ASIC/RDO eTOF 1024 pixel/ASIC, up to 28 ASIC/RDO
PID-Cherenkov: dRICH pfRICH DIRC | 317,952 69,632 73,728 | 4968 544 576 | 4968 68 144 | 1242 17 24 | 1240 24 11 | 13.5 12.5 6 | 30 1 1 | SiPM / ALCOR HRPPD / FCFD or EICROCx MCP-PMT / FCFD or EICROCx | Worse case after radiation. Includes 30% timing window. Requires further data volume reduction Firmware trigger
EPIC Detector Scale and Technology Summary:

## Slide 2
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD |  | Det Fiber Down | Det Fiber Up | RDO | Fiber Pair (DAQ) | DAM | Data Volume (RDO) (Gb/s) | Data Volume (To Tape) (Gb/s)
 | MAPS | AC-LGAD | SiPM/PMT | MPGD | HRPPD/ MCP-PMT |  |  |  |  |  |  | 
Tracking (MAPS) | 16B |  |  |  |  | 183 | 5863 | 183 | 183 | 7 | 15 | 15
Tracking (MPGD) |  |  |  | 164k |  | 640 | 2560 | 160 | 160 | 5 | 27 | 5
Calorimeters | 500M |  | 100k |  |  |  |  | 522 | 522 | 17 | 70 | 17
Far Forward |  | 1.5M | 10k |  |  |  |  | 80 | 80 | 6 | 36 | 12
Far Backward | 66M | 128k | 4k |  |  |  |  | 60 | 82 | 14 | 301 | 16
PID (TOF) |  | 6.1M |  |  |  | 500 | 1364 | 500 | 500 | 14 | 50 | 12
PID Cherenkov |  |  | 318k |  | 143k |  |  | 1283 | 1283 | 32 | 1275 | 32
TOTAL | 16.6B | 7.7M | 432k | 164k | 143k | 843 | 9,787 | 2,788 | 2,810 | 95 | 1,774 | 109
Summary of Channel Counts