## Slide 1: Electron and Hadron Polarimetry
WBS 6.10.14
10th EIC DAC Meeting
June 11-13, 2025
Frank Rathmann
Dave Gaskell
Hadron Polarimetry Electron Polarimetry
BNL
JLab

## Slide 2: Charge Questions Addressed
Is the design of the ePIC detector and its sub-systems appropriate and progressing well?
Are the remaining work and technical, cost and schedule risks adequately understood? Are there opportunities?
Will the detector be technically ready for baselining by late 2025?
Are the detector integration and planning for installation and maintenance progressing well? Are there areas where further ideas should be pursued?
Will the detector be ready for start of construction by late 2026?

## Slide 3: Requirements
Polarized Electron Beams | Polarized Hadron Beams
Highly polarized beams, | 
Fast feedback for machine setup | 
Excellent measurement of absolute polarization, | 
Non-destructive polarimetry | 
Bunch-by-bunch polarization measurement (fill pattern: ,, ) | 
Sokolov-Ternov, | Polarization decay ()
 | Transverse bunch polarization profile
Polarization vector at experiment (transverse, longitudinal) | 
Polarized Electron Beams | Polarized Hadron Beams
Fast feedback for machine setup | 
Non-destructive polarimetry | 
 | Transverse bunch polarization profile
Polarization vector at experiment (transverse, longitudinal) | 

## Slide 4: Scope
Electron and hadron bunches stored for several hours.
transverse
longitudinal
IR-4
Hadron polarimetry
HJET for absolute polarization
Fiber target for polarization lifetime and bunch profile
IR-6
C fiber target to ensure
IR-6
Local polarimetry
Inside spin rotators
Fiber target for hadron polarization orientation
Compton backscattering for electron polarization (ESR)
RCS
Compton backscattering for electron polarization

## Slide 5
Electron Polarimeters

## Slide 6
Compton Polarimetry
Analyzing powers
Longitudinal analyzing power depends only on backscattered photon energy
Transverse analyzing power depends on backscattered photon energy and azimuthal angle relative to polarization direction
Key systems:
Laser
Photon and electron detectors
Dipole
Generic Compton Polarimeter
ESR Compton will measure both PL and PT
RCS Compton will measure primarily PT

## Slide 7: Electron Storage Ring Polarimeter
Polarimeter Components:
RF-pulsed laser system (under development)
Position sensitive detectors (diamond strips) for scattered electrons and backscattered photons
Calorimeter for backscattered photons
Will operate in single-photon mode
Beam energy | PL | PT
5 GeV | 99.1% | 13.2%
10 GeV | 96.5% | 26.2%
18 GeV | 89.0% | 45.6%
Polarization components at Laser IP
Crab cavity
Photon Detector
(30 m from Laser IP)
*
D4EF
qB=1.5 mr
Q9EF
D5EF
qB=1.5 mr
D6EF
qB=12 mr
Q10EF
Q8EF
Q7EF
Q6EF
Q5EF
Q4EF
Q3EF
D3EF
qB=13 mr
D2EF
Electron Detector
Laser IP​
74 m upstream of IP-6

## Slide 8
ESR Compton Laser System Requirements
Laser power constraint: sufficient power to provide ~ 1 backscattered photon/bunch-laser crossing
Want to make “single photon” measurements – not integrating
532 nm laser with ~5 W average power at same frequency as EIC electron bunches sufficient
Resulting measurement times as noted above – easily meets beam lifetime constraints  less than 2 minutes
Time estimates from Ciprian Gal
Configuration | Beam energy | Time (minutes)
PL | 18 | 0.1
PT |  | 0.8
PL | 10 | 0.2
PT |  | 1.4
PL | 5 | 0.5
PT |  | 1.8
Time needed for 1% (statistics) measurement
Estimates assume ”differential” measurement, 100% efficiency

## Slide 9: ESR Compton: Laser System
Laser system based on similar system used in JLab injector and LERF
Gain-switched diode seed laser 10 ps pulses @ 1064 nm
  Variable frequency allows optimal use at different bunch frequencies (100 MHz vs 25 MHz)
Fiber amplifier → average power 10-20 W
Optional: Frequency doubling system (LBO or PPLN)
Partially reflective exit window to monitor reflected laser polarization
Gain-switched seed laser components procured under earlier generic EIC R&D
Shukui Zhang (JLab) assisting with seed laser configuration and system testing
Fiber amplifier obtained - work underway in Compton polarimetry laser lab at JLab

## Slide 10: ESR Compton: Position Detectors
Position sensitive detectors are needed to measure:
  Scattered electrons → PL
  Backscattered photons → PT
Technology choice: diamond strips
  Radiation hard, good time response
  No performance degradation after 10 MRad of exposure (Q-weak @ JLAB)
Detector size: 6 cm (electrons) / 5 cm (photons)
Required segmentation: 250 mm (electrons) / 100-200 mm (photons)
Custom ASIC readout required
  New “FLAT32” chip based on “CALYPSO” (used at LHC) under development for JLab/MOLLER (just completed)
  Meets timing requirements of EIC (10 ns)
  Can also be used for pulse height, pulse integration readout
    Some minor modifications needed
JLab Hall C diamond detector
10 ns

## Slide 11: ESR Compton Photon Calorimeter
Will use a Forward EMCAL module for photon calorimeter
  Block of W/SciFi, subdivided into 4 towers
  2 cm light guide from block to PMT
  Expected resolution:
Only modest resolution required since calorimeter will be used in threshold-less integrating mode for longitudinal polarization measurements

## Slide 12: ESR Beamline Design
Current beamline design with RCS removed
 2 weak & 2 strong dipoles  mitigates synchrotron radiation (see backup)  only need collimator plus W shield
Electron detector outside vacuum pipe  RF shield used to mitigate beam impedance issues
Photon
detector
IP6
Weak dipoles
qB=1.5 mr
Laser IP
Electron
detector
Crab Cavity
Bijan Bhandari 09.12.2024

## Slide 13: Rapid Cycling Synchrotron Polarimeter
RCS properties
RCS accelerates electron bunches from 3 GeV to full beam energy (5-18 GeV)
Bunch repetition rate: 1-2 Hz
Bunch charge: up to 28 nA
Ramping time: 100 ms
Polarimetry challenges
Analyzing power depends on beam energy
Low average current
Bunch lifetime is short
Compton polarimeter will also be used in the RCS
Average over several bunches – can tag accelerating bunches to get information on bunches at fixed energy
Requires measurement in multiphoton mode (many backscattered photons/electron bunch)
Will use same detector technologies as ESR Compton
RCS
Proposed polarimeter location

## Slide 14: RCS Compton Detector Simulations
RCS Compton polarimeter will operate in multi-photon mode
Each laser-electron bunch collision will result in thousands of backscattered photons
Polarization will be extracted by measuring the energy-asymmetry  total energy deposited in the detector for each laser helicity state
Diamond strips (0.1 mm pitch)
Tungsten converter
Calorimeter (5 cm x 5 cm)
Energy deposited in each strip of diamond detector
Energy asymmetry
18 GeV
Simulated 10 laser pulses  10,000 backscattered photons per pules

## Slide 15
Details for polarimeter and beamline integration
  Both laser system and photon/electron detector exit ports need careful integration
  Impedance issues must be included in design
  Integrate polarimeter layout details in machine model
Complete DAQ design
  Specify modules
  Determine readout mode (streaming vs. triggered)
Tasks for CD-2 readiness: Electron polarimeters
Will have 2nd Preliminary Design Review at the end of 2025

## Slide 16
Hadron Polarimeters

## Slide 17
Hadron Polarimetry: CNI region
Spin-dependent cross section
unpolarized cross section
vertical component of beam polarization
Analyzing power, polarization sensitivity ot scattering process
      , where e.g.,
At AGS, RHIC, EIC energies, no processes available with known to sufficient accuracy for
Interference of EM & strong interaction (CNI) at small angles sizeable for and scattering
in CNI region N. Buttimore, PoS PSTP2013, 057 (2013)

## Slide 18: Hadron Polarimetry at EIC
HJET polarimeter (absolute, slow)
per 4 hours
pC polarimeters (fast, relative)
per scan
+ polarization profile
ABS
BRP

## Slide 19
Polarimetry at EIC: Timing
 |  | EIC |  | 
ring | RHIC | HSR | HSR | ESR
species | proton | proton | proton | electron
mode | flattop | injection | flattop | flattop
Energy [GeV)] | 250 | 23.5 | 275 | 10
Number of bunches | 120 | 290 | 1160 | 1160
Bunch length [cm] | 55 | 24 | 6 | 0.7
Bunch frequency [MHz] | 9.38 | 22.65 | 90.68 | 90.68
Bunch spacing [ns] | 106.6 | 44.14 | 11.02 | 11.02
Hadron polarization measurements foreseen at:
  Injector chain Beam polarizations measured at 200 MeV linac and AGS
  HSR absolute polarization measurements at:
    injection (½ h electron cooling period)
    Flattop through store
Routine operation of pC and HJET

## Slide 20: HJET at EIC: bunch field depolarization
ok
RHIC | EIC
RHIC | EIC
Bunch repetition frequency increased by factor of 10
  enhanced bunch-induced depolarization at EIC
No operation like that at EIC
Depolarization analysis for HJET show that we need to to avoid low harmonic numbers

## Slide 21
HJET at EIC: mitigation
Operate
HJET here
Avoid bunch-induced depolarization by HJET operation at

## Slide 22
Design holding field system (in progress)
Design new target chamber to accommodate holding field (in progress)
Upgrade BRP with mass analyzer (in progress)
  improve e.g., H2 background determination
Upgrade detector system (in progress)
  obtain
  cope with EIC bunch frequency
Upgrade HJET slow control system, ensure compatibility with EPICS database
Impedance calculation for HJET addressed when concepts for 2. and 3. available
Aim of proposed changes: improve systematics to get to
  Next: In early 2026: HJET move to 510 for refurbishment/upgrade work: items 2. to 5.
HJET at EIC: planned modifications

## Slide 23: C fiber target polarimeter: present system
Ultra-thin ribbon targets:
target holder inside beam pipe
For RHIC: target length

## Slide 24: C fiber target polarimeter: upgrades for EIC
EIC conditions with 10 ns bunch repetition and higher current require:
  Estimate C target temperatures
  Effects of increased wake field power in target chamber and target holders
  Develop vacuum transfer chamber
    One target at a time in chamber
    improve target conditioning & installation
  Upgrade detectors and readout systems
    cope with timing requirements
  For EIC, due to larger beam size in IP4, targets need to be long
pC target chambers will be moved to 510 for refurbishment and upgrades in early 2026

## Slide 25
Target heating (code by Peter Thieberger)
With realistic beam sizes, target heating about same at RHIC and EIC
changed ID #128 in Risk Registry to low
Independent modeling approach of C target heating by proton beams (in progress)
C fiber target polarimeter: target heating

## Slide 26
Shorter bunch spacing at EIC
  Fiber target chambers ok for single-bunches
  Higher order modes → pumping ports → RF shielding
C fiber target polarimeter: impedance calculations I
C target chambers (steel 316L) will work for EIC
Simulations of C target holders
  Studies involved target holders made from Al, SS and dielectric (e.g., Al2O3)
  Preliminary results favor dielectric target holder over metallic ones
  gold layer to avoid charging up of target
  Operation: one target in chamber at a time
    design vacuum transfer chamber
  No adverse effect from shifted targets positions
Fresh results from Medani Sangroula (CAD)
Wake field potential
Wake impedance
Improved performance of machine when dielectric target holder will be used

## Slide 27
C fiber target polarimeter: impedance calculations II
Shifted dielectric target positions:
Like RHIC, EIC will use multiple targets on same target holders
Wake field potential
Wakefield amplitude decrease with target holder shifted down
Similar behavior when different C targets are inserted into beam from same target holder

## Slide 28: New development: 3He atomic beam
High flux device with beam at 1 K
ideal for absolute 3He++ polarimetry at EIC
Provide absolute polarization measurement for beams
MIT development for nEDM exp’t at Oakridge (discontinued) (P. T MohanMurthy, J. Kelsey, J. Dodge, R. Redwine, R. Milner, P. Binns, B. O’Rourke)
3He beam polarimetry will be needed a few years after initial EIC commissioning

## Slide 29: Hadron polarimetry overview: Layout at IP4
Choice of location driven by required drift space
Carbon and polarized H and 3He targets all located in one place
  minimize spin rotations between polarimeters
  Enables efficient use of common infrastructure
CNI
Triplet (Q3)
3He Jet
HJet
2X Warm D0
Longit SC Pickup
4X Horiz SC Kicker
4X Vert SC Kicker
HJet Tagger Drift /
Tagging System
Q4
Ion Pump
HSR
E. Link
5/16/2025
7.5 m

## Slide 30
Polarimeter Schedule
Final RHIC operations
Final Design Review
Final commissioning
Polarimeters ready for beam development (L2_0600 Construction of Components Complete)
Construction
Installation
2nd PDR

## Slide 31: Polarimeter systematics: previous experiments
Hadron polarimeters
Transverse:
Systematic error for RHIC proton beam polarization () in run 17
  SSA:, DSA:
Longitudinal
is at present not directly accessible at RHIC
Electron polarimetry: systematic uncertainties from previous Compton polarimeters
Longitudinal:
LPOL @ HERA (collider): Photon detector in multi-photon mode
Q-Weak in Hall C @ JLab (fixed target): Electron detector, counting mode
CREX in Hall A @ JLab (fixed target): Photon detector, integrating mode
Transverse:
TPOL @ HERA (collider): Photon detector in counting mode
EIC Compton polarimeter designs make use of lessons learned from these devices
Goal of not needed on day 1
Systematics of absolute polarimetry during first years of operation will benefit from upgrades (slides 22 & 24)

## Slide 32
Hadron polarimeters
  Accelerator integration of hadron polarimetry available
  HJET modifications
    to be integrated: target chamber with holding field, QMA for BRP, detector system
  Present RHIC pC polarimeter system applicable at EIC
    Temperature estimates of C ribbon targets with updated EIC beam sizes at IP4, targets will hold
      corresponding estimates for targets at IP6 to be done
    Wakefield calculations indicate use of dielectric target holders
    Redesign of existing chamber to accommodate vacuum loading system for targets
  New 3He atomic beam target development is in progress and aligned with EIC ramp up & commissioning
  Readout/detector choice for C, HJET, and 3He polarimeter required
Will have 2nd Preliminary Design Review at the end of 2025
Tasks for CD-2 readiness: hadron polarimeters

## Slide 33
Summary
Basic polarimetry methods and detector technologies established
Design progressing towards CD-2 in FY26 and CD-3 in FY27
Demands at EIC significantly higher than at previous facilities
  designs in place to meet demands
Future modifications beyond EIC baseline not precluded with current designs
All polarimeters shall be ready for operation at start of polarized beam commissioning
  Primary purpose of RCS polarimeter is beam development
  All other polarimeters will be used for beam development in addition to later monitoring

## Slide 34
Backup

## Slide 35: Scope Definition

## Slide 36: ESH and QA
Electron polarimeters:
ESH: Compton polarimeter laser safety systems will use common approach with other EIC laser systems (i.e., detector gain monitoring , etc.)
  Requirements:
  Interlocked laser room outside accelerator tunnel
  Interlocked laser enclosures where laser interacts with electron beam
  Needs have been identified in dependency review
  QA: Compton laser and detector components will be tested at JLab before installation at EIC
  Laser  seed laser, amplifiers, fiber, reflective window
  Diamond detectors  tests of detectors and FLAT32 with cosmics and radioactive sources
  Photon calorimeters  tests with cosmics and sources. Tests in JLab polarimeters possible depending on beam schedule
Hadron polarimeters:
After 20 years of operating experience with pC and HJET polarimeters at RHIC, ESH and QA related issues have been ironed out.

## Slide 37: Polarimetry design: status review
Committee:
Dipangkar Dutta (Mississippi State University)
Jenny List (DESY)
Paolo Lenisa (Ferrara University)
Frank Rathmann (FZ Jülich)
Review: January 17-18, 2023
Summary of Recommendations
Electron Polarimetry
Develop alternative detector concept based on silicon
Detailed simulations including all backgrounds and shielding
Explore transverse polarization measurements using synchrotron radiation
More detailed detector requirements for RCS polarimeter
Hadron Polarimetry
Target gas analyzer should be used to determine molecular fraction in the HJet
Explore using thinner Si detectors in both HJet and pC polarimeters to veto punch through events
In addition to exploring new target materials for pC polarimeter, explore larger beam size
Obtain beam time with AGS pC polarimeter to test detectors
Theoretical assessment of in 3He-3He elastic
Further 3He studies during remaining RHIC runs
Closed
On-going/scheduled

## Slide 38
additional material
Electron polarimeter

## Slide 39: Synchrotron Backgrounds in ESR Compton
Synchrotron radiation from strong dipoles (D6EF, D3EF) too large – thick shield needed for photon detector
 Weak dipoles with small bend will re-direct synchrotron flux from strong dipoles to be outside photon detector acceptance
Strong dipoles
Weak dipoles
Simulations by Zhengqiao Zhang (Synrad+ and Geant4)
18 GeV

## Slide 40: ESR Beamline Design
New beamline design with 2 weak and 2 strong dipoles mitigates synchrotron radiation  only need collimator plus W shield
Crab cavity
*
qB=1.5 mr
qB=1.5 mr
Laser IP​
Electron detector outside vacuum pipe  RF shield used to mitigate beam impedance issues
Weak dipoles
Photon detector
Electron detector

## Slide 41: Electron Detector Size and Segmentation
Asymmetry at electron detector @18 GeV
Beam position
Electron detector (horizontal) size determined by spectrum at 18 GeV (spectrum has largest horizontal spread)
  Need to capture zero-crossing to endpoint  detector should cover at least 60 mm
Segmentation dictated by spectrum at 5 GeV (smallest spread)
  Scales ~ energy  17 mm
  Need at least 30 bins, so a strip pitch of about 550 mm would be sufficient
At 18 GeV, zero-crossing about 3 cm from beam
  5 GeV  8-10 mm – this might be challenging
Ciprian Gal

## Slide 42: RCS Compton Rates Rate and measurement time estimates
Ebeam | Aavg | Tavg | Aenergy | Tenergy | Adiff | Tdiff
5 | 4.51% | 243 s | 5.78% | 148 s | 5.48% | 164 s
10 | 7.79% | 92 s | 10.15% | 54 s | 9.56% | 61 s
18 | 11.29% | 51 s | 14.91% | 29 s | 13.96% | 33 s
Average analyzing power:
 Average value of asymmetry over acceptance
Energy-weighted:
Differential:
 Energy deposited in detector for each helicity state
 Measurement of asymmetry bin-by-bin vs. energy, etc.
Assuming 80% polarization, <Plaser>= 6mW, 300 mm beam spot size…,  time for 1% measurement

## Slide 43
additional material
Hadron polarimeters

## Slide 44: Polarized Atomic Hydrogen Jet Target
Set of eight strip detectors
12 vertical strips
  pitch
  thick
Dissociator
beam
Detectors
Holding field

## Slide 45: Coulomb-Nuclear interference I

## Slide 46
Coulomb-Nuclear interference II

## Slide 47
Hadron Polarimetry R&D
break-up
  Tagging with hadron calorimeters
  ZDC’s installed downstream of HJET (behind DX)
  Operational in RHIC Run 23 (𝐴𝑢+𝐴𝑢)
  Neutron peak calibration needed
target
(Part of WBS 6.02.03 Accelerator R&D)
During RHIC Run 24
  beam from EBIS source ready
  Successful APEX 100 GeV in July/August 2024
Deflection angle
Installation at IP12
3 modules between beam pipes
  nA, nB, nC
1 module outside beam pipes
  pC
All modules operational
DX

## Slide 48: Simulation of 3He-3He tagger in IP4
Two warm dipoles behind polarimeter targets
Drift region includes stochastic kicker tanks
40 m
DMP jet model to simulate fixed target collisions
Four types of events:
  All 3He break up
  Breakup of 3He target
  Breakup of 3He beam
  All 3He stay intact
Tag events where 3He beam breaks up, as detectors identify 3He recoil
1
2
3
4
Simulations by Zhengqiao Zhang

## Slide 49: Hadron Polarimeter R&D
Second detector layer installed in pC polarimeter
  Included in DAQ since start of Run22 operations
  Data from RHIC Run 22
TOF vs. in layer 1 (F)
with a match in second layer (R)
Hybrid simulation
  PYTHIA & GEANT
  Repeated with 10 ns bunch spacing
Proton time-of-flight
Veto punch through particles
(Part of WBS 6.02.03 Accelerator R&D)