## Slide 1: Overview AC-LGAD Time-of-Flight
Satoshi YANO
(Hiroshima University)
The 10th Detector Advisory Committee Review
June 11th – 13th, 2025

## Slide 2: Recap of AC-LGAD TOF
The ePIC AC-LGAD TOF system is used for particle identification (PID), tracking, and background rejection in both mid-rapidity (BTOF) and forward-rapidity (FTOF) regions.
A position resolution of O(10s ps) and a timing resolution of O(10s um) for PID and tracking within a space of less than 10 cm in thickness are required
Barrel-TOF (BTOF)
0.64 m
~2.8 m
-1.33<η<1.74
1.84<η<3.61
Forward-TOF (FTOF)
60 cm
10.5 cm

## Slide 3: Impact on the ePIC PID performance
Focus of TOF is below p = 1 GeV/c
Particle-Identification at low momentum region is the primary task
Used in conjunction with Cherenkov light detectors to eliminate PID gaps and to cross-calibrate each other in overlapping regions
hpDIRC
BTOF
K/p 3σ
dRICH
FTOF
π/K 3σ
hpDIRC
BTOF
dRICH
FTOF
Decay products from D-meson in ep DIS @ √s = 141 GeV
Assuming
BTOF σtot = 35 ps
FTOF σtot = 25 ps

## Slide 4: Technology Choice: AC-LGAD
Low Gain Avalanche Detector (LGAD) is a silicon detector with a thin gain layer making high electric field
  High field increases the signal rise time and improves time resolution
  Individual layer is implemented under each electrode, so inactive is not negligible and granularity limitation is there
AC-LGAD uses AC-coupled readout with one large gain layer
  Inactive area is eliminated by one large gain layer
  Position resolution is improved by using the charge sharing
K. Nakamura et al., JPS Conf. Proc. 34, 010016 (2021)

## Slide 5: AC-LGAD Sensor Design for TOF
Strip-type sensor for BTOF
  32x20 mm2 (full-size) and 32x10 mm2 (half) size with 0.05x10 mm2 pad
  The readout geometry is 64x2=128 ch for full-size, 64x1=64 ch for half-size
  Prototype best score: σtime ~ 35 ps and σpos < 20 μm
Pixel-type sensor for FTOF
  16x16 mm2 size with 0.05x0.05 mm2 pad
  The readout geometry is 32x32=1024 ch
  Prototype best score: σtime ~ 20 ps and σpos ~ 20 μm
Strip-type for BTOF
  # Full-size: ~13.8k
  # Half-size: ~4.6k
  ~12 m2
  ~2.4 M channels
Pixel-type for FTOF
  # Sensor: ~3.6k
  ~1.1 m2
  ~3.6 M channels
2 rows
64 cols
32 rows
32 cols

## Slide 6: Sensor Timing Resolution on the entire PID performance
hpDIRC limit for K/p sep.
hpDIRC limit for π/K sep.
Δp ~ 0.5 GeV/c
Even in the worst case scenario, with current sensor performance (σsensor~35 ps), there is an overlap area with hpDIRC → Already no PID hole
σsensor< 90 ps meets the requirement of having overlap region with hpDIRC in the worst case
Δp ~ 0.45 GeV/c
Current best performance
σsensor ~ 35 ps
PID overlapping with hpDIRC for cross calibration
 More robust PID
Lost overlap

## Slide 7: Important Points in Development
Performance of Large AC-LGAD Sensors
  First application using AC-LGAD for HEP
  Identify the elements necessary for stable operation by thoroughly understand the characteristics
Mechanical and electrical design on a low material budget
  Over 2.7 m length but within a few percent of material budget (for BTOF)
  Accurate transmission of signal strength and timing information on a low material budget in a long distance
  Thermal control due to AC-LGAD's high sensitivity to temperature gradients
BTOF → Simone Mazza (UCSC)
FTOF → Mathieu Benoit (ORNL)
Detail will be introduced by