## Slide 1
Team: ANNL, Baruch, BNL, GSU, ISU, ORNL , UNH
The Barrel Hadronic Calorimeter - BHCal
DSLs: S. Bathe (Baruch) & M. Sarsour (GSU)

## Slide 2
The Barrel Hadronic Calorimeter - BHCal
Why HCal at midrapidity in ePIC:
  Account for contributions from neutral particles for precise jet energy reconstruction
  Charged-current DIS
  Hadronic final state and identification
  Solenoid flux return

## Slide 3
BHCal Requirements
The Yellow Report indicates that will be adequate.
sPHENIX Outer Hadronic Cal. (OHCAL) with
  Tilted-plate: alternating steel & scintillating tile (+ WLS fibers)
    coverage.
    32 sectors – 6 m long, 16 tons each
    48 towers/sector @ 5 tiles/tower (1)
ePIC will refurbish sPHENIX OHCal, but read out each tile ()
Half-sector

## Slide 4
BHCal implemented in DD4hep simulation of ePIC
    Resolution&Linearity from ePIC simulation vs. sPHENIX test beam data (IEEE Transactions on Nuc. Sci., Vol. 65, 2901 – 2919 (2018))
BHCal in ePIC Simulation Framework
The simulation results are done with towers.
Ongoing: include CAD geom. through GDML files + per-tile simulations (clustering, ... etc).
By Derek Anderson (ISU)

## Slide 5
Refurbishing sPHENIX Barrel HCal
Parts to be reused
  Steel sectors
  Scintillating tiles
    Have few spares (of order 8 per shape)
  fiber system to distribute LED light
    intended to be reused
    LED system is being developed

## Slide 6
New parts
SiPMs
Read-out boards
Coax cables to read-out board
Bias & LV supplies
LED monitoring system
Labor
sPHENIX outer HCal assembly was 5-person-year effort, e.g. if done in a year, it needs 5 people working each day
Setting up the factory takes time:
    Space lay-out
    Set up of test racks
    Establishing testing procedures
In sPHENIX, started this two years early
Refurbishing sPHENIX Barrel HCal

## Slide 7
Have as many sectors set up for assembly simultaneously as possible
  doubling the space used for sPHENIX in 912
Do most of the labor with students and postdocs
  Some 50 people worked in the sPHENIX HCal factory
Dedicated technician support essential (electrical/mechanical work)
Heavy need for rigging
Lessons Learned

## Slide 8
Beam Test
Plan
  Refurbish sPHENIX old prototype steel
  80 spare tiles
  120 new ePIC SiPMs
  H2GCROCv3 board from Norbert Novitzky (ORNL)
Desired to characterize all components and calibrate simulations

## Slide 9
What do we have?
  Test-stand in the HCal Lab at BNL (5 OHCal tiles read individually with H2GCROCv3 board with RCDAQ.)
  Similar test stands are planned at UNH and GSU to gain hands-on experience with the readout system and DAQ.
Where?
FermiLab (pending schedule)
CERN
Beam Test

## Slide 10
Summary
Reuse sPHENIX BHCAL
  Generally satisfies Yellow-Report energy resolution requirements and plan to read single tiles to improve constat term
  Performance already measured in a test beam as well as in sPHENIX
Plan for BHCal test beam
  Reading single tiles with the new H2GCROC based electronics chain
  Have all components and plan to put it together over the summer
It is critical to have time to refurbish the Barrel HCal for the reuse at ePIC. The refurbishment is estimated to take 1.5 years with one team redoing the work done constructing the HCal.

## Slide 11
Backup Slides

## Slide 12
Charge Questions Addressed

## Slide 13: Prior Test Beam Results
Detailed studies of performance and comparison with simulations done in test beam (T-1044).
Performance of full device will be measured in sPHENIX. We should achieve a reduced constant term due to tighter control on the scintillator variation in a tower for production sectors.
Data vs. Monte-Carlo comparison

## Slide 14
Initial studies: Log Likelihood Difference Using Barrel HCal E/p and Shower Radius