## Slide 1: Beamline Design and Integration
10th EIC DAC Review
June 11th – 13th, 2025
Charles Hetzel
EIC Vacuum Group Leader

## Slide 2: Outline
Interaction Region Vacuum Overview
Design Status and Progress
  Central Detector Chamber
  Forward Side
  Rear Side
Next Steps
Summary

## Slide 3: IR Vacuum overview
Complicated integrations between detectors and magnets
Very different requirements between rings
  Electron cloud in HSR
  Synchrotron radiation in ESR
Zero-degree calorimeter
B0 magnet spectrometer
Roman pot and off momentum detectors
Low Q2 taggers
Luminosity system
Central detector
REAR SIDE
FORWARD SIDE
CENTRAL DETECTOR

## Slide 4: Requirements and Challenges
Cryostats will be assembled in the tunnel
Low dynamic pressure required to minimize beam-gas interactions (< 1 x10-9 mbar)
Electron forward side
  Large beam sizes due to strong focusing (βx > 900m)
  Synchrotron radiation from upstream dipoles (26mrad bend 30m away -> 38 kW)
Electron rear side
  Synchrotron radiation
Hadron forward side
  Large aperture required to transport off-momentum and neutral particles
  Chamber integration, alignment and support system
Hadron rear side
  Injection and ramping optics
4

## Slide 5: Central Detector Chamber Updates
Improved electron beam pipe
  Diameter steps down with stay clear envelope
  Collimates scattered photons from upstream
Better integration with detector
  Optimized flange locations
  Removed flange before DRICH
Integration of BPMs
Gate valve solution for both sides of detector
B0 cone
Hadron stay clear
(Collision optics)
Beryllium section
Hadron stay clear
(Includes injection, neutral and +/-1.3 GeV )
Electron stay clear
(13.5σx 22.5 σy)
Electron stay clear
(13.5σx 22.5 σy)
Hadron stay clear
(Injection optics)
Electron beam pipe
Luminosity cone

## Slide 6: Central Detector Chamber - Rear Side
Beam pipes rigidly connected
Electrons
Hadrons
Gate valves
RF shielded bellows
(not shown)
BPMs
(2 sets)
Rear cryostat
Hadrons
Electrons

## Slide 7: Central Detector Chamber – Forward Side
RF taper
Vacuum window
Pump port
Electrons
Hadrons
RF bellows (not shown)
GV (electrons)
BPMs
Anchor to B0

## Slide 8: Modified Lattice Improvements
Chart: Core Sigma
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
SD=1, Intensity =1 | 1 | 0.31731 | 0.0455 | 0.0026998 | 6.3342e-05 | 5.733e-07 | 1.9732e-09 | 2.5596e-12 | 1.2442e-15 | 2.2572e-19 | 1.524e-23 | 3.8213e-28 | 3.553e-33 | 1.2234e-38 | 1.5587e-44 | 7.3419e-51
SD=3.24, Intensity = 0.1 | 0.1 | 0.031731 | 0.00455 | 0.00026998 | 6.3342e-06 | 5.733e-08 | 1.9732e-10 | 2.5596e-13 | 1.2442e-16 | 2.2572e-20 | 1.524e-24 | 3.8213e-29 | 3.553e-34 | 1.2234e-39 | 1.5587e-45 | 7.3419e-52
D3eF
(3.8 m, 19.56 mrad)
D2eF
(2.726 m, 5.14 mrad)
D1eF
(.891 m, 1.5 mrad)
Start of cryostat
Before cryostat: 34.41 kW
(~91% of total power)
Drift 5: 1141 W
(~3% of total power)
Drift 4: 413 W
(~1% of total power)
Drift 3 + Q1eF: 418 W
(~1% of total power)
Taper Q1eF->Q0eF: 874 W
(~3% of total power)
Q0eF: 58 W
Exit rear cryostat: 274 W
Exit rear central detector chamber: 274 W
Entrance of Be section: 274 W
Major reduction of heat load inside cryostat (2.9kW vs 7.2kW)
1mm tungsten shielding required instead of 3mm
High heat load beam screen required
Constant aperture through rear side
Simulation assumes 10% of charge in tails

## Slide 9: B0 Vacuum Chambers
Actuator outside cryostat
(Port for hot N2 injection)
Hadron ring GV
Valve body: DN100
Aperture: 72.78mm
Extended actuator
Extra ports on valve body
Electron ring GV
Valve body: DN40
Aperture: 52mm (DN50 CF flange)
Extra ports on valve body
Anchor to B0

## Slide 10: B0 Vacuum Chambers
Warm/Cold border Electrons
Warm/Cold border Hadrons
Off momentum stay clear
Actively cooled electron beam pipe
Electron stay clear
Room temperature hadron beam pipe
RF shielded bellows
(not shown)

## Slide 11: B0 Hadron Vacuum Chamber
Insulating vacuum wall of B0 cryostat
Stepped beam pipe due to stay clear envelope
Exit window
Electrons
Requires copper platting and aC coating
Integral part of B0 magnet
BPMs for both beam lines on single part
  Weld-in to minimize footprint
Compliance between cryostat
Weld after installation
Hole in cryostat wall

## Slide 12: B0 Electron Vacuum Chamber
Liquid helium exit
Outer cooling jacket
Requires copper platting
Integral part of B0 magnet
Final welding after installed in cold mass
Liquid helium inlet
Thinned wall section
Welded on after chamber inserted
Welded on after chamber inserted
Compliance bellows
Coolant passage
Welded to magnet structure
Coolant passage

## Slide 13: Electron Beam Screen
Very high heat load in first section and taper (375 W/m)
Added complication due to shielding
  May be easier to increase beam screen wall thickness
Need to take advantage of 2K cryopumping from cold bore
  Beam screen <80K
C. Garion
CERN (HiLumi)
M. Morrone
CERN (FCC-hh)

## Slide 14: Rear Cryostat Assembly
Hadrons
Electrons
Q1ApR
Q1BpR
Q2pR
Q1eR
Q2eR
Drift
Hadron stay clear based on points provided
  10 σx and 10 σy high divergence (no orbit offsets)
  Gold injection at 2.5 micron normalized, 8/7 sigma (x/y), 10m horizontal 0.9m vertical betas
  Points provide at beginning, middle and end of each lattice magnet element plus every 10cm through the detector
Electron stay clear based on 18 GeV collision optics
  Envelope for other energies are smaller (V6.3.1)
  Stay clear includes 13.5 σx and 22.5 σy only (no orbit offsets)
RF bellows required between each cold mass (both beam lines)
BPM required in each interconnect

## Slide 15
Chamber Concept
Liquid He interface
(no UHV – He interface)
Split ring installed after magnet installation
Small diameter weld cuff
(slightly larger than flange insert)
Standard tubing
Intermediate spacers not shown
Weld seam
Taper
Large diameter weld cuff
NON-IP SIDE
Part of chamber
Split flange ring
IP SIDE

## Slide 16: Rear Interconnects
Non-IP Side of RC-1
IP side of RC-1
Standard tubing sizes
  Hadrons : 2” x .065” wall
  Electrons: 3.5” x .12” wall
Chambers complete before installation
  Slid in from non-IP side
  Welding cuffs to protect plating/coatings
Intermediate spacers to keep tube centered
Taper transitions at ends
  Sperate weld on piece
  Weld joint protected by cuffs
Bellows welded to IP side

## Slide 17: Next Steps
Finalize and document apertures through final focusing magnets
  Beam stay clear envelopes defined
  Record of decision in draft
Central detector chamber
  Water cooling to mitigate synchrotron radiation
  Chamber integration, alignment and support system
  Finalize in situ bake out system
Beam screen design for forward electron side
  High heat load, radiation shielding required
  Optimize to maximize cryo-pumping from cold bore (decrease beam-gas events)
Update pressure profile through IR area
Geometry for rear side electron vacuum chambers
  Luminosity exit window, low Q2 taggers
Advance mechanical design of far forward side vacuum system

## Slide 18: Summary
Integration of detector systems with the accelerator components progressing
  Geometry shared as it is being developed
Experimental requirements are key drivers in designs
Compromises are negotiated when needed
Active discussions between stake holders to resolve remaining challenges
  Experimental program, magnet division, accelerator physics, technical systems, etc.