## Slide 1
Far-Forward / Far-Backward
Detector Integration
Jonathan Smith (JLAB), Ron Lassiter (JLAB),
and India Krehbiel (JLab), David Powell (JLAB)
February 18th, 2025

## Slide 2: Primary Updates Outline
Far-Backward Region
  Lumi Detector
  Low Q² Tagger
Far-Forward Region
  B0 Detector
  Roman Pots
  ZDC

## Slide 3: Lumi Detector Stand
Old
New
Previous table design was a ‘stand-in’
New design requirements dictated the front detectors move independently 5cm in Z-Axis
Top and bottom shelves of calorimeters/detectors need 10cm of movement in Y-Axis

## Slide 4: Lumi Detector Stand
SIDE
5cm
Must remain clear in way of detectors
10cm in -Y
10cm in +Y
FRONT
5cm

## Slide 5: Low Q2 Tagger Stand
Latest design as of Fall 2024
No design update requirements at this time

## Slide 6: Low Q2 Tagger Stand
Latest beampipe update in Far-Backward may result in design. Yulia is investigating

## Slide 7: B0 Detector Layout
The B0 Detector Layout has undergone numerous changes since 2023.
Latest version is using Forward TOF detectors
Currently looking to replace TOF Detectors with Stave Detectors

## Slide 8
B0 Detector Removal/Install (Legacy)
New design direction requires the two halves of detectors must be separated from the outside, and combine from inside the B0 barrel
Current design has the two halves meeting outside the B0 barrel

## Slide 9: B0 Detector Removal/Install (Latest Concept)

## Slide 10: B0 Detector Removal/Install (Latest Concept)
New rail system allows for all detector halves to be separate until in fixed position. Once fixed, the rails will move in parallel position in Z-Axis
Carriages will use a non-captive motor on a fixed lead screw to individually ‘drive’ each detector half into position
Screw jacks will secure on the front face of the support barrel
Inside will likely require a jig for securing the top and bottom rail pivot point in precise location

## Slide 11: Roman Pot Detector Layout
Detector layers are double-sided with maximum coverage
Raphael Dupre (IJCLab, France) is currently simulating cooling methods
Detector layout will not fit in the current Roman Pot design in lattice. There will be an updated model design TBD.

## Slide 12: ZDC EMCAL Removal
EMCAL must be removable for maintenance.
Sourced a COTS lifting table to fit the allotted space in front of the ZDC
Secured the EMCAL on an array of ball transfers.

## Slide 13: ZDC EMCAL Removal