## Slide 1: Echelon-0 (DAQ) Overview and Timeline
Jeff Landgraf

## Slide 2: Outline
Brief Overview of DAQ
DAQ / Echelon-0 Setup
Timeline

## Slide 3
DAQ
Definition of streaming is “No L0 trigger”
  All data is zero suppressed by the front-end electronics
  No system wide deadtime in normal operation
  Collaboration should have the full ability to make data selection cuts on the widest possible criteria
    Flexible event selection, data selection and background characterization
  But subject to an overall throughput budget of ~100Gb/sec
ePIC Streaming will include
  Capabilities for hardware and firmware based Filtering
  Capability for flow control
  Zero suppression & aggregation within data packets
Greater sensitivity to noise
Greater sensitivity to backgrounds
Computing
Definition of streaming is “Process data as it arrives”
  Fast Analysis (~3 weeks not months or years) using automation of calibration and reconstruction.
Requires some overlap between DAQ/computing
  Automation of calibrations
    Mapping calibration dependencies
    Mapping application of calibrations
    Mapping evolution of calibrations
  QA and monitoring can make use of full offline structure
  Consistent schemes and language for data/metadata
  Event selection / tagging / and accounting
ePIC DAQ uses streaming architecture

## Slide 4: EIC Streaming DAQ/Computing Architecture
Collider Characteristics
1260 Bunches arriving at 98.5Mhz (10.15ns bunch separation)
1.015us abort gaps (100 bunches)
⇒ 20 – 141 GeV
𝓛max ⇒ 1034 cm-2 s-1
Electron, proton, and light nuclei beams can be polarized
Each bunch can have different polarization states
  DAQ must tag data to specific bunch crossings
  Need to track luminosity for each bunch crossing
Physics Performance
Maximum DIS rate ~500kHz
Large number of Channels
Low occupancy

## Slide 5: Summary Data Flow
FEB
RDO
Readout Computer
Detector
DAM
PCI/Eth
Fiber
Copper
Aggregate | 2.0 Tb/sec
Noise | 1.6 Tb /sec
Signal from Physics + Background | 400 Gb / sec
Aggregate | 2.0 Tb/sec
Per RDO (Avg) | 0.7 Gb/sec
Eth
Aggregate | 109 Gb/sec
Collision Signal | 62 Gb/sec
Synchrotron Rad | Under design
Electron Beam | 4.5 Gb/sec
Hadron Beam | 1.0 Gb/sec
Noise | 41 Gb/sec
Worst case Data Flow
“Worse Case Data Flow”
𝓛max ⇒ 1034 cm-2 s-1
10 x 275 GeV DIS
DIS rate ~500kHz
After 9 x 109 (1-MeV neq / cm2) delivered fluence
  300kHz DCR in dRICH
  200x rate with no damage
At Worse Case
Need a factor of 20 reduction

## Slide 6: DAQ / Echelon-0
DAQ
O(100 Servers)
Echelon-0
O(100 servers)
daq.local
epic.controlroom
sdcc.local
jlab.local
(esnet)
slowcontrols.local
epic.public
Network Structure:
O(100 links)
O(10 links)
O(1 link)
O(30 link)

## Slide 7
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones

## Slide 8
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones
Common Definition for all DAQ Releases
  Tagged GIT release for all software and firmware so that a collaborator can retrieve and compile
  Written manual to describe use
  Definition of supported hardware
Echelon 1/2/3 – SRO
Should support DAQ releases
Should be supported by DAQ releases

## Slide 9
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones
“PicoDAQ” - Readout Test Setups
  Communicate, program, access features: “Hello data”
  Supporting:
    FLX-155
    DAM substitutes (2-port VD100, 48 port VMK180)
    RDO articles (TBD)
    GTU article
No direct connection to DAQ at this stage
Can have independent prototyping on same time scale

## Slide 10
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones
“MicroDAQ” – Readout detector data in test stand w engineering articles
  Stand alone FEB -> RDO -> DAM implementation using DAQ protocol
  Single RDO, DAM
  Emulation of GTU in DAM
Echelon 0 still not developed at this point, so no interface to Echelon 1!
Will be creating “real” detector data

## Slide 11
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones
“MiniDAQ” – Readout detector data using full hardware and timing chain
  As above, with GTU echelon 0
  Still single stream
First stage where integrated tests can start
DAQ will still be stressing electronics
Development of QA/Calibrations should be in full swing
Echelon 0 should exist with final network structure. Do not need high-rates

## Slide 12
Detector Install: FY29Q2 - FY31Q2
Cosmics: FY31Q3
Early CD-4: FY32Q4
DAQ Releases:
PicoDAQ FY26Q1
  Readout test setups
MicroDAQ: FY26Q4
  Readout detector data in test stand using engineering articles
MiniDAQ: FY28Q1
  Readout detector data using full hardware and timing chain
Full DAQ-v1: FY29Q2
  Full functionality DAQ ready for full system integration & testing
Production DAQ: FY31Q3
Ready for cosmics
MiniDAQ
Production
DAQ
PicoDAQ
MicroDAQ
PDR2
Full DAQ-V1
PDR1
PDR3
Streaming DAQ Milestones
“FullDAQ-v1 – Full functionality DAQ ready for system integration
  Includes run control, capability for merging streams from separate DAM boards, and interface to echelon 1
All components should exist. This is when detectors are installed and integration testing begins. The streaming readout is still being debugged, but is a tool for the collaboration at this point
Echelon 0 computer purchases to ramp up with data needs

## Slide 13
Backup…

## Slide 14
IP-6
DAQ
Room
Control
Room
Control Room overhaul should include total replacement of old consoles and replacement with sufficient workspaces to support the 24+ detector subsystems and their associated control systems
.
DAQ room upgrades (cooling and power) will be dependent on how much of the online computing is housed there.
Updates to available cable tray routing and availability of Riggers are needed to support pulling some 6000+ fibers to three different areas of the Interaction region (south platform and tunnels).

## Slide 15: Scale of Echelon 0 (DAQ) Computing
Current Project estimates provide for roughly a total of 20 racks/cabinets
  200+ total CPU nodes
  ~6000 fibers from the IR (~150m run)
  100-110 DAM Servers (all must reside in the DAQ Room)
Expected total power requirements are between 300-350kW.
Current power infrastructure at IP-6 for the DAQ Room is sufficient (two 330kW taps avaiable):
  Some additional power distribution will be needed
  Existing cooling infrastructure needs to be updated.
  Overall cooling efficiency will need to be improved if everything will be housed locally (DAQ Room).
Default option would be splitting Echelon 0 resources between IP-6 and the BNL Data Center (SDCC).
DAQ Room
From Control Room
26 ft
48 ft
To Assembly Hall
DAQ
Room
Control
Room

## Slide 16
SDCC
IP-6
DAQ
ROOM
To JLAB ePIC
Echelon 1
BNL ePIC
Echelon 1
ESNET
4Tbps
400Gbps
400Gbps
Data Transfer to Echelon 1
Principles
Equal transfer to both echelon 1 facilities (Both receive copies of data)
The desired transfer time to the echelon 1 is O(seconds) for fast feedback
  Buffering for up to several days is available in Echelon 0
ePIC DAQ
Echelon 0
Details not yet fully defined
Data transfer mechanisms are under discussion
Orchestration is under discussion
Are reconstructions done twice or are they split between echelon 1 facilities?
How is QA organized
  Some QA needed in echelon 0
  Physics based QA expected at echelon 1

## Slide 17: Network Infrastructure
ePIC DAQ and computing will require network connectivity at BNL between resources in IP-6, SDCC as well as development labs that is bandwidth guaranteed and minimizes routing.
SDCC
Lab
Lab
Lab
IP-6
DAQ
ROOM
To JLAB ePIC (Echelon 1)
BNL ePIC
Echelon 1
ePIC
DAQ
ESNET
4Tbps
100Gbps
400Gbps
400Gbps
Early DAQ & Electronics development will be in labs (Physics, early 2026-).
Initial computing needs for development would best be placed in a central location (SDCC, initially 1-2 racks, by Q2 FY27).
As construction and installation ramps up at IP-6 additional Echelon 0 computing resources can be placed in both sites (5-6 racks at SDCC, Q2 FY29).
For production running it is important to all network infrastructure in place (Q1 FY32) and have equal and transparent network access from SDCC to both Echelon 1 sites (BNL and JLAB)
Physics

## Slide 18: ePIC Readout Chain (role in data reduction)
Name
Design
Adapter
Detector Specific
Sensor
Detector Specific
Front End Board
(FEB)
Detector Specific
Readout Board
(RDO)
Few Variants
Data Aggregation Module (DAM)
Common
Echelon 0
Computing
Common
Global Timing Unit (GTU)
- Interfaces to Collider
Run Control & DAM
- Config & Control
- Clock & Timing
On Detector
SMT BGA
(BNL)
(JLAB)
Echelon 1
Computing
Common
COTS
Type
Custom Electronics
Custom Electronics
Custom Electronics
FPGA
Large FPGA / SoC
COTS
Role
Aggregation
High Level Filter
Data Reduction Processing
High Level Filter
Data Reduction Processing