## Slide 1
ePIC Electronics and DAQ WG – ASIC / RDO protocols
News / Announcements
  Schedule
    Mar 20: Echelon 0 -- revisit RC / discuss timeframe building?
    Mar 27: GTU & Timing synchronization updates
    April 1&2: Cherenkov PID review
    April 2: Mini Workshop echelon 0/echelon 1/off project computing (S&C, SRO, SDCC)
    https://indico.bnl.gov/event/26856/
    April 3: eRD109 Updates
    April 10: RDO protocols
    Week of April 24: Joint Meeting with SRO regarding monitoring needs / requirements
  Other Announcements?
  TIC report
ASIC / RDO protocols
  Revisit last months summary
  Synchronization

## Slide 2
TIC Summary for 3/10/25: (Fernando, Tonko, Gerard, Jo, Dave, Jeff present)
Test beam plans at CERN
  PS --- CAL 1 week. dRICH has 2 weeks, but too early to use (May). Any requests to replace this time need to be made immediately! But not guaranteed
  SPS --- dRICH 1 week
  MPDG doesn’t have any time this year at cern
Timepix4 Had Beam time (MAMA B 885MeV electrons) (Timepix @ 40MHz) (Simon Gardner)
    DAQ should to LowQ2 regarding spyder 4: plans, streaming scheme, interface to FELIX
Next Mondays Meeting
  Summary of backward EMCAL testbeam
  Define geometries for simulation studies (2 options FF/FB cylindrical symmetry, maximum acceptance)

## Slide 3
Protocol Document Proposals
Command/Group | Purpose | Require Constant Latency? | Universal
syncSet | Define Clock Reference | Yes | Yes
revTick | Define Collider Revolution | Yes | No (or is synchSet)
syncRead | Trigger clock read (full trigger?) | Yes | Yes
pulsers | Synchronized calibration | Yes | No
reset and configure | Initiate configuration/potentially with help from SC interface | No | Yes
slow controls | Fast slow controls routes | No | Yes/No
Not present? Needed? |  |  | 
Run Start | Instruct ASICs to send data |  | 
Run Stop | Instruct ASICs to stop sending data |  | 
Document the rule that synchronous commands are only sent on multiples of 5 EIC Bunch crossings
Decide and document whether RDOs are aware of both 98.5 MHz and 39.4 MHz clocks, or that they are only aware of clock cycles and the clock counter to time conversion is handled in the DAM board. (My preference is the second)
Avoid micromanaging the ASIC commands per detector. Instead assume that there will be a translation stage required for many commands
  For the same synchronous commands there may be different bit patterns firing that command for different ASICs
  For commands that do not require constant latency, and are not universal define a superset of commands, and allow the translation of a single command into a series of commands issued from the DAM board
Define a series of states for the ASICs to be in, the triggers for translations to each state, and the behavior of the ASICs in these states:
  Irakli has put together a slide deck proposing some ideas: https://indico.bnl.gov/event/26507/contributions/103235/attachments/59952/102982/250106_IM_RunControl.pdf
    One of his main requests is that the time frame synchronization be strictly repeating (e.g. Based on a count of rev-ticks)
    This seems shared by the ALCOR concept, for example which is defining ASIC frames based on revolutions in the current scheme
      Advantage here is that the ASICs can maintain their own understanding of the timing / counters / bunch structure
    The other concept is asynchronous definition of the time frame synchronization
      Advantage here is that the time frame definition is flexible and defined by the higher level DAQ system, time frame concept doesn’t need to have specific uniform support among different ASICs
      Reset scheme has well defined rule (Comes from GTU, not arbitrated with ASIC states)
  Eg: On, Configured, Running, etc…
  This includes indicating whether inhibiting data sends means that the ASICs don’t produce data, that the RDO doesn’t read any data produced, or whether the DAM board doesn’t read any data produced.
Existing document to be gutted, with obsolete details removed, but existing features listed as requirements. These points to be added. Discuss next month!
This should be true for global “actions”
  Calibration events, Flow control, Set Bunch Crossing
  Run Start / Stop
Generally, though needs more thought. Filled Bunch, spin orientation, and the like are associated with actual Bunch crossings. These items need to be stored in the data stream and potentially available to the GTU/DAM but not needed at the RDO/ASIC level.
Need to define a more complete set of commands with the applicable sources, destinations, and time alignments

## Slide 4
Protocol Document Proposals
Command/Group | Purpose | Require Constant Latency? | Universal
syncSet | Define Clock Reference | Yes | Yes
revTick | Define Collider Revolution | Yes | No (or is synchSet)
syncRead | Trigger clock read (full trigger?) | Yes | Yes
pulsers | Synchronized calibration | Yes | No
reset and configure | Initiate configuration/potentially with help from SC interface | No | Yes
slow controls | Fast slow controls routes | No | Yes/No
Not present? Needed? |  |  | 
Run Start | Instruct ASICs to send data |  | 
Run Stop | Instruct ASICs to stop sending data |  | 
Document the rule that synchronous commands are only sent on multiples of 5 EIC Bunch crossings
Decide and document whether RDOs are aware of both 98.5 MHz and 39.4 MHz clocks, or that they are only aware of clock cycles and the clock counter to time conversion is handled in the DAM board. (My preference is the second)
Avoid micromanaging the ASIC commands per detector. Instead assume that there will be a translation stage required for many commands
  For the same synchronous commands there may be different bit patterns firing that command for different ASICs
  For commands that do not require constant latency, and are not universal define a superset of commands, and allow the translation of a single command into a series of commands issued from the DAM board
Define a series of states for the ASICs to be in, the triggers for translations to each state, and the behavior of the ASICs in these states:
  Irakli has put together a slide deck proposing some ideas: https://indico.bnl.gov/event/26507/contributions/103235/attachments/59952/102982/250106_IM_RunControl.pdf
    One of his main requests is that the time frame synchronization be strictly repeating (e.g. Based on a count of rev-ticks)
    This seems shared by the ALCOR concept, for example which is defining ASIC frames based on revolutions in the current scheme
      Advantage here is that the ASICs can maintain their own understanding of the timing / counters / bunch structure
    The other concept is asynchronous definition of the time frame synchronization
      Advantage here is that the time frame definition is flexible and defined by the higher level DAQ system, time frame concept doesn’t need to have specific uniform support among different ASICs
      Reset scheme has well defined rule (Comes from GTU, not arbitrated with ASIC states)
  Eg: On, Configured, Running, etc…
  This includes indicating whether inhibiting data sends means that the ASICs don’t produce data, that the RDO doesn’t read any data produced, or whether the DAM board doesn’t read any data produced.
Existing document to be gutted, with obsolete details removed, but existing features listed as requirements. These points to be added. Discuss next month!
There seemed to be consensus that the RDO is only aware of the clock for it’s own sub-components

## Slide 5
Protocol Document Proposals
Command/Group | Purpose | Require Constant Latency? | Universal
syncSet | Define Clock Reference | Yes | Yes
revTick | Define Collider Revolution | Yes | No (or is synchSet)
syncRead | Trigger clock read (full trigger?) | Yes | Yes
pulsers | Synchronized calibration | Yes | No
reset and configure | Initiate configuration/potentially with help from SC interface | No | Yes
slow controls | Fast slow controls routes | No | Yes/No
Not present? Needed? |  |  | 
Run Start | Instruct ASICs to send data |  | 
Run Stop | Instruct ASICs to stop sending data |  | 
Document the rule that synchronous commands are only sent on multiples of 5 EIC Bunch crossings
Decide and document whether RDOs are aware of both 98.5 MHz and 39.4 MHz clocks, or that they are only aware of clock cycles and the clock counter to time conversion is handled in the DAM board. (My preference is the second)
Avoid micromanaging the ASIC commands per detector. Instead assume that there will be a translation stage required for many commands
  For the same synchronous commands there may be different bit patterns firing that command for different ASICs
  For commands that do not require constant latency, and are not universal define a superset of commands, and allow the translation of a single command into a series of commands issued from the DAM board
Define a series of states for the ASICs to be in, the triggers for translations to each state, and the behavior of the ASICs in these states:
  Irakli has put together a slide deck proposing some ideas: https://indico.bnl.gov/event/26507/contributions/103235/attachments/59952/102982/250106_IM_RunControl.pdf
    One of his main requests is that the time frame synchronization be strictly repeating (e.g. Based on a count of rev-ticks)
    This seems shared by the ALCOR concept, for example which is defining ASIC frames based on revolutions in the current scheme
      Advantage here is that the ASICs can maintain their own understanding of the timing / counters / bunch structure
    The other concept is asynchronous definition of the time frame synchronization
      Advantage here is that the time frame definition is flexible and defined by the higher level DAQ system, time frame concept doesn’t need to have specific uniform support among different ASICs
      Reset scheme has well defined rule (Comes from GTU, not arbitrated with ASIC states)
  Eg: On, Configured, Running, etc…
  This includes indicating whether inhibiting data sends means that the ASICs don’t produce data, that the RDO doesn’t read any data produced, or whether the DAM board doesn’t read any data produced.
Existing document to be gutted, with obsolete details removed, but existing features listed as requirements. These points to be added. Discuss next month!
Martin detailed the scheme by which sPHENIX handles something very like this.
Martins Presentation: https://indico.bnl.gov/event/27174/contributions/104464/attachments/60494/103877/GTU_Discussion_2025_03_11.pptx
In this scheme the full run periods commands are configured to fire on a deterministic preset schedule and implemented for each detector by the ePIC equivalent of the DAM Board
The scheme could also be easily adapted to be initiated synchronously from the GTU, but operated by the DAM boards and if so, could handle both simple and complex translation tasks for ASIC differences. Some tasks can also be removed entirely from the GTU.

## Slide 6
Protocol Document Proposals
Command/Group | Purpose | Require Constant Latency? | Universal
syncSet | Define Clock Reference | Yes | Yes
revTick | Define Collider Revolution | Yes | No (or is synchSet)
syncRead | Trigger clock read (full trigger?) | Yes | Yes
pulsers | Synchronized calibration | Yes | No
reset and configure | Initiate configuration/potentially with help from SC interface | No | Yes
slow controls | Fast slow controls routes | No | Yes/No
Not present? Needed? |  |  | 
Run Start | Instruct ASICs to send data |  | 
Run Stop | Instruct ASICs to stop sending data |  | 
Document the rule that synchronous commands are only sent on multiples of 5 EIC Bunch crossings
Decide and document whether RDOs are aware of both 98.5 MHz and 39.4 MHz clocks, or that they are only aware of clock cycles and the clock counter to time conversion is handled in the DAM board. (My preference is the second)
Avoid micromanaging the ASIC commands per detector. Instead assume that there will be a translation stage required for many commands
  For the same synchronous commands there may be different bit patterns firing that command for different ASICs
  For commands that do not require constant latency, and are not universal define a superset of commands, and allow the translation of a single command into a series of commands issued from the DAM board
Define a series of states for the ASICs to be in, the triggers for translations to each state, and the behavior of the ASICs in these states:
  Irakli has put together a slide deck proposing some ideas: https://indico.bnl.gov/event/26507/contributions/103235/attachments/59952/102982/250106_IM_RunControl.pdf
    One of his main requests is that the time frame synchronization be strictly repeating (e.g. Based on a count of rev-ticks)
    This seems shared by the ALCOR concept, for example which is defining ASIC frames based on revolutions in the current scheme
      Advantage here is that the ASICs can maintain their own understanding of the timing / counters / bunch structure
    The other concept is asynchronous definition of the time frame synchronization
      Advantage here is that the time frame definition is flexible and defined by the higher level DAQ system, time frame concept doesn’t need to have specific uniform support among different ASICs
      Reset scheme has well defined rule (Comes from GTU, not arbitrated with ASIC states)
  Eg: On, Configured, Running, etc…
  This includes indicating whether inhibiting data sends means that the ASICs don’t produce data, that the RDO doesn’t read any data produced, or whether the DAM board doesn’t read any data produced.
Existing document to be gutted, with obsolete details removed, but existing features listed as requirements. These points to be added. Discuss next month!
The consensus for the synchronization scheme seems to be the repeating signal of fixed length sent to the ASICs
A synchronous trigger (preferably with only time response) is still very useful for verification at the software level
There may be detectors with different lengths for the repeating signal (revtic=12us, CERN revtic=89us, 128xCERN revtic=11ms)?
Does anyone know the synchronization scheme for the Timepix/Astropix?

## Slide 7
Protocol Document Proposals
Command/Group | Purpose | Require Constant Latency? | Universal
syncSet | Define Clock Reference | Yes | Yes
revTick | Define Collider Revolution | Yes | No (or is synchSet)
syncRead | Trigger clock read (full trigger?) | Yes | Yes
pulsers | Synchronized calibration | Yes | No
reset and configure | Initiate configuration/potentially with help from SC interface | No | Yes
slow controls | Fast slow controls routes | No | Yes/No
Not present? Needed? |  |  | 
Run Start | Instruct ASICs to send data |  | 
Run Stop | Instruct ASICs to stop sending data |  | 
Document the rule that synchronous commands are only sent on multiples of 5 EIC Bunch crossings
Decide and document whether RDOs are aware of both 98.5 MHz and 39.4 MHz clocks, or that they are only aware of clock cycles and the clock counter to time conversion is handled in the DAM board. (My preference is the second)
Avoid micromanaging the ASIC commands per detector. Instead assume that there will be a translation stage required for many commands
  For the same synchronous commands there may be different bit patterns firing that command for different ASICs
  For commands that do not require constant latency, and are not universal define a superset of commands, and allow the translation of a single command into a series of commands issued from the DAM board
Define a series of states for the ASICs to be in, the triggers for translations to each state, and the behavior of the ASICs in these states:
  Irakli has put together a slide deck proposing some ideas: https://indico.bnl.gov/event/26507/contributions/103235/attachments/59952/102982/250106_IM_RunControl.pdf
    One of his main requests is that the time frame synchronization be strictly repeating (e.g. Based on a count of rev-ticks)
    This seems shared by the ALCOR concept, for example which is defining ASIC frames based on revolutions in the current scheme
      Advantage here is that the ASICs can maintain their own understanding of the timing / counters / bunch structure
    The other concept is asynchronous definition of the time frame synchronization
      Advantage here is that the time frame definition is flexible and defined by the higher level DAQ system, time frame concept doesn’t need to have specific uniform support among different ASICs
      Reset scheme has well defined rule (Comes from GTU, not arbitrated with ASIC states)
  Eg: On, Configured, Running, etc…
  This includes indicating whether inhibiting data sends means that the ASICs don’t produce data, that the RDO doesn’t read any data produced, or whether the DAM board doesn’t read any data produced.
Existing document to be gutted, with obsolete details removed, but existing features listed as requirements. These points to be added. Discuss next month!
Not done

## Slide 8: Absolute Synchronization
What are our requirements for absolute synchronization?
The dRICH needs to apply time windows relative to the bunch crossing for data volume reduction. The time window is currently estimated to be 2 ns. This needs an absolute calibration of the timing to O(100-200 ps)
For all other subsystems, to first order we could calibrate time synchronization using beam, or detector wide calibration systems (e.g. lasers) and apply these in software
Are there potential issues if the absolute synchronization is too far out?
  Any sort of action trigger (pulsers, etc) would arrive at different actual times. Potentially even in different bunch crossings which might affect attempts to issue such commands during abort gaps
  Any echelon 0 analysis (pre-T0 calibration) would we affected.
    Cluster finding?
    Summing / histogramming of luminosity detector
  Others?
  These would seem to lead to some requirement (1ns?) for internal detector absolute timing, if not for a global requirement.
Where are phase adjustments necessary, and where do characteristics such as fiber lengths need to be carefully controlled?