## Slide 1: Neural Compression for sPHENIX TPC Data
Oct. 16, 2024
By Yi Huang, Yihui Ren, Shinjae Yoo, Jin Huang
Speaker: Yi Huang

## Slide 2: The sPHENIX Experiment

## Slide 3: Detector model at sPHENIX
Silicon Trackers
Calorimeters
Time-projection Chamber
Notes: sPHENIX is composed of 9 detectors at the Relativistic Heavy Ion Collider at BNL. From inside out, are the silicon trackers, the Time-projection Chamber which is the subject of our study and the calorimeters. Time-projection chamber is the major tracking device at sPHENIX and dominate the data volume.

## Slide 4: Time projection Chamber (TPC)
A TPC acts as a camera capturing 3D particle trajectories.
Along the radial dimension, TPC has 3 groups of layers of 16 layers each group.
Along the beam dimension, TPC is divided into two sides by the transverse plane passing the collision point
Along the azimuthal dimension, TPC is divided into 12 sectors, degree each.
Notes: Time projection chamber produce tracking data at extremely high data rate and we cannot save all the data produced to the permanent storage for future study. The currently solution is to use a trigger system to select collision most valuable events and discard the remaining. However, as we move gradually to streaming data intake, we want to see whether we develop fast compression algorithm based on deep neural network to make saving all data possible.

## Slide 6: TPC Data
The challenge of sparse data

## Slide 7
In this study, we are going to focus on the outer layer group:
16 layers along the radial direction
2304 columns of sensor nodes along the azimuth direction
498 rows along the beam direction
Subdivided into 24 TPC wedges of shape (16, 192, 249)

## Slide 8
Each sensor node output an analog-to-digit converter (ADC) value as an integer in [0, 1023].
All ADC values below 64 are suppressed to 0 to increase sparsity.
In this study, we use log scale ADC value, i.e. . A log scale ADC value is in [0, 10]. There is no value less 6 because of the zero suppression.
TPC wedges of shape (16, 192, 249)
Input to the neural compression algorithm
Fig. Log scale ADC value in a TPC wedge

## Slide 9
Discontinuous, bi-modal distribution

## Slide 10: Neural Compression, stage 1
Design neural compressor for discontinuous distribution

## Slide 11
https://arxiv.org/pdf/2111.05423.pdf
BCAE

## Slide 12
input
Segmentation output (mask)
Regression output
Permanent storage

## Slide 13
input
Segmentation output (mask)
Regression output
Permanent storage

## Slide 14
input
Regression output mask
Regression loss

## Slide 15
Classification ground truth (input )
mask
Classification loss

## Slide 16
Performance of BCAE comparing to off-the-shelf lossy compression algorithms

## Slide 17: Neural Compression, stage 2
Aiming for higher throughput

## Slide 18: Use 2D Convolution to make BCAE Faster
16 layers
The TPC wedge data has shape (16, 192, 249).
Comparing to the azimuth and horizontal direction, the radial dimension is thin.
We can treat the radial dimension as the feature dimension and use 2D convolutions

## Slide 19: Throughput comparison two computing modes

## Slide 20: Performance comparison

## Slide 21: Neural Compression, stage 3
Can sparsity be a bless?

## Slide 24
Locate the most valuable signals

## Slide 25
Sparse
Convolution
BCAE-VS
Variable ratio Compression for Sparse input

## Slide 26
Sparse Convolution Engines

## Slide 27
Performance Comparison

## Slide 28
Performance Comparison

## Slide 29
Reconstruction Accuracy—regression

## Slide 30
Reconstruction Accuracy—classification

## Slide 31
Variable compression ratio and Throughput
as function of sparsity

## Slide 32
Newest Result of BCAE-VS on proton-proton Collision
type |  | PSNR | precision | recall
Au + Au | 0.0284 | 26.0 | 0.996 | 0.988
p + p | 0.0073 | 28.7 | 0.994 | 0.985
p + p (scaled) | 0.0329 |  |  | 
type |  | PSNR | precision | recall
Au + Au | 0.0284 | 26.0 | 0.996 | 0.988
p + p | 0.0073 | 28.7 | 0.994 | 0.985
p + p (scaled) | 0.0329 |  |  | 
When comparing and compression ratio, the number should be scaled by ratio of occupancy of the two datasets (0.108 / 0.024 = 4.5).
type | Retention ratio | occupancy | Compression ratio
Au + Au | 0.133 | 0.108 | 34
p + p | 0.109 | 0.024 | 185
p + p (scaled) |  |  | 152

## Slide 33: Neural Compressor on AI Accelerators

## Slide 34
How Fast could Compression be on Alternative
AI Hardware Accelerators
GPUs (shared memory)
GraphCore and Groq (on-chip memory)

## Slide 35
BCAE-2D Encoder

## Slide 36: Thank you!