## Slide 1: eRD108: MPGD for ePIC Progress Report
ePIC EIC Project R&D Day
Apr 16th 2025
F. Jeanneau on behalf of
eRD108 consortium

## Slide 2: eRD108 Consortium and ePIC MPGD-DCS
eRD108
ePIC MPGD Detector Subsystem Collaboration

## Slide 3: MPGD in ePIC tracking system
MPGDs complement the silicon tracker:
- redundancy hit points
- faster hits for track finding
Three systems:
- CyMBaL: Cylindrical Micromegas Barrel Layer at R=55cm
- µRWELL Barrel Outer Tracker: planar detectors at the DIRC surface
- µRWELL End Cap Tracker: disks in the forward and backward regions
eRD108 program about Cylindrical MPGD detectors with 2D readout:
Development of 2D cylindrical Micromegas detectors: funded in FY24
Development of a cylindrical μRWELL prototype: completing the FY23 program

## Slide 4: Cylindrical Micromegas R&D
Update on 2D readout R&D
and scale 1:1 prototype
CEA Saclay

## Slide 5: CyMBaL
CyMBaL: Cylindrical Micromegas Barrel Layer
32 module: 8 modules in ϕ times 4 modules in z
Overlaps in ϕ and in z for hermeticity
1024 readout channels/module
32K readout channels
67 cm
59 cm
46 cm
Design of a module
Requirements:
Spatial resolution ~150µm
Time resolution ~20ns
Light, less than 1% X0
Hermetic
Tight space: ~5cm in R
Magnetic field: ~2T
Ongoing:
Rethinking and validating requirement assumptions.
Do we need the same resolution in both directions?
  R*Phi ≤ 500 μm
  Z ≤ 300 μm
Time resolution better than 20ns needed?

## Slide 6: CyMBaL – Technology and planned R&D
CLAS12 resistive Micromegas
  Material budget ~0.4%
  Working in high radiation environment and in B=5T
  Taking data since 2017
  Fit in tight spaces
Upgrade for ePIC: 2D readout
R&D ongoing activities
Analysis of the 2023 test beam data: too much multiple scattering to draw firm conclusions
Standard photoresist material no more produced  R&D to adapt process to new material (Dynamask) resulting in delays
New prototypes production to complete the previous tests (November 2025 test beam):
  resistive patterns
  2D readout
  inclined tracks (1 mm drift) vs clustering with time information
Design of a scale 1 prototype (2D readout)

## Slide 7: CyMBaL – 2023 Test Beam analysis -- recap
Data taken in June 2023 at MAMI
880 MeV electron beam
ALPIDE-based reference telescope
Tested several prototypes
Important multiple scattering effect
Geant4 simulations to cross check
~30cm from ref tracker
~78cm from ref tracker
Data
MC

## Slide 8: CyMBaL – Test 2D prototypes
12x12 cm2 prototypes to test:
2D readout patterns
Resistive layer motifs
very-low material budget (0.2% X0)
Pitch and interstrip variations
ASACUSA like motifs
Variation of resistive layer (full, strips, grid)
R/O Patterns and resistive motifs
More info: S. Rafael Plocher QNP proceedings
Amplitude fraction, 25% low, 50% too high: the sharing of the signal is not uniform, interstrip with values round 30% should work better
Residues (uncorrected):
D1 (closest to beam exit) provides less than 200µm with 1mm pitch, with high resistiviy

## Slide 9: CyMBaL – Tests in Saclay
Cosmic rays test bench refurbished
Silicon telescope (same as in beam test) added to the system
Mechanical structure to hold up to six prototypes
Synchronization of MM and ALPIDE DAQs
Development of software tool for the data taking and analysis optimization
The DAQ system is now adapted to be portable to a next beam test

## Slide 10: CyMBaL – Tests in Saclay
In order to improve the bulk process feasibility we glue our readout Kapton on FR4 substrate and we can see the gluing defects !
Credit: Dylan Neff

## Slide 11: CyMBaL – new prototypes RD5

## Slide 12: CyMBaL – Toward a scale 1:1 prototype
Based on CLAS12 construction process
Bulk of a metallic and a resistive CLAS12 PCB
Bent in shape
Small mechanical prototype
Connector KEL validation
Different connectors orientations
Robustness of soldering
Connection feasibility
Holders needed?
Size 1 prototype:
Working prototype
  Readout plane validation
  HV segmentation
  Drift design
Mechanical prototype
  Curving tooling and procedure
  Interfaces design (fixation, cooling, gas,…)
Top / Top
Top / Bottom
Face to face
MEC8
Segmented resistif

## Slide 13: CyMBaL – Milestones
T2/25: Small mechanical proto to test connectors vs geometry vs bending
T3/25: re-manufacturing of RD4 PCB to tune bulk process and prepare test beam
T3/25: new protos design and manufacturing in preparation of november test beam
T4/25: test beam
T4/25: Finalisation design size 1 prototype 0 (GEIC0)
T1/26: production and test of GEIC0
T3/26: developement and production of size 1 prototype 1 (GEIC1), including feedback from RDx test beam and GEIC0

## Slide 14
eRD108: R&D on Cylindrical µRWELL Prototypes
µRWELL-R/O
Cathode foil
Inner clamp
Outer clamp
Main frame
40 cm
26 cm
Design features & Goal
Prototype consists of 2 half-cylinder chambers with two different capacitive-sharing readout structures
            2D capaSh proto: µRWELL/readout foil with straight U-V strips
2D zigzag proto: µRWELL/readout foil with zigzag U-V strips
Goal is to study performance of two readout options for cylindrical µRWELL
1.35 mm
pitch
1.35 mm
pitch
U-strip
V-strip
U-V zigzag readout concept (BNL)
U-V capacitive-sharing readout (JLab)
Exploded 3D view of detector design

## Slide 15
Earlier Work on Cylindrical µRWELL prototypes
Cyl. µRWELL prototype at Fermilab test beam setup, June 2023
Downstream
GEM Trackers
Cyl. µRWELL
Unable to operate and take data at the Fermilab 2023 test beam
      Fermilab shut down that week for safety concerns at the lab
      HV instabilities caused by dents on the Al cathode during operation
Initial prototype with Al-mylar foil drift cathode
Dents on cathode foil
Consequently, detector rebuilt & refurbished in 2024/25
      Honeycomb support to consolidate to Al/Mylar cathode foil  completed August 2024
      Gas tightness & HV test  completed Dec 2024
        Observe larger leakage currents (tens of µA) than expected for both prototypes

## Slide 16
New Material Budget for Reinforced Cathode Drift Foil
Area = 36.7 cm × 36.7 cm
Height = 5mm
Wall thickness = 0.11mm
Component | Mass (g) | Thickness (cm) | X₀ (g/cm²) | Material Budget (X/X₀)
Nomex honeycomb (Drift Cathode Support Structure) | 10 | 0.5 | 29.6 | 0.025%
Al/mylar + epoxy (Original Drift Cathode) | 70 | 0.03 | ~30 | 0.168%
Total Reinforced Cath. Drift Foil | 80 | ~0.53 cm | — | ≈ 0.193% X₀

## Slide 17
Commissioning of the Prototypes @ UVa
Straight-Strip U-V Prototype
Orange Detector Frame
ZigZag U-V Prototype :
Black Detector Frame
Two Scintillators
Trigger Rate: ~ 10 Hz
CODA-based SRS DAQ with APV25 readout
March 21st, 2025
Both prototypes moved to UVa for preliminary HV test and hunt for signal in the chambers in preparation for Hall D beam test at JLab
      Repeat HV test in N2 (April 2027)
      Check pedestal data with APV25-SRS electronics
      HV conditioning with Ar-CO2
            Some HV instabilities observed
  Prototypes will be sent to JLab on April 21st for installation in the Hall D Pair Spectrometer for two-week beam test

## Slide 18
Measured Leakage Currents
N2 Gas flowing rate
  140 units
Dew Point: -48.7
I_drift :
  Zigzag-Strip: <0.02 µA
  Straight-Strip: <0.3 µA
HV scans in N2 Gas

## Slide 19
Pedestal Data Taken with One of the Prototypes
Six (6) APVs for each detector
Pedestal data were taken in N2 gas with VuRWELL = 250V, Vdrift = 600V
DAQ working

## Slide 20
First hits from Cosmic
Cosmic data for Straight-Strip Detector
  ArCO2 (80/20) Gas flowing rate: 140 units; Dew Point: -49.9
  μRWELL =540 V; Drift =1240 V
  μRWELL current fluctuated at the first 10 mins, then stabilized at the expected value (64.8 µA)

## Slide 21
Timeline for closure
Detector rebuild and refurbishment August 2024
Gas tightness test December 2024
HV tests January 2025
Transport detector to UVA March 21
Repeat HV Test April 7
Taking cosmics data at UVA April 18 -20
Transport detectors from UVA and mount setup at JLab and flush gas April 21
Data taking at JLab in beam test April 23 - May 7
Data analysis May – Aug
Prepare publication Sep – Dec

## Slide 22
ePIC MPGD Outer Tracker: Update on the Engineering Test Article

## Slide 23
ePIC Barrel Outer Tracker: PED Test Article
µRWELL-BOT module
Thin-gap (1-mm drift) hybrid amplification GEM-µRWELL detector
On-detector Front End Boards (FEBs) based on SALSA chips
Requirements:
Spatial resolution:
  100 µm (normal tracks), < 150 µm @ 45O
Time resolution: 10 ns
Efficiency ~97%
Active area 34 cm
Active area 36 cm
3 mm honeycomb
readout PCB
FEB
G10 frames
GEM
µRWELL
cathode
cross-section view of thin-gap GEM-µRWELL detector
https://wiki.bnl.gov/eic/upload/ERD_tgMPGD_FY22_endOfYearReport_final.pdf

## Slide 24
ePIC Barrel Outer Tracker: PED Test Article
μRWELL foil Design
CAD design of thin-gap GEM-µRWELL engineering test article
GEM foil Design
Capacitive-sharing U/V strip readout plane Design

## Slide 25
PED Test Article: Assembly clean room @ JLab
Clean room floor plan

## Slide 26
PED Test Article: Timeline & Milestones
GEM foil and μRWELL PCB at the CERN workshop: Delivery expected June 2025 (instead of January)
Support frames for the detector parts (RESARM (Belgium): Delivered early March 2025
Clean room space allocated and equipment for the assembly of the test article at JLab
  Design of mechanical stretcher completed: Procurement of parts ongoing
  Design of HV test box for GEM foil and μRWELL completed: Procurement of parts ongoing
If GEM and μRWELL are delivered “in time” by May 2025  assembly will be completed by August / September 2025
  In time for test in beam at CERN in Fall 2025