## Slide 1
Electronics overview with respect to digitization
We need to define the goal of the digitization to specify the level of digitization needed:
What | Description
RAW_Hits/REC_Hits | CellID, floating point X,Y,Z,T,Q,E,Errors(x,y,z,t,e) [Cell_ID contains local coordinates – last I looked (Dec 2023) somewhat inconsistently handled and don’t go down to channel level] --- (Hits correspond to active volume, not readout)
Remove Event ID / AssembleTimeframes | Done in specific cases using the mixing software, but could be incorporated more generally in simulation
Make Discrete / Apply Thresholds | ADCs/Times are integers. Dynamic range / Discrete step size depend upon detector. Thresholds are applied, but may not be valid when applied at hit level if they need to be applied by channel (sum then cut != cut then sum)
Go to local coordinates | (X,Y,Z)  (sector, module, sensor, asic, channel). In some detectors this is a calculation, perhaps a complex calculation: - Needs to go to channel level (which may not be available in CellID, and mapping may not be defined yet) - RICH detectors (sense the photons @ the sensors, not the simulated particles) - Barrel ECAL (fiber drift time corresponds to z position) - Pair Spectrometer: sweeper magnet / photon conversion - Calibration parameterization for component level timing / alignment shifts - Find T0’s
Extend hits to channels with charge sharing | Simulated hits can fire multiple channels - Calorimeters/TOF/MPGDs all have charge sharing - Calorimeters are summed SiPMs in some cases with many layers (angled tracks cross channel boundaries) - pfRICH electronics sees direct particles and Cherenkov photons
ASIC Formats | Present data in ASIC format (Requires a high-level bank structure to navigate to ASICs, then ASIC data). Time series hit info, TOA, TOT values which need translation to Time/(charge or energy deposited)
Awareness of ASIC/FEB response | Preamp / Shaping / Mapping ASIC parameters to hit features (e.g. CALOROC ADC is a calculation from TOT/a series of potentially saturated sampled ADCs)
Awareness of FEB aggregation | Eg. Summing of SiPMs / layers in FEB before they are read into ASICs / Digitization
Sensor response | I don’t know how much this is already incorporated in the simulations…

## Slide 2
Electronics overview with respect to digitization
We need to define the goal of the digitization to specify the level of digitization needed:
  There are many levels of digitization we might care about, in increasing levels of detail
What | Description
RAW_Hits/REC_Hits | CellID, floating point X,Y,Z,T,Q,E,Errors(x,y,z,t,e), [Cell_ID contains local coordinates – last I looked (Dec 2023) somewhat inconsistently handled and don’t go down to channel level] --- (Hits correspond to active volume, not readout)
Remove Event ID / AssembleTimeframes | Done in specific cases using the mixing software, but could be incorporated more generally in simulation
Make Discrete / Apply Thresholds | ADCs/Times are integers. Dynamic range / Discrete step size depend upon detector. Thresholds are applied, but may not be valid when applied at hit level if they need to be applied by channel (sum then cut != cut then sum)
Go to local coordinates | (X,Y,Z)  (sector, module, sensor, asic, channel). In some detectors this is a calculation, perhaps a complex calculation: - Needs to go to channel level (which may not be available in CellID, and mapping may not be defined yet) - RICH detectors (sense the photons @ the sensors, not the simulated particles) - Barrel ECAL (fiber drift time corresponds to z position - Pair Spectrometer: sweeper magnet / photon conversion - Calibration parameterization for component level timing / alignment shifts
Extend hits to channels with charge sharing | Simulated hits can fire multiple channels - Calorimeters/TOF/MPGDs all have charge sharing - Calorimeters are summed SiPMs in some cases with many layers (angled tracks cross channel boundaries) - pfRICH electronics sees direct particles and Cherenkov photons
ASIC Formats | Present data in ASIC format (Requires a high-level bank structure to navigate to ASICs, then ASIC data). Time series hit info, TOA, TOT values which need translation to Time/(charge or energy deposited)
Awareness of ASIC/FEB response | Preamp / Shaping / Mapping ASIC parameters to hit features (e.g. CALOROC charge deposited is a calculation from TOT/a series of potentially saturated sampled ADCs)
Awareness of FEB aggregation | Eg. Summing of SiPMs / layers in FEB before they are read into ASICs / Digitization
Sensor response | I don’t know how much this is already incorporated in the simulations…
Needed to Verify Physics

## Slide 3
Electronics overview with respect to digitization
We need to define the goal of the digitization to specify the level of digitization needed:
  There are many levels of digitization we might care about, in increasing levels of detail
What | Description
RAW_Hits/REC_Hits | CellID, floating point X,Y,Z,T,Q,E,Errors(x,y,z,t,e) [Cell_ID contains local coordinates – last I looked (Dec 2023) somewhat inconsistently handled and don’t go down to channel level] --- (Hits correspond to active volume, not readout)
Remove Event ID / AssembleTimeframes | Done in specific cases using the mixing software, but could be incorporated more generally in simulation
Make Discrete / Apply Thresholds | ADCs/Times are integers. Dynamic range / Discrete step size depend upon detector. Thresholds are applied, but may not be valid when applied at hit level if they need to be applied by channel (sum then cut != cut then sum)
Go to local coordinates | (X,Y,Z)  (sector, module, sensor, asic, channel). In some detectors this is a calculation, perhaps a complex calculation: - Needs to go to channel level (which may not be available in CellID, and mapping may not be defined yet) - RICH detectors (sense the photons @ the sensors, not the simulated particles) - Barrel ECAL (fiber drift time corresponds to z position - Pair Spectrometer: sweeper magnet / photon conversion - Calibration parameterization for component level timing / alignment shifts
Extend hits to channels with charge sharing | Simulated hits can fire multiple channels - Calorimeters/TOF/MPGDs all have charge sharing - Calorimeters are summed SiPMs in some cases with many layers (angled tracks cross channel boundaries) - pfRICH electronics sees direct particles and Cherenkov photons
ASIC Formats | Present data in ASIC format (Requires a high-level bank structure to navigate to ASICs, then ASIC data). Time series hit info, TOA, TOT values which need translation to Time/(charge or energy deposited)
Awareness of ASIC/FEB response | Preamp / Shaping / Mapping ASIC parameters to hit features (e.g. CALOROC ADC is a calculation from TOT/a series of potentially saturated sampled ADCs)
Awareness of FEB aggregation | Eg. Summing of SiPMs / layers in FEB before they are read into ASICs / Digitization
Sensor response | I don’t know how much this is already incorporated in the simulations…
Needed to analyze data volumes, to demonstrate full reconstruction under operations-like conditions

## Slide 4
Electronics overview with respect to digitization
We need to define the goal of the digitization to specify the level of digitization needed:
  There are many levels of digitization we might care about, in increasing levels of detail
What | Description
RAW_Hits/REC_Hits | CellID, floating point X,Y,Z,T,Q,E,Errors(x,y,z,t,e) [Cell_ID contains local coordinates – last I looked (Dec 2023) somewhat inconsistently handled and don’t go down to channel level] --- (Hits correspond to active volume, not readout)
Remove Event ID / AssembleTimeframes | Done in specific cases using the mixing software, but could be incorporated more generally in simulation
Make Discrete / Apply Thresholds | ADCs/Times are integers. Dynamic range / Discrete step size depend upon detector. Thresholds are applied, but may not be valid when applied at hit level if they need to be applied by channel (sum then cut != cut then sum)
Go to local coordinates | (X,Y,Z)  (sector, module, sensor, asic, channel). In some detectors this is a calculation, perhaps a complex calculation: - Needs to go to channel level (which may not be available in CellID, and mapping may not be defined yet) - RICH detectors (sense the photons @ the sensors, not the simulated particles) - Barrel ECAL (fiber drift time corresponds to z position - Pair Spectrometer: sweeper magnet / photon conversion - Calibration parameterization for component level timing / alignment shifts
Extend hits to channels with charge sharing | Simulated hits can fire multiple channels - Calorimeters/TOF/MPGDs all have charge sharing - Calorimeters are summed SiPMs in some cases with many layers (angled tracks cross channel boundaries) - pfRICH electronics sees direct particles and Cherenkov photons
ASIC Formats | Present data in ASIC format (Requires a high-level bank structure to navigate to ASICs, then ASIC data). Time series hit info, TOA, TOT values which need translation to Time/(charge or energy deposited)
Awareness of ASIC/FEB response | Preamp / Shaping / Mapping ASIC parameters to hit features (e.g. CALOROC adc is a calculation from TOT/a series of potentially saturated sampled ADCs)
Awareness of FEB aggregation | Eg. Summing of SiPMs / layers in FEB before they are read into ASICs / Digitization
Sensor response | I don’t know how much this is already incorporated in the simulations…
Needed to study detector response and set up, calibrate, understand ASICs.
Likely best done in dedicated detector studies.

## Slide 5
Electronics overview with respect to digitization
List of electronics models:
Detector(s) | ASIC | Similarities | Differences
Encap TOF, B0, RP, OffM, | EICROC | Same Data Format / Digital Operation | Different Organization, but similar responses…
Hadronic Calorimeters | CALOROC |  | Different Organization, different detector responses…?
Barrel ECAL | CALOROC |  | Z position calculated from times &/or Astopix matching
Barrel TOF, pfRICH, hpDIRC | FCFD |  | Different Organization, Different spatial connection to physical hits
dRICH | ALCOR | Unique | Unique
Cymbal / Barrel / Endcaps MPGD | SALSA | Same | Similar responses
Backward / Forward Ecal | Discrete |  | Similar responses
Direct Photon | Discreet | Unique | Digitized data will be summarized by DAQ
SVT, B0 | ITS3 | Same | Same
Imaging Calorimeter | Astropix | Unique | Unique
LowQ2 | Timepix | Unique | Unique