## Slide 1: 27th Accelerator Test Facility (ATF) Users' Meeting LWIR Laser Status and Upgrades
Misha Polyanskiy
2025-05-01
Accelerator Facilities Division

## Slide 2: Overview & Statistics Recent System Developments Near-Term Improvement Plans Strategic Outlook

## Slide 3
Polyanskiy et al. OSA Continuum 3, 459 (2020)
Gas
Solid state
ATF’s 5 TW LWIR laser

## Slide 4
---------------------------------------------------------------------
Typical* Extreme** --------------------------------------------------------------------- Central wavelength 9.22 μm Pulse duration 2 ps Pulse energy in IP 5 J 10 J Peak power in IP 2.5 TW 5 TW Shot-to-shot delay 90 sec 20 sec
---------------------------------------------------------------------
LWIR Spec Sheet v.2025
* Typical
Proven reliable operation. Recommended for most experiment designs.
** Extreme
Demonstrated performance. Can be attempted in limited number of shots. Not guaranteed.

## Slide 5
Shot statistics
User mtg. 2024
AE-100
AE-138
AE-119
AE-127
AE-132
AE-134
3,500 shots
Summer down

## Slide 6: Overview & Statistics Recent System Developments Near-Term Improvement Plans Strategic Outlook
Goals
Ramp up delivered energy
Improve beam quality
Increase system reliability

## Slide 7
Shot logger
Asynchronous and Expandable Logging Scheme
Each HV discharge in the final amplifier triggers the shot counter
“Log master” script monitors the shot counter; upon update:
  Creates an HDF5 file
  Emits a ZMQ signal with the file name
Each instrument’s “Logger” script writes its data to the HDF5 file
Flexible Data Types Currently supported:
Float (e.g., energy, charge voltage)
Bitmap (e.g., scope screenshot)
Text (e.g., experiment ID, notes)
Data Storage
All data is stored on a dedicated NAS server
Unique ID is assigned to every shot
One file / shot
“Log display” GUI
“Log master”
Instrument “Loggers”

## Slide 8
NaCl → BaF2 transition
Amplifier output
One window
Two windows
25 m
NaCl windows tend to degrade beam quality
Gradual degradation of surface quality upon contact with the atmosphere.
Permanent crystal lattice shift caused by even moderate mechanical stress
Parameter (at 9.2 μm) | Unit | NaCl | BaF2
Solubility in water | g/L | 360 | 1.61
Modulus of rupture | MPa | 2.4 | 26.9
Refractive index | - | 1.500 | 1.412
Fresnel reflection | % | 4.0 | 2.9
Volume absorption | % / cm | 0.0 | 2.8
Nonlinear index | 10-20 m2/W | 3.5 | 1.7
Group-velocity dispersion | fs2/mm | -1010 | -2340
Compressor input
vacuum
38 mm → 14 mm
Amplifier output high pressure
100 mm → 35 mm

## Slide 9
P(CO2) 0.5 → 0.6 bar
Good discharge P(CO2) = 0.7 bar
Arc (during conditioning)
Old Gas Composition – Final Amplifier
P(CO2) = 0.50 bar | P(N2) = 0.25 bar | P(He) = 7.50 bar Role of He: buffer gas for discharge stabilization
Improvements Over The Years
Repeated cleaning of the pressure vessel interior
Added particle filter in gas circulation loop (removes dust from discharge)
Reduced outgassing by pumping with turbo pump overnight at each vessel refill
Switched to fully DI water in H2O capacitor tank with HV spark-gap optimization
Introduced “threaded” electrode-supporting insulator to prevent surface discharge
Replaced diffusion pump with a turbo in the pre-ionizer chamber
Optimized dry-air pressure in Marx generator spark-gaps:
  Lower, adjustable pressure in actively triggered SG1
  Higher, constant pressure in self-triggered SG2–SG10
Implemented 90-second delay between shots for spark-gap purge and cooldown
New Gas Composition – 2025 Run Campaign
P(CO2) = 0.60 bar | P(N2) = 0.25 bar | P(He) = 7.40 bar
Expected Outcome
20% higher gain and stored energy, or improved reliability at reduced voltage

## Slide 10: Overview & Statistics Recent System Developments Near-Term Improvement Plans Strategic Outlook
Goals
Ramp up delivered energy
Improve beam quality
Increase system reliability
Provide post-compressed pulses to early-adopter experiments

## Slide 11
Working wish-list (items to tackle as time / resources allow, no fixed order or hard deadlines)
BaF2 windows for the regen section and at the final-amplifier input
Small in-air plasma shutter separating the regen from the final amplifier
Bypass for the “big” plasma shutter (remove potential beam distortion with two off-axis parabolas)
Herriott-cell (“zig-zag”) optical arrangement for the regen
New mount for the lower periscope mirror in the compressor chamber
Target deployment: 2025
Post-compressor pulse shortening: 2 ps → 500 fs (Part of AE-138)
Ongoing work & near-term plans

## Slide 12
560 fs
2 ps
Compressed
Input
R&D in progress: Deployment in 2025
Polyanskiy et al. Opt. Express 29, 31714 (2021)
Pogorelsky et al. Front. Phys. 12, 1390225 (2024)

## Slide 13: Overview & Statistics Recent System Developments Near-Term Improvement Plans Strategic Outlook
Goal
Develop and deploy a next-generation LWIR laser system:
  Few-cycle pulse duration
  Hz-level repetition rate
  24/7 operation capability

## Slide 14
Power (TW)
500 fs 15 TW
100 fs 25 TW
Now (10 µJ seed)
10 mJ seed
Post-compression
Gain spectrum
9P
9R
2 ps 5 TW
1 optical cycle = 31 fs
With 20% contingency
9.2 μm
9.3 μm
Roadmap for pulse shortening
Polyanskiy et al. Photonics 8, 101 (2021)

## Slide 15
Optical pumping: Now within reach!
O C O
O C O
O C O
Stenersen & Wang IEEE J. Quant Electron. 25, 147 (1989)
Tovey et al. Appl. Opt. 21, 5756 (2019)

## Slide 16
Next-generation multi-TW LWIR laser architecture
MASTER OSCILLATOR
Requirements:
  10 mJ, 300 fs , 9.3 µm
High efficiency
  not critical
Cr:ZnS(ZnSe)
147 mJ, 126.7 fs reported in China Lu et al. Optica 10, 1567 (2023)
Two 1-TW systems “100 mJ; 100 fs” under construction in Germany & US
ZGP crystals
Domestic supplier available (BAE)
POWER AMPLIFIER
Requirements:
  >100 J, <100 ns , 1.44 µm
  (can be in multiple beams)
High efficiency
  very desirable for future practical applications
Nd:YAG
High energies achievable
e.g., NIF: 20 kJ per beam, 20 ns,
OPO
Large KTA crystals, e.g., 20x20 mm available, larger crystals can be grown.
ALL CRITICAL TECHNOLOGIES ARE AVAILABLE
1.44 µm

## Slide 17: Overview & Statistics Recent System Developments Near-Term Improvement Plans Strategic Outlook
Routine delivery of 2—3 TW
Ramping-up energy and improving reliability
Next-generation LWIR laser:
  Femtosecond
  Optically pumped
  Based on existing technologies
Thank you, ATF Team, Users & Sponsors!
QUESTIONS?