## Slide 1: 27th Accelerator Test Facility (ATF) Users' Meeting NP-318747: Efficient and Stable Acceleration of Electrons in Laser Wakefield Accelerators
Accelerator Facilities Division
N. Vafaei-Najafabadi1,2, W. Li1*, N. Pathak2, A. Jain2, R. Zgadzaj3, Z. Ouyang3, M. Downer3, A. Gaikwad2, B. Romasky2, E. Trommer2, M. Babzien1, M. Polyanskiy1, I. Pogorelsky1, M. Palmer1
1Brookhaven National Laboratory
2Stony Brook University
3University of Texas at Austin
*PI
Funding received: Department of Energy (Accelerator Stewardship) Grant DE-SC0024277

## Slide 2: LWFAs Offer a Compact Path Toward TeV-Scale Colliders.
C. Benedetti, Linear colliders based on laser-plasma accelerators, 2022, arXiv:2203.08366 [physics.acc-ph]
Notes: Visual choices: high fields of lwfa/colliders

## Slide 3: Key Parameter Considerations for Collider Applications
For a specified center-of-mass energy and luminosity (set by desired collision rates), the required beam power is
Beam charge High charge
LWFA Collider: nC
PWFA Collider:
Emittance, nm
Energy spread, 1%
Focusability low emittance and energy spread
Efficiency
Efficient acceleration is critical for keeping wall-plug power manageable.
E. Esarey, C. B. Schroeder, 2021 International Workshop on Future Linear Colliders

## Slide 4: Beam Loading of nC-scale charge at High Efficiency in Blowout Regime
A trailing beam with a trapezoidal density profile result in flattening of the wakefield.
M. Tzoufras, Physics of Plasmas 16, 056705 (2009)

## Slide 5: Stability: The Critical Weakness in an Otherwise Compelling Solution
Based on short-range wakefield theory, this paper proposed a limit on the combination of low energy spread, efficient acceleration, and transverse stability in plasma accelerators
V. Lebedev, Phys. Rev. ST Accel. Beams 20, 121301 (2017)
A proxy for efficiency
F is desired
Amplitude growth

## Slide 6
This proposal seeks to experimentally examine the short-range wakefield underlying the theoretically proposed connection between low energy spread, efficient acceleration, and transverse stability

## Slide 7: ATF Facilities Are Ideal For Carrying Out This Experiment – Suitability of LWIR Laser
= 0.8 um, 25 TW, 30 fs
ne = 2e19 cm-3
= 10 um, 25 TW, 500 fs
ne = 1e16 cm-3
LWIR CO2 laser drives plasma wakefield efficiently at low density, creating large structures that are highly suitable for injection experiments
Courtesy of Gennady Shvets
Courtesy of Gennady Shvets

## Slide 8: ATF Facilities Are Ideal For Carrying Out This Experiment – Growth of e-beam Oscillation Amplitude During Acceleration
The instability grows along the beam and is a function of tilt in the beam.
Electron energy correlation with position within the wakefield may allow for mapping of slice positions
Laser: , ps, , , Power = 20 TW, cm-3
e-beam: , , , linear tilt:
Z=5mm

## Slide 9: Experiment Layout

## Slide 10: Experimental Milestones
Year 1
Investigation of short-range wake physics in LWFA in simulations
LWFA Characterization – AE 136 experiment
Electron beam Compression and focusing – design and implementation
Year 2
Tilt Characterization
Alignment and Synchnorization between CO2 and e-beam in a longitudinal configuration
First experiments: Commissioning diagnostics and attempt to observe the instability
Year 3
Experimental characterization of short-range wake function (and BBU) at various energy spread and efficiency values

## Slide 11: Developing Theory: Current Theories for Short Range Wakefield in LWFA are Inadequate
G. Stupakov, Phys. Rev. Accel. Beams 21, 041301 (2018)
V. Lebedev, Phys. Rev. ST Accel. Beams 20, 121301 (2017)
SBU (unpublished)

## Slide 12: Electron Beam Compression Design to Achieve

## Slide 13: Electron Beam Compression
Beam direction

## Slide 14: Electron Beam Focusing to is still Under Investigation
Without Beamline Modification
With Beamline Modification
Our simulations show beam size without beamline modifications. Achieving sub beam waist might require beamline modification (i.e. moving components) – under discussion with ATF team

## Slide 15
Achromatic
Objective
bandpass
filters
Si
beam
splitters
COTR
COTR
450
800 nm
750
700
680
630
500
400
Laser Pulse
Gas
Nozzle
Electron
Spectrometer
COTR foil
e-beam
Gas Jet
400
200
10
pC/MeV-mrad
0
0.5
Down-ramp
STII
self
Electron Energy (MeV)
0.25
0
-10
10
Divergence (mrad)
0
-10
10
0
-10
10
Self
STII
Down-ramp
0
1
Normalized COTR fluence
0.5
50 µm
Multi-spectral COTR imaging:
experimental setup and data
2 Self-Truncated Ionization Injection:
[Mirzaie, Sci. Rpts. 5, 14659 (2015)]
1 Schmid, PR-STAB 13, 091301 (2010)
1
2
Dichroic
COTR imaged
from foil surface
to each of 8
𝜆-filtered CCDs
LaBerge et al.,”Revealing the 3D structure of LPA e-bunches,”
Nat. Photonics 18, 952 (2024).
Max LaBerge
UT-PhD 2022
22
OTR images recorded
in a spectral range in
which OTR transitions
from fully coherent
(longer 𝜆) to fully inco-
herent (shorter 𝜆), thus
providing maximum
structural information.

## Slide 16
3D Snapshot of Downramp-Injected LWFA e-bunch
How do we know this solution is unique?
reproduces COTR data
Q ≈ Qm
Q negative
longitudinal profile
• not separable [i.e.
• not symmetric
✓
✓
✓
✓
✓
Measured
COTR
Calculated
COTR
Check list:
23
• Reconstruction algorithm was run hundreds of
times with randomly-varied initial parameters.
• The resulting cluster of reconstructions reveals
reproducible common characteristics.
• The cluster-averaged structure reproduces the
COTR data with fidelity equivalent to individual
reconstructions, providing a quanitative
“uniqueness” evaluation.
Single-shot reconstruction!

## Slide 17: Questions?

## Slide 18
Expected Experimental Regimes with 5 TW Laser Pulse
“Classic” Blowout Regime
Primarily used in LWFA research at
High acceleration and focusing fields
Structure radius ~ 200
“Wakeless” Blowout Regime ()
Onset of “Forced” LWFA
High focusing fields only
Structure radius ~ 50

## Slide 19: Changing e-Beam Current Modifies Both Energy Spread and Efficiency
Calculations of based on 1D nonlinear LWFA theory
Laser: , ps, , cm-3

## Slide 20: Electron Beam Parameters Used in Compression Design
Initial electron beam parameters | 
Energy | 55 MeV
Normalized emittance | 1 mm-mrad
Beam charge | 200 pC
std(tau) / sigma_tau [ Pulse length (fwhm) ] | 0.25 mm [ 0.552 mm ]
std(p) / sigma_p [ with Energy chirp ] | 3.0e-4 [ 1.98 GeV/m ]
beta_x | 2
beta_y | 2
alpha_x | 0
alpha_y | 0

## Slide 21: Leveraging Wavelength Scaling
Courtesy of Michael Downer (UT Austin)
ne ≈ 5 × 1018 cm-3
ne ≈ 2 × 1016 cm-3
λ [µm]:
1 (NIR)
10 (LWIR)
τ [fs]:
30
30
w0 [µm]:
8
8
Laser Energy [J]:
0.7
0.007
λ [µm]:
1
10
τ [fs]:
500
500
w0 [µm]:
120
120
Energy [J]:
2500
25
0
5
10
electron density (1018 cm-3)
x = 0 mm
x = 0.3 mm
x = 0.6 mm
(τ ≈ 1 cycle)
(w0 < λ)
(impractical)
not previously demonstrated
Max e- energy gain [GeV]:
0.6
Max e- energy gain [GeV]:
1.6
Pogorelsky et al., Plasma Phys. Control. Fusion 58, 034003 (2016).
Driving the wake efficiently requires laser size and field strength matched to plasma wavelength
Notes: Read tag line first
For example at two different densities shown here, you need to match the pulse length and spot size to these values

## Slide 22
Courtesy of Michael Downer (UT Austin)
Large Bubble Size Makes Injection Feasible
0
5
10
electron density (1018 cm-3)
x = 0 mm
x = 0.6 mm
ne ≈ 5 × 1018 cm-3
Vinjection determined by:
• e-bunch compressibility & focusability
0
100
-100
y (µm)
ne ≈ 2 × 1016 cm-3
* Xu et al., PR-STAB (2014)
injection
point
after
acceleration
Notes: The bubble sizes at two densities are not equal and if scaled, it looks something like this

## Slide 23
Electron Beam Requirements
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | Nominal
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | 0.2-0.5 nC
Bunch Length | ps | 1-10 | Bunch charge & emittance vary with length | Varied as part of experiment
Peak current | A | 100 | Variable with bunch charge and length | Varied as part of experiment
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | Varied as part of experiment (down to 60 fs)
Focused transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | Down to 10 micron
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | nominal
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | nominal
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | Single Bunch

## Slide 24
CO2 Laser Requirements
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regen. Amplifier | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 2-3 | Up to 5 TW operation will be available in a limited number of shots upon the user's request. | Max available
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 | 3-year development effort to achieve <500 fs at >10 TW and deliver to users is in progress. | Min available
 | Pulse Energy | J | ~5 | 10J will be available in a limited number of shots upon the user's request. | Max available
 | Strehl Ratio | --- | ~0.5 | Recommended conservative estimate subject to verification. | nominal
 | Repetition Rate | Hz | 0.01 | Burst operation at up to 0.05 Hz for a limited period is possible upon user’s request. This regime should be avoided to extend the lifetime of the HV spark gaps in the amplifier’s PFN | nominal
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | Linear

## Slide 25
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II should be available summer 2025 | N/A
FWHM Bandwidth | nm | 20 | 13 |  | N/A
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | N/A
Chirped FWHM Pulse Width | ps | 50 | 50 |  | N/A
Chirped Energy | mJ | 10 | 200 |  | N/A
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | N/A
Energy to Experiments | mJ | >4.9 | >80 |  | N/A
Power to Experiments | GW | >100 | >1000 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | N/A
Energy | mJ | 100 |  | N/A
Pulse Width | ps | 14 |  | N/A
Wavelength | nm | 532 | Frequency doubled | N/A
Energy | mJ | 0.5 |  | N/A
Pulse Width | ps | 10 |  | N/A

## Slide 26: Special Equipment Requirements and Hazards
Electron Beam
  Please indicate any special equipment that you expect to need, including (but not limited to) the transverse deflecting cavity, shaped bunch using mask technique, plasma capillary discharge system, bolometer/interferometer setup etc.:
CO2 Laser
  Please note any specialty laser configurations required here:
Ti:Sapphire and Nd:YAG Lasers
  Please note any specialty non-CO2 laser configurations required here:
Hazards & Special Installation Requirements
  Large installation (chamber, insertion device, etc.):
  Cryogens:
  Introducing new magnetic elements:
  Introducing new materials into the beam path:
  Any other foreseeable beam line modifications: