## Slide 1
AE-137: Toward bubble-regime
CO2-laser-driven wakefield acceleration
ATF User’s Meeting
30 April 2025
PI: Mike Downer, University of Texas at Austin
Collaborators:
University of Texas at Austin:
Faculty: M. C. Downer
Research Scientist: R. Zgadzaj
PhD students: Y. Cao, B. Dinh
Stony Brook University:
Faculty: Navid Vafaei-Najafabadi
Roman Samulyak
V. N. Litvinenko
Postdoc: N. Pathak, W. Li
PhD Students: A. Cheng, A. Gaikwad,
B. Romasky, E. Trommer
Brookhaven NL:
ATF Director: M. A. Palmer
Research Scientists: M. Babzien,
M. Fedurin, R. Kupfer, K. Kusche,
W. Li, I. V. Pogorelsky,
M. N. Polyanskiy
Main Group Funding: US Department of Energy grant DE-SC0014043 (received thru 2025, renewal pending)
Additional Individual Support: DE-SC0011617 (UT-Austin); DE-SC0012704 (BNL)
1
UCLA:
Faculty: C. Joshi
Yuxuan Cao, PhD student
Dr. Rafal Zgadzaj

## Slide 2
Goal: develop LWFAs that routinely produce e-beams
with ∆Ee/Ee and ℇn low enough to drive XFELs
The AE-137 Project builds upon AE71 and AE95 success.
1) Large plasma bubbles (Rb ≳ 0.3 mm)
⇒ ne ≲ 1016 cm-3
2) External injection of low ∆Ee/Ee, low ℇn e-bunches
Key ingredients:
*
**
**
Synchronized, compressed ATF linac bunches uniquely enable 1st-generation experiments.
Efficiently excited by LWIR laser pulses uniquely realizeable at ATF
*
• Pogorelsky et al., Phys. Rev. Accel. Beams 19, 091001 (2016);
Kumar et al., Phys. Plasmas 28, 013102 (2021)
Project # | CO2 laser parameters | Main results
AE-71 | 2 J, 4 ps, 0.5 TW, 10.3 µm | • Generation, characterization of self-modulated (SM) wakes. No electrons.
AE-95 | 4 J, 2 ps, 2 TW, 9.2 µm | • Self-injected MeV electrons produced at ne ≳ 3 × 1016 cm-3 • Quasi-monoenergetic, collimated features observed.
AE-137 | 5-20 J, < 2 ps, 5-20 TW | • Excite, characterize Rb ~ 0.3 mm bubbles at ne ~ 1016 cm-3 w/o self-injection • Inject e- from ATF linac, characterize ∆Ee/Ee and ℇn
[1] Predicted by Kumar et al., Phys. Plasmas 26, 083106 (2019)
[1]
[2] Zgadzaj et al., Nat. Comms. 15, 437(2024)
[2]
2

## Slide 3
Discovery of the “bubble” regime and “quasi”-monoenergetic “dream” beams
was an occasion for community-wide celebration...
Before 2004:
After 2004:
Leemans, Nat. Phys.(2006)
Energy Gain (MeV)
1000
500
0
250
500
0
pC GeV-1
sinusoidal wake
Review: Esarey, Rev. Mod. Phys. 81, 1229 (2009)
E = 1 GeV
∆E/E = 5 %
θdiv = 5 mrad
Q ~ 0.03 nC
tbunch < 10 fs
Ipeak ~ 10 kA
... but improving on ∆E/E ~ few % since 2004 has proven challenging.
0
5
10
electron density (1018 cm-3)
Kalmykov (2009)
x = 0 mm
Kalmykov (2009)
x = 0.3 mm
Kalmykov, Shvets PRL (2009)
x = 0.6 mm
plasma bubble
Pukhov and Meyer-ter-Vehn, Appl. Phys. B 74, 355 (2002); Kostyukov, Phys. Plasmas 11, 5256 (2004)
Geddes, Nature (2004)
Faure, Nature (2004)
Mangles, Nature (2004)
3
...in 2004.
Notes: Lead-in: One of the most important discoveries along the 20-year path to mature TW-LPA was that the quasi-linear sinusoidal waves depicted in the previous slide produced electrons with wide energy spread, because of the difficulty of injecting electrons into the wave with sub-plasma-wavelength precision.
• In 2004, we learned that a highly nonlinear regime in which the drive pulse creates an electron density “bubble”, in a remarkable act of self-organization, gives rise to highly mono-energetic electrons up to 1 GeV in energy, as depicted here.

## Slide 4
The conventional approach to monoenergetic plasma acceleration
is based on longitudinal beam-loading by a nC injected bunch
Tzoufras et al., “Beam loading in the nonlinear regime of plasma-based acceleration,” Phys. Rev. Lett.101, 145002 (2008)
with
beamload
w/o beamload
required field-flattening charge
value of flat field
bubble radius
⇒
⇒
Promising for high-Q monoenergetic acceleration...
... but challenging to achieve at ATF in the short term.
4

## Slide 5
Chirped Bunch Acceleration (CBA)
+ Plasma Compression (PC)
Yuxuan Cao, PhD student
Electron energy (MeV)
laser: E = 30 J,
Propagation distance z (mm)
Normalized emittance (µm)
minimal emittance
growth
plasma:
matched focus: ;
injected e-: 10 pC; div;
20µm behind laser peak
Electron
Energy
Chirp
new 2025 simulations
with FB-PIC
5
CBA
PC

## Slide 6
SPACE simulations predicted electron injection
and acceleration for PL = 2 TW (4 J, 2 ps) CO2 pulses
Zgadzaj et al., Nat. Commun. 15, 4037 (2024)
PL = 2 TW (4 J, 2 ps)
MeV
ne = 5 × 1017 cm-3
~ 75 mrad
e- output
Q ≈ 50 pC
6
simulations by A. Cheng & R. Samulyak
pz from trapped,
accelerated e- observed
above e- injection threshold
simulations by...
Prof. Roman Samulyak
Aiqi Cheng
0
2
1
z (mm)

## Slide 7
CO2 pulse
2-5 J, 2ps
H2
jet
Lanex
7
CCD
e-
integrated luminescence
⇒ total charge Q
Detection and Characterization of
relativistic electron beams
P appearance thresholds
⇒ all are sub-Pcr
appearance thresholds
⇒ all are relativistic
Qmax ≈ 500 pC
For 2 TW pulses,
self-focusing no
longer essential
to trigger LWFA.
Zgadzaj et al., Nat. Comms. 15, 437 (2024)

## Slide 8
Electron energy spectra have
2 corresponding components
CO2 pulse
2-5 J, 2ps
H2
jet
Lanex
CCD
magnet
12
ne = 4 × 1017 cm-3
*
*
*
SM-LWFA → bubble regime
Collimated quasi-monoenergetic
e-spectral features
*
⇒ transition from
Zgadzaj et al., Nat. Comms. 15, 437 (2024)

## Slide 9
Laser focus at 0mm E=5J, a0=3.5,
FWHM = 2ps, w0=27.5um,
Wavelength=9.2um
New FB-PIC simulations have confirmed self-injection thresholds and
energy spectral in Self-Modulated LWFA Expts.

## Slide 10
This is the waterfall plot of externally injected electron cylinder with 10MeV energy. Injected bunch energy spectrum vs z position. Portion of energy below 10MeV signifies energy loss.
Electrons within highlighted green rectangle corresponds to highlighted green bunch in the animation on the previous slide; Energy of these small bunch is above 36MeV. (26MeV energy gain)
Laser focus at 0mm E=5J, a0=3.5,
FWHM = 2ps, w0=27.5um,
Wavelength=9.2um
New FB-PIC simulations have generated predictions for 1st-generation ATF
experiments: external injection
into SM-LWFA

## Slide 11
Achromatic
Objective
bandpass
filters
Si
beam
splitters
COTR
COTR
450
800 nm
750
700
680
630
500
400
Laser Pulse
Gas
Nozzle
Electron
Spectrometer
COTR foil
e-beam
Gas Jet
400
200
10
pC/MeV-mrad
0
0.5
Down-ramp
STII
self
Electron Energy (MeV)
0.25
0
-10
10
Divergence (mrad)
0
-10
10
0
-10
10
Self
STII
Down-ramp
0
1
Normalized COTR fluence
0.5
50 µm
Multi-spectral COTR imaging:
experimental setup and data
2 Self-Truncated Ionization Injection:
[Mirzaie, Sci. Rpts. 5, 14659 (2015)]
1 Schmid, PR-STAB 13, 091301 (2010)
1
2
Dichroic
COTR imaged
from foil surface
to each of 8
𝜆-filtered CCDs
LaBerge et al.,”Revealing the 3D structure of LPA e-bunches,”
Nat. Photonics 18, 952 (2024).
Max LaBerge
UT-PhD 2022
22
OTR images recorded
in a spectral range in
which OTR transitions
from fully coherent
(longer 𝜆) to fully inco-
herent (shorter 𝜆), thus
providing maximum
structural information.

## Slide 12
3D Snapshot of Downramp-Injected LWFA e-bunch
How do we know this solution is unique?
reproduces COTR data
Q ≈ Qm
Q negative
longitudinal profile
• not separable [i.e.
• not symmetric
✓
✓
✓
✓
✓
Measured
COTR
Calculated
COTR
Check list:
23
• Reconstruction algorithm was run hundreds of
times with randomly-varied initial parameters.
• The resulting cluster of reconstructions reveals
reproducible common characteristics.
• The cluster-averaged structure reproduces the
COTR data with fidelity equivalent to individual
reconstructions, providing a quanitative
“uniqueness” evaluation.
Single-shot reconstruction!

## Slide 13
AE-137 SUMMARY
Year 1-accomplishments:
2) Achieved good simulation-experiment agreement w/ current ATF parameters
2) Strengthened optical wake diagnostics for ne ~ 1016 cm-3 plasma
1) Discovered a chirped-beam acceleration/plasma-compression regime
- achieves acceleration to ~0.5 GeV with sub-% ∆E seen so far in simulations
- appears compatible with current ATF parameters
- using machine-learning algorithms to hasten search for optimum laser-plasma parameters
1) External e—injection into bubble-regime CO2-laser-driven LWFA.
improved CTS, Faraday probes; MIR harmonics of CO2 drive pulse
developed single-shot COTR-based diagnostic of ultrashort e-bunches (LaBerge, Nat. Phot. (2024))
• take advantage of CO2 power upgrades & e-beam synchronization/compression advances
• leverages Navid’s work in developing e-beam probes
• a preparatory “Mercury” mission to build experience for a future “Apollo” moon-landing mission
10
self-injection threshold
simulations of 1st generation experiments completed: external injection into self-modulated wakes
Over-arching goal:

## Slide 14
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | Nominal (~55 MeV)
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | ~0.1 to ~1nC
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | 100 fs
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 2 mm (hor.) 0.5 mm (vert.) 0.01 mm (diameter)
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 1
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | 1.5
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | Single bunch
Electron Beam Requirements

## Slide 15
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 5 | ~5 TW operation is planned within the next year (requires further in-vacuum transport upgrade). A 3-year development effort to achieve >10 TW and deliver to users is in progress. | 2-5
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 |  | 2 or less
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | 10
 | M2 | --- | ~2 |  | ~2
 | Repetition Rate | Hz | 0.05 |  | 0.05
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | Linear
CO2 Laser Requirements

## Slide 16
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800
FWHM Bandwidth | nm | 20 | 13 |  | 20
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 50
Chirped FWHM Pulse Width | ps | 50 | 50 |  | N/A
Chirped Energy | mJ | 10 | 200 |  | N/A
Compressed Energy | mJ | 7 | 100 |  | 5
Energy to Experiments | mJ | >4.9 | >80 |  | 5
Power to Experiments | GW | >98 | >1067 |  | 100
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | N/A
Energy | mJ | 5 |  | N/A
Pulse Width | ps | 14 |  | N/A
Wavelength | nm | 532 | Frequency doubled | N/A
Energy | mJ | 0.5 |  | N/A
Pulse Width | ps | 10 |  | N/A

## Slide 17
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 0
Laser* Only (in FEL Room) |  | 0
Laser* + Electron Beam | 80 | 240
CY2025 Time Request
Experimental Time Request