## Slide 1: 27th Accelerator Test Facility (ATF) Users' Meeting AE127: Two Color Injection of Bright Electron Beams
Accelerator Facilities Division
N. Vafaei-Najafabadi1,2*, W. Li1, I. Petrushina2, R. Zgadzaj3, M. Downer3, A. Gaikwad2, B. Romasky2, E. Trommer2, M. Babzien1, M. Polyanskiy1, I. Pogorelsky1, M. Palmer1
1Brookhaven National Laboratory
2Stony Brook University
2University of Texas at Austin
*PI
Funding received: National Science Foundation Grant 2238840

## Slide 2: Laser wakefield acceleration
Laser ionizes a gas, producing plasma
Ponderomotive force of laser pushes free electrons away from areas of high intensity
Positive ions are nearly stationary due to their mass
With sufficiently high laser intensity, a plasma “bubble” is created, called the wakefield
Longitudinal electric field in the wakefield can be very high, up to 100 GeV/m
Strength of ponderomotive force scales with , so using LWIR drivers is beneficial
Bubble created by LWIR driver can be up to 100 µm, compared to 10 µm for NIR drivers
The bubble can trap and accelerate some of the electrons that were ionized, but the beam quality suffers due to the stochastic nature of this process
Kumar, Optical and Quantum Electronics, (2021)
Brunetti, Scientific Reports 12, 6703 (2022)

## Slide 3: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
Schroeder, PRSTAB 17, 101301 (2014)
Instead, using a second laser, we can ionize the gas inside the plasma wake to produce electrons, resulting in a high-quality beam
Drive laser needs large to form plasma wakefield, but we want low to avoid prematurely ionizing the gas
Injector laser needs high to ionize the gas, but low to maintain low emittance
Solution: long wavelength drive, short wavelength injector:
ATF CO2 and Ti:sapphire
Low emittance
Excellent phase space
Very intense, small
Less intense, large

## Slide 4: Trapping electrons
Low gradient, electron slips behind wake
High gradient, electron trapped inside wake
The electrons start at rest, while the plasma wake is moving at ~c
Race: electrons need to be accelerated to the wake velocity before the wake leaves them behind
Minimum accelerating gradient is called trapping threshold

## Slide 5: Wakefield with current CO2 parameters
Pulse energy = 7.5 J, = 3.275, µm, ps, cm-3
Relatively high gas density: not fully blown out by CO2 laser
, not enough to trap electrons on own
How can we do ionization injection in the meantime?

## Slide 6: Ponderomotive assistance
We can use the injector laser to help!
Below figure is an e-beam driver, but the same principle applies
Ponderomotive force of injector laser at oblique angle accelerates the ionized electrons
The electrons have an initial momentum, lowering the necessary trapping potential
Zeng, New J. Phys. 22, 123003 (2015)

## Slide 7: Lower energy  higher density
Pulse energy = 5 J, = 2.675, µm, ps, cm-3

## Slide 8: Ti:Sapphire parameters
0.5
Before ATF upgrade
After ATF upgrade
Sufficient for trapping

## Slide 9: Experimental setup
LWIR pulse
NIR pulse
f/#1.5 focusing
f/#2 focusing
NIR focus diagnostic
Nozzle
LWIR focus diagnostic
Dipole
magnet
LANEX
Slit
AOI rotation
Pepperpot

## Slide 10: 2024 run
Encountered and overcame several challenges (broken motorized stages, HVAC issues, etc.)
Used this run as a “test run” for developing alignment techniques and finding issues to fix before the next run
Able to align OAP and achieve small spot with purely manual stages: will have working motorized stages for next run

## Slide 11: Preliminary alignment tests
515 um pin
10 um Ti:Sa focus

## Slide 12: Conclusion
Two-color ionization injection has been shown in simulation to produce high quality electron beams
Ponderomotively assisted injection allows us to study ionization injection now
Stepping stone to experiments post-ATF upgrade to produce low emittance, high brightness beams

## Slide 13: Questions?

## Slide 14
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | 55
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | 0.2
Bunch Length | ps | 1-10 | Bunch charge & emittance vary with length | 2
Peak current | A | 100 | Variable with bunch charge and length | 
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | 
Focused transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | 
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | 
Electron Beam Requirements

## Slide 15
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regen. Amplifier | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 2-3 | Up to 5 TW operation will be available in a limited number of shots upon the user's request. | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 | 3-year development effort to achieve <500 fs at >10 TW and deliver to users is in progress. | 2
 | Pulse Energy | J | ~5 | 10J will be available in a limited number of shots upon the user's request. | 7.5 - max
 | Strehl Ratio | --- | ~0.5 | Recommended conservative estimate subject to verification. | 
 | Repetition Rate | Hz | 0.01 | Burst operation at up to 0.05 Hz for a limited period is possible upon user’s request. This regime should be avoided to extend the lifetime of the HV spark gaps in the amplifier’s PFN | 
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | 
CO2 Laser Requirements

## Slide 16
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II should be available summer 2025 | 
FWHM Bandwidth | nm | 20 | 13 |  | 
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 70
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 
Energy to Experiments | mJ | >4.9 | >80 |  | 30
Power to Experiments | GW | >100 | >1000 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 100 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 17: Special Equipment Requirements and Hazards
Electron Beam
  No special requirements
CO2 Laser
  No special requirements
Ti:Sapphire and Nd:YAG Lasers
  No special requirements
Hazards & Special Installation Requirements
  Compressed gas: krypton for gas jet
  Static magnetic field: electron spectrometer

## Slide 18: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) |  | 
Laser* + Electron Beam | 40 | 80
CY2025 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) |  | 
Laser* + Electron Beam | 80 | 160
* Laser = Near-IR or LWIR (CO2) Laser
Total Time Request for the Experiment remaining duration