## Slide 1: 27th Accelerator Test Facility (ATF) Users' Meeting AE108: Development of wavelength conversion techniques for generation of coherent radiation at the XUV to LWIR
April 29th, 2025
W. Li1, R. Kupfer2, F. Wang1, J. Wishart1, M. Babzien1, M. Polyanskiy1*, I. Pogorelsky1, T. Rao1, L. Cultrera1, N. Vafaei-Najafabadi1,3, M. Palmer1
1Brookhaven National Laboratory, 2Soreq Nuclear Research Center,
3Stony Brook University, *PI
Accelerator Facilities Division
Funding: BNL LDRD-21-001 and U.S. DOE Office of Science DE-SC0012704 (received)

## Slide 2: Experimental goals
Upgrading ATF CO2 laser
  9.3 μm: better LWIR seed  shorter pulse length
  4.3 μm: optical pumping  much higher repetition rate
XUV for imaging and lithography
  HHG scales with wavelength: natural fit for ATF
  With CO2 laser, potentially extend to zeptosecond hard x-rays
Seed
few mJ <500 fs 9.3 µm
10++ TW ~500 fs
Pump
100s J, < 1 µs, 4.3 µm
CO2 amplifier
Photo credit: ASML
Popmintchev, Nat. Photonics 4, 828 (2010)
CO2 laser
Accelerator Facilities Division

## Slide 3: Mid- and long-wave infrared
Commonly available lasers are limited to specific wavelengths
Generating mid- or long-wave infrared usually requires relatively inefficient OPA
Is there a better option?
Photo credit: Edmund Optics
Accelerator Facilities Division

## Slide 4: Raman + DFG
‘Cheap’ high energy laser source ωp
Raman Converter
Residual pump ωp
Converted pump ωp- ωtarget
Nonlinear crystal
Residual pump ωp
Converted pump ωp- ωtarget
ωtarget
Typical Raman shifts are on the order of 1000 cm-1
Perfect for generating LWIR!
Raman Scattering 
in
out
ΔE
ωpump
ωsignal
ωDFG
Difference-frequency generation (DFG)
Accelerator Facilities Division
Diagrams adapted from Welch, Opt. Express 26, 5145-5163 (2018)

## Slide 5: Seed generation in calcite
simulated
simulated
Correct peaks
BGS suppresses TPA
Effect on CO2 laser
Red-shifts at saturation
Accelerator Facilities Division
Possibly use 2 μm pump for better DFG efficiency
Good efficiency and energy scaling

## Slide 6: Pump (4.3 μm) generation in ionic liquid
Artificial salts that are liquid at room temperature
Can be designed to have specific properties
Settled on EMIM DCA
  Transparent at pump and Stokes wavelengths
  Peak Raman cross section at desired shift
  High viscosity (suppressing Brillouin scattering)
  Good stability
Plots from Kupfer, Phys. Rev. Applied 19, 014052 (2023)
High efficiency
Good spectrum
Raman shifts of selected ILs
Accelerator Facilities Division

## Slide 7: Open questions about ionic liquids
Cost effectiveness: how much liquid is necessary?
Repetition rate?
Other viable ionic liquids?
~300 ml
~30 ml
Original tube
New tube
Accelerator Facilities Division

## Slide 8: Ionic liquid test stand
Runs in parallel with Ti:S operations
Accelerator Facilities Division
Nd:YAG
(2nd harmonic)
Ionic liquid tube
Diagnostics

## Slide 9: Repetition rate scaling
Glass tube saturates quickly at 12 Hz, compared to metal tube
Significant improvement at 1 Hz
Thermal effects: thermal conductivity of EMIM-based ionic liquids is around 0.2 W/m·K* (water is about 0.6 W/m·K)
For high repetition rates, need active cooling
*Fröba, Int. J. Thermophys. 31, 2059-2077 (2010)
Accelerator Facilities Division

## Slide 10: Alternative ionic liquids
Now testable due to smaller requisite volume
~2200 cm-1 Stokes shift
  BenzMIM DCA, EMIM TCM: absorption at 532 nm too high
  No visible Stokes peak/burned liquid
~1000 cm-1 Stokes shift
  BuPy NTf2
  Low conversion efficiency
Accelerator Facilities Division

## Slide 11: EMIM DCA + LiNbO3 MIR generation

## Slide 12: High harmonic generation
Popmintchev, Science 336, 1287-1291 (2012)
Intense laser field tunnel ionizes gas
Free electron is ponderomotively pushed away from ion
Laser field changes sign and electron collides with ion
Ponderomotive nature of interaction causes longer pump wavelengths to lead to shorter harmonic wavelengths
Popmintchev, Nat. Photonics 4, 828 (2010)
Accelerator Facilities Division

## Slide 13: HHG apparatus
Full HHG apparatus
Gas cell schematic
Kr, Ar
Accelerator Facilities Division
Ti:S
XUV

## Slide 14: HHG commissioning
First HHG signal observed
Spectrometer camera had problems, manufacturer identified problem and repaired
Accelerator Facilities Division

## Slide 15: Conclusion
Successfully demonstrated proof-of-principle generation of MIR light with Raman conversion + DFG
Characterized utility of ionic liquids for wavelength conversion
Demonstrated proof-of-principle high harmonic generation for XUV wavelengths

## Slide 16: Products delivered
Journal publications
  R. Kupfer, F. Wang, J. F. Wishart, M. Babzien, M. N. Polyanskiy, I. V. Pogorelsky, T. Rao, L. Cultrera, N. Vafaei-Najafabadi, M. A. Palmer, “Raman Wavelength Conversion in Ionic Liquids”, Physical Review Applied 19, 014052 (2023)
Conference proceedings:
  W. H. Li, R. Kupfer, M. Babzien, L. Cultrera, M. N. Polyanskiy, I. V. Pogorelsky, T. Rao, N. Vafaei-Najafabadi, F. Wang, J. F. Wishart, and M. A. Palmer. "Raman Conversion in Calcite Crystals for Seeding CO2 Lasers," CLEO: Fundamental Science, San Jose, CA (USA), May 7-12, 2023
  W. H. Li, M. Babzien, M. Palmer, I. Pogorelsky, M. Polyanskiy, N. Vafaei-Najafabadi, F. Wang, and J. Wishart, “Optical Pump Generation for Long-wave Infrared Lasers for Advanced Acceleration”, International Particle Accelerator Conference, Nashville, TN, May 19-24, 2024
Conference presentations:
  R. Kupfer, F. Wang, J. F. Wishart, M. Babzien, M. N. Polyanskiy, I. V. Pogorelsky, W. Li, T. Rao, L. Cultrera, N. Vafaei-Najafabadi, and M. A. Palmer. "Raman Wavelength Conversions in Ionic Liquids," CLEO: Fundamental Science, San Jose, CA (USA), May 7-12, 2023
  W. H. Li, M. Babzien, L. Cultrera, R. Kupfer, I. V. Pogorelsky, M. N. Polyanskiy, F. Wang, J. F. Wishart, T. Rao, N. Vafaei-Najafabadi,, and M. A. Palmer. " Prospective methods for generating sub-picosecond long-wave infrared lasers for advanced accelerators," Physics and Applications of High Brightness Beams, San Sebastian, Spain, June 19-23, 2023
Poster presentations
  W. H. Li, M. Babzien, I. V. Pogorelsky, M. N. Polyanskiy, F. Wang, J. F. Wishart, N. Vafaei-Najafabadi, M. A. Palmer, “Optical pump generation for long-wave infrared lasers for wakefield accelerators”, Advanced Accelerator Concepts, Naperville, IL, July 21-26, 2024
Accelerator Facilities Division

## Slide 17: Questions?
Accelerator Facilities Division

## Slide 18: Backup slides
Accelerator Facilities Division

## Slide 19: EMIM DCA transmission spectrum
Problem for using Nd:YAG fundamental
Absorption peak from overtones of aliphatic C-H bonds
Deuteration should shift this peak without affecting the Stokes shift, which comes from C-N triple bonds
Accelerator Facilities Division

## Slide 20: HHG Feasibility for CO2
Simple model of HHG yield for unit interaction area and unit time given by equation
We can compare to Popmintchev, Science 336, 1287 (2012), using a 3.9 μm pump, where we target the same harmonic wavelength (~1 keV)
  Their yield was photons/shot in a bandwidth around 1 keV
goes as , but the peak power of the CO2 laser is much higher with a longer pulse length, and the optimal phase matching intensity is lower, so the interaction area is 20 times larger and the interaction time is also 20 times longer, resulting in a higher overall yield for the CO2 laser
Primary challenge will be developing a gas cell that can support the necessary pressure (several atm)
Accelerator Facilities Division