## Slide 1: 27th Accelerator Test Facility (ATF) Users' Meeting Facility Maintenance Status and Updates
Andrew Simmonds
April 29, 2025
Accelerator Facilities Division

## Slide 2: ATF Facility Maintenance Status and Updates
  Design Process
  Configuration Control
  B820
    Laser Configuration
    Capability and Safety Maintenance/Upgrades
    Facility Upgrades
  B912

## Slide 3: Design Process
  Scientific need is identified by the user community or AF staff member
  A specification document is generated
  Development of a conceptual design
  Hold design review with AF staff and relevant outside experts
  Conduct detailed design and structural analysis
  Check & approval of drawings and critical analyses
  Archival of drawings and analyses
  Utilize matrixed support from Discovery Technologies for engineering and drafting

## Slide 4: Configuration Control
  For wider accessibility, SharePoint will host a drawing repository for reference only copies of relevant drawing packages
  Radiation calculations are archived by the C-AD RSC
  Shielding is approved by the C-AD RSC. The drawings are reviewed and approved before being archived in Windchill.
  Utilize Windchill to release and archive controlled documents
  The part numbering and controlled document release process are fully AF’s responsibility

## Slide 5: Room Names

## Slide 6: Present Laser Configuration
LWIR
CPA Chamber
Seed Laser Table
Polarization Rotator Chamber
Final Amplifier
Shielding wall
NLPC 2
NLPC 1
Potential GV w/ window for LWIR alignment laser
NIR

## Slide 7: B820 Capability and Safety Maintenance/Upgrades
  LWIR Final Amplifier exit window upgraded to BaF2. Jan 2025
    Enables more favorable transmission properties.
  LWIR Water Capacitor preventative maintenance inspection.
    Previous repairs showed no signs of degradation and fluid was clear.
  NIR upstream vacuum transport upgrade. Oct 2024
  YAG laser head rebuilt after finding cracked flow tube.
  Smoke alarms installed in the NIR and LWIR Vestibules. March 2025
  Updated signage and labels throughout the facility.
  B820 high bay blue room roof insulation material changed to meet fire codes, and roof load calculations performed for maintenance areas

## Slide 8: NIR Upstream Upgrade
Vacuum transport upgraded between the NIR Clean Room and the Gun Laser Hutch
Separated the two crossing beams into their own parallel vacuum transport lines
Increased aperture to alleviate clipping issues allowing for higher power transmission

## Slide 9: Updated signage
Notes: As part of the updated ConOps we are updating our signage throughout the facility. These are the at the controls areas signifying that a capability is run from within the markings and that brings with it certain requirements.

## Slide 10: Updated signage cont’d
Notes: These gas line markings and load sign are a couple more examples

## Slide 11: Future ATF LINAC Upgrades
  Continuing focus on replacement of aging LINAC hardware (XK-5 klystron, old-style modulators, and magnet systems) and timing systems to enable a true multi-beam operations with 10s of femtoseconds resolution
Cycle- Femtosecond Class
Timing Distribution
Next Generation CAEN PS
System for ATF Magnets

## Slide 12: Future ATF LINAC Upgrades cont’d
Notes: Current design includes 2 Scandinova K300s. The first powers the gun and LINAC section 1. The second powers the second LINAC section. These would be installed on the high bay floor rather than on the mezzanine to reduce the length of waveguide. This design also aims to minimize the amount of required shielding changes to retain as short as possible installation time

## Slide 13: Updates to Areas Accessible by Users
Rolling out standard labels on key vacuum chambers
  These identify the common name as well as the drawing number where more information can be found
Due to cybersecurity and operational requirements, more doors are required to be locked. LWIR room from the High Bay, push button lock matching the Control Room
Notes: These drawings will be available on SharePoint once fully implemented.
Most notable to Users is the door into the LWIR room from the High Bay.

## Slide 14: New Machine Shop Progress
Installation Underway
  FRP wall panels installation complete. These aid in maintaining a clean shop.
  Electrical installation is underway.
  Machines are on hand awaiting installation.
Notes: At least a few more weeks on electrical installation

## Slide 15: HVAC systems
Carrier Chiller servicing the Experimental Areas
  Previously unused immersion heaters were connected and put into service.
    This should help with reducing failures.
Spare Parts Program
  Introduced in response to an unacceptable number of interruptions due to down time of the HVAC system servicing the Experimental areas.
  Spare parts are stored on site to reduce down time in the event of a failure
Notes: Recently experienced many issues with our HVAC servicing Experimental areas

## Slide 16: 3D Print Capability
BambuLab X1E
  FDM printer
  AMS material changer
Notes: Allows us an easier and faster prototyping. This is a printed foil clamp we used to practice installation of the foil for an upcoming project. We were able to quickly iterate the foil shape we start with to improve the final product much faster than with our traditional prototype machining.

## Slide 17: Background efforts
  The Engineering and Design group has been very busy updating our documentation
    Long list of older documents are being reviewed and modernized
      LINAC tunnel area
      Gun area
      Gun shielding
      Klystron area
  Radiation simulations are being performed with the new models to confirm old calculations in key areas
Notes: Modernization includes higher fidelity models & drawings

## Slide 18: ATF Summary Next Steps
FY25-26
  Major focus on further improvements in Electron Beam Performance as strongly driven by user needs
    LINAC RF system improvements
    Pulse compression (to better match with combined e-beam/laser requests)
    Short-pulse diagnostics
  Continue facility-level corrective action plans (CAPs) as developed during ARR process
    Example: Electrical Systems CAP will continue for multiple years
  Facility Upgrade Proposal – a few identified thrusts
    Path to <500 fs & >20 TW LWIR capabilities
    Dedicated shielded research space to pursue laser-only particle source experiments
    Further development of multi-beam research capabilities
      Dedicated IPs
      Improved multi-beam timing and synchronization
    LWIR rep-rate path

## Slide 19: B912 LEAD Facility
UED
  Planning for beamline extension
  Designing deployment of new highly stable solid-state modulator and klystron
AS&T Research Bunkers
  Planning installation of a new shielding penetration for S-band waveguide

## Slide 20: Questions?