## Slide 1: Integration, Installation and Infrastructure (Triple I Group)
Roland Wimmer
TIC Update

## Slide 2: Detector Model Updates
GST Workshop
Cradle Updates
Services

## Slide 3: GST Workshop
Summary
ToF
  Where do the temperature requirements come from?
  Why is it mounted at 18° angles?
  Need to make the detector more serviceable
  Should look into encapsulating wire bonds
Inner MPGD
  Need to discuss FEB mounting and overall installation onto PST
MPGD Disks
  Installation into PST should be compatible with SVT design needs
  Once installation is figured out then services routing need to be looked at
  There are temperature concerns surrounding beampipe bakeout
  Need to reinvestigate beampipe bakeout temperatures
pfRICH
  Need to float on one side to accommodate rails

## Slide 4: GST Workshop
Summary
EEEMCal
  Beampipe clearance needs to be discussed further
  ΔT across detector needs to be discussed, there are a few external factors that need to be considered
    Insulating plate needs to be looked at
  May need to include a break in the outer aluminum structure to accommodate for potential magnet quench
    True for all subsystems with a metal support frame.
SVT
  Need to figure out services routing out of the PST
  Talked about enclosing the entire detector such that heat doesn’t escape
GST
  Installation of PST and detectors into the GST needs to be looked at more
  Services routing during installation is a major concern
PST
  Beampipe support locations
  Services routing

## Slide 5: GST Workshop
Summary
Services
  Currently do not fit around EEEMCal and pfRICH
  Depending on adjustment needs, the space between the Barrel EMCal and dRICH may not be enough
Other
  Must assign interface responsibilities to individual teams
  Revisit ePIC interface control documentation with added responsibilities.

## Slide 6: Cradle Updates
New proposed cradle design
Planning on reusing the sPHENIX support webs (shown in purple and teal)
Will use new base, the old sPHENIX base wont work with our track setup
New design pros
  Incorporating 8mrad rotation will be much easier
  Much less weight due to less steel
  Magnet group had concerns about too much steel on the bottom of the detector
OLD
NEW

## Slide 7: Magnet Simulations
New cradle design
Try to get away with less steel internally in Endcaps
Due to the removal of the Flux return steel new magnet links needed to be designed
  Clearance concerns during endcap movement
  Each link weighs about ~350lbs (~160kg)
Need to see if these Links will work so services can start being routed out

## Slide 8: Services
After the recent updates there are some areas of concern
Not enough space around pfRICH and EEEMCal
Concerns regarding adjustments in-between barrel EMCal and dRICH
Services coming out at 3 & 9 O’clock from dRICH and fEMCal

## Slide 9: Backup Slides