## Slide 1
HRPPD ageing studies – points for discussion 1/2
The following questions to be discussed and agreed upon together
Reference integrated photon fluence
  Hottest region + margin
  Which is the max indicated by the simulation studies ?
  Reference integration time: 10y (=6 months) at max luminosity
  Which margin? ( a factor 5 ?)
Gain and HV setting
  Voltage at PC: do we fix it at 200 V?
  We do not know at which gain the detectors can be used
    this would require exercises of detector readout with final FEE, which have not been performed yet
  Proposal: let’s study two values corresponding to two extreme possibility:
  Min: 106 – minimum conceivable
  Max: 5 x 106 – conservative maximum
  Proposal of MCP HV setting: 2 settings per gain (exact HV-values to be determined experimentally)
  Equal HV on the two MCPs ~ 650 V from INCOM data sheet
  More gain on the second MCP, but with the first one gaining at least 0.5 x 103

## Slide 2
HRPPD ageing studies – points for discussion 2/2
Measurement strategy
  Light flux rate, proposal:
  reaching the integrated flux in 10 d
  3 intermediate pauses to check the performance + a final check
    Checking performance require a pause time between intense light application and measurements: 1 d?
  In the above hypothesis an ageing study takes 14 d
  A slower rate exercise for comparison ?
Resulting matrix
of measurements
Exercise label | Gain (in 106units) | MCP HV: balanced | MCP HV: unbalanced | Slower light flux rate
1b | 1 | x |  | 
5b | 5 | x |  | 
1u | 1 |  | x | 
5u | 5 |  | x | 
5u-slow | 5 |  | x | x