## Slide 1: HEARTS at LEIR: radiation testing of electronics for space applications
Cristopher Cortés on behalf of the HEARTS@LEIR initiative
6th Slow Extraction Workshop (SX 2025)
Oct 6 – 9, 2025 Stony Brook, NY, USA

## Slide 2: Acknowledgments
Many thanks to the CERN Knowledge Transfer team for partially funding the studies
Special thanks to R. Alemany Fernandez, T. Argyropoulus, M. Slupecki, O. Hans, D. Bodart, G. Le Godec, S. Joffe, S. Deleval, C. Mutin, A. Waets, N. Emriskova, R. Tomas Garcia, M. Jebramcik, J. Borburgh, SY-ABT-BTP group, D. Gamba, G. Khatri, R. Garcia Alia, M. Fraser, and technical groups involved

## Slide 3: Outline
Introduction and motivation
  HEARTS project
  Motivation
Low Energy Ion Ring accelerator
  CERN Ion Complex Chain
  LEIR
Resonant slow extraction from LEIR
Summary

## Slide 4: High-Energy Accelerators for Radiation Testing and Shielding
EU-funded project (2023 - 2026)
Aim: build and upgrade infrastructures in Europe for radiation testing for space exploration (mimic Galactic Cosmic Rays)
Focus
Electronics testing, shielding, and radiobiology
Consortium:
CERN, GSI, University of Padua and industrial partners (ThalesAlenia Space, Airbus, COSYLab)
Picture generated by ChatGPT

## Slide 5: HEARTS 2024-2025
Successful pilot user run at CERN, 2024
  Access to consortium partners as well as external users
  10 companies and institutions
  168 hours of beam time
Second run planned for Nov/Dec 2025
  Approx. 200 hours of beam time have been allocated

## Slide 6: Motivation
Electronics are essential in any space mission
Space sector turns to commercial-off-the-shelf (COTS) components for cost, performance and availability
Exposure to ionizing radiation from space
  can generate failures
  can be emulated by heavy ion beams available in synchrotron facilities
Picture generated by ChatGPT
Space exploration requires testing of radiobiology constraints
Amongst many other applications

## Slide 7: Motivation
A global supply gap exists in terms of availability of heavy ion beams
  Low- and standard-energies
(< 50 MeV/nucleon or < 1mm range in Silicon)
  High-energy
(> 50 MeV/nucleon or > 1mm range in Silicon)
Access can take time (approval time at NSRL is approx. 1 year)
High-energy ion supply gap
(crude estimate)
* Taken from [2] based on [3]
What comes next ?
  Take advantage of existing CERN infrastructure potential
  Middle to long term plan (>2030)
Other important key players not yet considered:

## Slide 8: Objective
Concept Design Report
  Add 2000 hours/year of high-energy ions to the global supply around 2030
High-energy ion supply gap
* Taken from [2] based on [3]
Energies from 20 to 100 MeV/nucleon
At least five ions

## Slide 9: Outline
Introduction and motivation
  HEARTS project
  Motivation
Low Energy Ion Ring accelerator
  CERN Ion Complex Chain
  LEIR
Resonant slow extraction from LEIR
Summary

## Slide 10: CERN Ion Chain Complex
Ion physics program at CERN
  LHC dedicated experiments
  SPS North Area: HiRadMat (p+ and Pb)
  PS East Area: HEARTS
Runs of approx. 5 weeks/year at LHC with ions
LEIR remains idle for most of the year and is available for exploitation
Injector complex runs approx. 9 months with ion beams:
  22 weeks in 2023
  36 weeks in 2024
  36 weeks in 2025
Higher availability of ion source, Linac3 and LEIR !

## Slide 11: Low Energy Ion Ring layout
Injection
E-cooling
Fast extraction
Slow extraction

## Slide 12: Low Energy Ion Ring
Injection
E-cooling
Fast extraction
Lead ion beams are injected at 4 MeV/nucleon
Accumulation is enabled by multi-turn injection together with e-cooling
Figure taken from [4]
Charge accumulation at LEIR

## Slide 13: Low Energy Ion Ring
Lead ion beams are injected at 4 MeV/nucleon
Accumulation is enabled by multi-turn injection together with e-cooling
Figure taken from [4]
Charge accumulation at LEIR
Upgrade the injection chain to allow fast ion switching (<15 min)
2000h of beam time (~3 months)
Duty cycle: >10%
Figure of merit:
  Time to achieve 10^7 ions / cm^2 in a 20cmx20cm irradiation field
  Always less than 1min
3 to 4 orders of magnitude of dynamic range available at user’s request
Five LET values (ions) in ~1.5 hours

## Slide 14: Outline
Introduction and motivation
  HEARTS project
  Motivation
Low Energy Ion Ring accelerator
  CERN Ion Complex Chain
  LEIR
Resonant slow extraction from LEIR
Summary

## Slide 15: Slow extraction from LEIR
Optics optimized for e-cooling
Optics optimized for RF-KO
Adjust working point near the third order resonance
Displace dispersion-wave by one sector

## Slide 16: Slow extraction from LEIR
Optics test on 26 Sept. 2025
(M. Jebramcik, T. Argyropoulus, M. Slupecki)
Courtesy of M. Jebramcik
Dispersion wave
Hor. Position (mm)
Monitor index (s-pos)
Measured tune ramp to prepare the optics
E-cooler
Slow extraction
-20-
20-

## Slide 17: Practical considerations
Fast extraction should not be impacted negatively
Septa specifications:
  E-septum
  Max. E-field < 7 MV/m
  Effective blade thickness : 200 microns
  M-Septum
  Thinnest blade in-vacuum is 5 mm
  Vertical aperture 3cm
Max. possible beam rigidity at LEIR: 6.6 Tm
Study to extract without E-Septum:
  Approx. 30% extraction efficiency
Fast kickers

## Slide 18: Practical considerations
Fast extraction should not be impacted negatively
Septa specifications:
  E-septum
  Max. E-field < 7 MV/m
  Effective blade thickness : 200 microns
  M-Septum
  Thinnest blade in-vacuum is 5 mm
  Vertical aperture 3cm
Max. possible beam rigidity at LEIR: 6.6 Tm
Study to extract without E-Septum:
  Approx. 30% extraction efficiency
Fast kickers

## Slide 19: Extraction efficiency
Beam cut-off illustration due to sextupoles strengths with resonant slow extraction optics
 | Lead ions | Oxygen ions
Emittance (mm mrad) | 0.4 | 0.3
Low energy
High energy
Emittance scales inversely proportional to the beam energy
Also proportional to the bunch intensity
(*) Emittance is RMS and normalized

## Slide 20: Extraction efficiency
Beam cut-off illustration due to sextupoles strengths with resonant slow extraction optics
Extraction efficiency for Oxygen with two different normalized emittances
Emittance scales inversely proportional to the beam energy
Emittance also scales proportionally with beam intensity

## Slide 21: Model and non-linear dynamics
Attempt to increase spiral step with large RDT amplitudes leads to the formation of stable islands in simulation
Driven by second order amplitude detuning from sextupoles and terms in the main dipole definition
Nonlinear dynamics must be characterized
(MD planned in collaboration with M. Jebramcik)
Stable island formation at LEIR
Measured beta-beating at LEIR from [5]
Systematic horizontal beating due to main bend model
Model refinement being lead by Halil Deveci and Marc Jebramcik

## Slide 22: Preliminary flattop extension test (D. Bodart, S. Deleval, G. Le Godec, T. Argyropoulos, M. Slupecki)
Evaluate the machine performance with extended flattop on 22 Sep. 2025
Validation of cooling power, power converter capabilities and magnet performance
Heating test of magnet coils: temperature measurements
Two hours test run with extended flattop
  From 0.15s to 1.5s
Time (ms)
Beam rigidity (Tm)
1.5 s

## Slide 23: Outline
Introduction and motivation
  HEARTS project
  Motivation
Low Energy Ion Ring accelerator
  CERN Ion Complex Chain
  LEIR
Resonant slow extraction from LEIR
Summary

## Slide 24: Summary
Global heavy ion supply is scarce
HEARTS at LEIR aims to close/reduce the gap
Concept design report is being developed at CERN
Machine readiness test have been planned/performed
Slow extraction optics and extraction efficiency have been evaluated

## Slide 25: Sources
https://report2024-kt.web.cern.ch/boosting-europes-space-radiation-testing-capabilities
Waets, A., García Alía, R. and Emriskova, N. Introduction to HEARTS@LEIR, 2025.
National Academies of Sciences, Engineering, and Medicine. Testing at the Speed of Light: The State of U.S. Electronic Parts Space Radiation Testing Infrastructure (2018). https://doi.org/10.17226/24993.
A. Sa Hernandez, et. al., Detailed Characterization of the LEIR Intensity Limitations for a Pb Ion Beam, in Proc. IPAC'19, Melbourne, Australia, May 2019, pp. 3196-3199. doi:10.18429/JACoW-IPAC2019-WEPTS042
F. Carlier et al., "Towards optics measurements with a new LEIR BPM system", in Proc. IPAC'23, Venice, Italy, May 2023, pp. 1644-1647. doi:10.18429/JACoW-IPAC2023-TUPA150

## Slide 26
Thanks for your attention !

## Slide 27: Extraction efficiency vs RDT
Extraction efficiency dependency on RDT strength
Extracted beam distribution in phase-space RDT=25 m^{-1/2}, Ekin=40 MeV per nucleon