## Slide 1: Slow Extraction of Mixed Ion Beams
Slow Extraction Workshop 2025 | Stony Brook, Long Island | 06-10-2025
,
Elisabeth Renner, TU Wien
David Ondreka, GSI
Andrii Pastushenko, GSI
C. Becker1, B. Galnander2, C. Graeff2, K. Holzfeind1,3, M. Kausel3, A. Mereghetti4, F. Plassard3, M. Pullia4, S. Savazzi4, C. Schmitzer3, J. Stadlmann2, L. Volz2, M. Wolf3
[1] Atominstitut, TU Wien
[2] GSI Helmholtzzentrum für Schwerionenforschung GmbH
[3] MedAustron
[4] CNAO

## Slide 2: Mixed Ion Beams for Concurrent Therapy and Monitoring
Ion beam therapy vs. conventional radiotherapy
  Improved dose conformity (Bragg peak) & higher biological effectiveness
  More sensitive to uncertainties
  Accurate treatment planning & monitoring crucial*
* Various proposals for monitoring in addition to routine regular treatment plan verification CTs: e.g. prompt gamma, nuclear fragmentation imaging, pRad,...

## Slide 3: Mixed Ion Beams for Concurrent Therapy and Monitoring
Proposal: Add small 4He2+ contribution to therapeutic 12C6+ beam for monitoring [1,2]
similar charge-to-mass ratio (≈0.5)
Extracted with similar E/m  range of 4He2+ approx. 3x larger than of 12C6+
Preliminarily aim: approx. 10% helium ions throughout the spill:
  He still distinguishable from C fragments
  acceptable dose contribution from He (~1%)
Ion beam therapy vs. conventional radiotherapy
  Improved dose conformity (Bragg peak) & higher biological effectiveness
  More sensitive to uncertainties
  Accurate treatment planning & monitoring crucial*
[1] D. Mazzucconi et al., CNAO, Med. Phys. 45 (11), 2018
[2] C. Graeff et al., GSI, Physica Medica 52, 2018
* Various proposals for monitoring in addition to routine regular treatment plan verification CTs: e.g. prompt gamma, nuclear fragmentation imaging, pRad,...

## Slide 4: Towards Mixed Beam Radiography Systems
* alternative: range shifter between between nozzle and patient and/or patient and detector to increase dynamic range
** would require sophisticated 4D-clustering to deal with increased hit multiplicity
Particle-integrating approach
Obtain WET map (e.g. per energy layer)
E.g. range telescope, scintillator, ...
Figure: ERC PROMISE project, C. Graeff [7]
Single-particle tracking
Figure: F. Ulrich-Pur [12]
Clinical flux may require system without front tracker**
Measure residual He energy e.g., via TOF
He/C-fragment distinction e.g., via dE/dx measurement
Needs to detect as wide a range as possible of residual He energies, while enabling distinction of He from C fragments

## Slide 5: Example: Scintillator Based Monitor I
Experiments at GSI in May 2025: scan of a dual beam through a sphere
sphere
Beam
Beam
CMOS camera
Cubic plastic (BC408) scintillator, 20x20x20 cm
Figure and video: C+He#21 with sphere, no range shifter.
Slide courtesy of M. Pullia & Simone Savazzi (CNAO)
[1] D. Mazzucconi et al., CNAO, Med. Phys. 45 (11), 2018

## Slide 6: Example: Scintillator Based Monitor II
3 mm sphere displacement
4 mm range variation
Experiments performed in 05/2025 at GSI (C. Graeff)
Figures: difference between the present image, taken after the target has changed, and the reference image.
Slide courtesy of M. Pullia & Simone Savazzi (CNAO)

## Slide 7: Outline
Overview: ongoing mixed helium-carbon ion beam experiments
Mixed beam slow extraction at GSI
Mixed beam slow extraction at MedAustron
Conclusion and Outlook
aka: how to deliver a mixed beam to get such nice videos?
GSI
MedAustron

## Slide 8: Recent Activities
Since <2018: Initial concept studies (CNAO [1], GSI [2], DKFZ [3,4])
  No mixed beam experimentally available back then
  Detection & treatment planning (simulations, sequential irradiation, ...)
Since 2023: ERC project PROMISE at GSI (C. Graeff et al. [5-7]).
  “Portal Range Monitoring in Mixed Ion Beam Surgery”
  Imaging & mixed beam delivery concepts, ...
  Nov. 2023: First delivery of mixed 12C3+ and 4He1+ beam (single ion source)
  Very successful beam time in May 2025.
Since 2023: Collaboration between TU Wien & MedAustron [8-10].
  Focus: Mixed ion beam delivery in medical synchrotron facilities
  Summer 2024: First delivery of a mixed beam in a medical facility (12C6+ & 4He2+, double injection)
[1] D. Mazzucconi et al., CNAO, Med. Phys. 45 (11), 2018
[2] C. Graeff et al., GSI, Physica Medica 52, 2018
[3] L. Volz et al., DKFZ, Phys Med Biol 65/2, 2020
[4] J. Hardt, DKFZ, Phys Med Biol 69/5, 2024
[8] E. Renner et al., IPAC ‘24
[9] M. Kausel, E. Renner et al. Submitted to PRAB, 2025
[10] M. Kausel, et al. IPAC ‘25
[5] M. Galonska et al., GSI, IPAC’24
[6] D. Ondreka et al., GSI, IPAC’24
[7] C. Graeff et al. PROMISE Project, GSI

## Slide 9: Mixed Ion Beams at GSI
  14 GHz ECRIS
  Source gas: methane & helium
  Acceleration in UNILAC & SIS18  biophysics cave
Figure: Number of counts at 728 nm wavelength (He I) for stepwise increase of He flow in a methane / helium plasma [5].
Figure: Mixed beam depth-dose curve measured in 2023 at GSI. Signal from IC3 and IC2 are carbon fragment tail corrected [11].
[5] Galonska et al. IPAC ‘24
[11] L. Volz et al, Ion Imaging ‘24
4He1+ content tailored by stepwise addition of helium flow to ion source plasma
  Monitor He contribution using optical emission spectroscopy
  2023 16O4+ contamination of less than 10%
  2025 16O4+ contamination significantly reduced.
Direct extraction of 12C3+ & 4He1+ mixture from single ion source [5]

## Slide 10: Mixed Ion Beams at MedAustron
Mixed beam from single ion source not deliverable in current medical synchrotron facilities.
  ⁴He¹⁺ + ¹²C³⁺ → cannot be accelerated in LINAC (requires q/m ≤ ⅓)
  ⁴He²⁺ + ¹²C⁶⁺ → insufficient ¹²C⁶⁺ yield with 14 GHz ECRIS
  ³He¹⁺ + ¹²C⁴⁺ → limited energy range + large ΔBρ/Bρ in synchrotron
Stripping foil
  *In the current configuration, mixed beam setup not suitable for clinical use.
(e) 12C4+ from source 2
(a) 4He2+ from Source 3
Aim: provide beam for research*
[9] M. Kausel et al., submitted to PRAB
Alternative: mixing via sequential multi-turn injection of 4He2+ and 12C6+ into synchrotron
Poster - F. Plassard
MedAustron Facility Overview
Tailor He:C ratio: adapt 2nd inj. bump amplitude
First mixed beam in summer ‘24

## Slide 11: Implication of Charge-to-Mass Ratio During RF Acceleration
causes acceleration to slightly different (depending on extraction and transition energy)
Example: Relative momentum per mass offset (𝛿) between the two ion species in a PIMMS-like synchrotron (𝛾tr≈2, )
[8] E. Renner, IPAC ‘24

## Slide 12: Take Away: Mixed Beams & RF Acceleration
Both contributions add up to total rigidity offset (depending on extraction and transition energy) ....
... & hence affect closed orbit and tune.
Example: Relative momentum per mass offset (𝛿) and horiz. tune (𝑄𝑥 ) separation between 4He2+ and 12C6+ in a PIMMS-like synchrotron (𝛾tr≈2, here 𝑄′𝑥 = − 1.3 and ).
[8] E. Renner, IPAC ‘24

## Slide 13: Slow Extraction Requirements in a Nutshell
Helium and carbon feature
different rigidity distributions (depending on extraction and transition energy),
in case of sequential injection also different horizontal phase space distributions.
Goal: Ideally extract mixed beam with (roughly) constant He:C ratio throughout the spill.
Long term goal: custom tailoring of He:C ratio throughout the spill.

## Slide 14: Selected Tools for Mixed Beam and Spill Characterization I
Set-up at GSI (Biophysics cave)
Set-up at MedAustron
(A) Time-resolved characterization of the extracted He:C ratio (e.g., using ionization chambers at different depths)
Courtesy of C. Graeff, L. Volz et al. [5, 11]
M. Kausel, C. Becker, et al. IPAC’25 [10]
He:C ratio obtained from Ifield / Iref (corrected for C fragments).

## Slide 15: Selected Tools for Mixed Beam and Spill Characterization II
(B) Alternative: Single particle distinction via dE/dx, e.g., with 50 µm Si sensor.
A. Gsponer, M. Kausel
(C) Non-invasive mixing ratio quantification based on RF regulation loop corrections.
Preliminary results: Mixing ratio estimate from synchrotron RF (y-axis) and ionization chambers in irradiation room (x-axis) agree within a few %.
Figure: Ekin=262 MeV, RL: 29.9mm. Extracted using Phase displacement extraction.
N. Okropiridze
Not routinely employed in current studies

## Slide 16: Outline
Overview: ongoing mixed helium-carbon ion beam experiments
Mixed beam slow extraction at GSI
Mixed beam slow extraction at MedAustron
Conclusion and Outlook
GSI
MedAustron

## Slide 17: Mixed Beam Slow Extraction at GSI: Overview
Single ion source: He and C with similar initial horiz. emittances
Beam time in 2023: tune sweep and RFKO
  Successful, but further studies needed.
  Δx=1-2mm between He and C at isocenter  most likely due to Dx (see appendix)
In May 2025: main on achieving stable He-to-C ratio across spill.
  RFKO, utilize spill feedback for rectangular spill.
  Check chromaticity and dispersion in transfer line (see appendix)
Slide courtesy of A. Pastushenko
Poster - A. Pastushenko: Flat C/He spills for online range monitoring in particle therapy
D. Ondreka et al. IPAC’24 [6]
Figure: tune sweep extr. with different chromaticities (2023)
Q
A
He-2+
C-6+
Schematic illustration. Proportions not to scale

## Slide 18: Mixed Beam Slow Extraction at GSI: Settings
SIS 18 mixed beam slow extraction configuration 05/2025
Extr. from below resonance (here:
At natural chromaticity (): tune difference betw. He and C is similar to
Simulations: Xsuite
Slide courtesy of A. Pastushenko
 To set up the condition for the simultaneous extraction of C and He one has to adjust the chromaticity.
Q
A
He-2+
C-6+
Schematic illustration. Proportions not to scale

## Slide 19: Mixed Beam Slow Extraction at GSI: Chromaticity Scan
Scan the range of [-2.0, 2.0]
RFKO signal: BPSK; center tune 4.(3) – 0.0037 and BW 0.01
Get He:C ratio from normalized ionization chamber currents IC2/IC1 and IC3/IC1
  Late extraction of He for
  Early extraction of He for
    For positive chromaticity we had to move away from resonance to avoid He extraction without RF-KO
  was set for the operation
*labels in brown – chromaticity was measured
Estimate impact of horizontal chromaticity on the extracted He:C ratio throughout spill:
Slide courtesy of A. Pastushenko

## Slide 20: Mixed Beam Slow Extraction at GSI: Spill Optimization
BPSK
Spill feedback on
Spill for the chromaticity of with and without spill optimization system
Average of ~20 cycles
Slide courtesy of A. Pastushenko
Talk - P. Niedermayer:
Spill feedback and optimisation system for RFKO and tune scan extraction

## Slide 21: Mixed Beam Slow Extraction at MedAustron: Overview
First mixed beam extracted in summer 2024
  Betatron core (clinically used for extraction) currently not operational in double cycle setup for mixed beams
  Until 01/2025: Preliminarily extract using Phase Displacement Extraction, without focus on spill characteristics.
Talk (Wednesday) - F. Plassard
  Status of RF knock-out extraction development at MedAustron
Talk (Tuesday) - K. Holzfeind
Investigations into multi energy extraction at MedAustron
Poster - F. Plassard
MedAustron Facility Overview
Poster – C. Schmitzer
Ultra High Dose Rate Beam Monitoring with Radiation-Hard SiC-Based Detectors
Since winter 2025: baseline RFKO
  Investigate effects due to differences in initial horizontal He & C (x,x’) and dpp distributions (double injection)
    Application of different RFKO signals & combinations, both for bunched and coasting beams
A
Q
He-2+
C-6+
  Employ experimental RFKO setup as described in:

## Slide 22: Putting the glasses on: Where are He and C located?
Example: Slow RFKO frequency sweep through coasting beam stack (from higher frequencies towards resonance).
← Schematic illustration (!) based several assumptions
See appendix
Frequency sweep (several seconds)
He and C with the expected offset in
* Assumed value

## Slide 23: Mixed Beam SX at MedAustron: Simulations
In this configuration, Xsuite simulations suggest that when applying a
... broadband phase shift keying excitation centered at C tunes,
... He extraction begins with a delay due to the initially smaller horizontal He emittance.
(1) Initial losses during sextupole ramp: mainly C.
* Disclaimer: Conceptual simulations: initial (x, x′) and δp/p distributions for He and C, are based on assumptions.

## Slide 24: Mixed Beam SX at MedAustron: Measurements
Coasting, BPSK
Bunched*
Lucky? Shift BPSK spectrum (coasting)
*presence of quadrupolar-mode synch. osc. during extr.
However, measurements show more constant He:C ratio throughout spill than expected.
Follow-ups: sensitivity studies (RFKO signals, optics, extraction energies), refine simulation model (x,x’, dpp dist); assess off-momentum losses in transfer line, increase resolution of measurements, ....
Nice, but not fully understood ... Even when varying the 2nd injection bump and hence the (expected)

## Slide 25: Outlook: Mixed Beams with Different Charge-to-Mass Ratios
Multiple, independent RF frequencies allow simultaneous acceleration of ion species with different q/m
Injection Fe
Injection
Bi
Simultaneous acceleration
Acceleration Fe
time / us
f/Hz
56Fe25+
209Bi68+
Milestone in May 2025 at GSI (SIS18)
  First successful acceleration and fast extraction of ion species with different q/m
Paves way for new ion combinations & respective range differences for treatment monitoring
  Simultaneous p+/C acceleration: feasibility tests at MedAustron in preparation
Opportunities for broader scientific communities. Any potentially interested user groups?
D. Ondreka

## Slide 26: Conclusion & Outlook
Mixed helium and carbon beams are now available for experimental studies
  GSI: generated in single ion source → similar horizontal He and C emittances
  MedAustron / TU Wien: sequential multi-turn injection → different horizontal He & C emittances
Mixed beam slow extraction studies ongoing
  Managed to extract constant He:C ratios.
  Demonstrated sensitivity of He:C ratio to chromaticity and RFKO excitation signals.
  Follow-up experiments and Xsuite simulations ongoing
  Long term goal: Flexibly tailor extracted He:C ratio across the spill (multiple RFKO signals?)
Outlook: First simultaneous acceleration of ions with different q/m (Fe, Bi)
  → paves the way for new research applications
Poster - A. Pastushenko: Flat C/He spills for online range monitoring in particle therapy
Our test set-ups are flexible – any ideas welcome!
Many thanks for your time!
Questions?

## Slide 27: References
[1] D. Mazzucconi, M. Pullia et al., “Mixed particle beam for simultaneous treatment and online range verification in carbon ion therapy: Proof-of-concept study” Med. Phys. 45 (11), 2018
[2] C. Graeff et al. “Helium as a range probe in carbon ion therapy”, Physica Medica 52, 2018
[3] L. Volz “Experimental exploration of a mixed helium/carbon beam for online treatment monitoring in carbon ion beam therapy” et al., Phys Med Biol 65/2, 2020
[4] J. Hardt “The potential of mixed carbon–helium beams for online treatment verification: a simulation and treatment planning study”, Phys Med Biol 69/5, 2024
[5] M. Galonska et al., “First dual isotope beam production for simultaneous heavy ion radiotherapy and radiography”, IPAC’24
[6] D. Ondreka et al., “Slow extraction of a dual-isotope beam from SIS18”, IPAC’24
[7] C. Graeff et al. ERC PROMISE, https://www.gsi.de/work/forschung/biophysik/erc_barb/promise
[8] E. Renner et al., “Towards the slow extraction of mixed He-2+ and C-6+ beams for online range verification” IPAC’24
[9] M. Kausel et al. “A double multi-turn injection scheme for generating mixed helium and carbon ion beams at medical synchrotron facilities” submitted to PRAB, https://arxiv.org/abs/2501.12797, 2025
[10] M. Kausel et al., “Recent developments in delivering mixed helium and carbon ion beams for online treatment monitoring research at MedAustron”, IPAC ‘25
[11] L Volz et al., “Portal imaging with mixed beams: Status and future Potential”, 5th Ion Imaging Workshop, 2024
[12] F. Ulrich-Pur “First experimental time-of-flight-based proton radiography using low gain avalanche diodes” Phys Med Biol 69 (2024)

## Slide 28: Spare Slides

## Slide 29: GSI SIS 18 Machine Properties: Chromaticity
We measure on/off – momentum tunes. The beam is excited with a broad noise.
Agreement is reached with m-2 component in the dipoles.
Measurements were done with resonance sextupoles on and off.
For one setting (ks.offset = 0.14, ), tune was measured for a bigger range of momentum offsets. Nonlinear chromaticity hints nonlinearities in magnets ( in quads, ..)
Chromaticity in the ring is set with a parameter (ks.offset). We checked if the relation agrees with the simulations.

## Slide 30: GSI SIS 18 Machine Properties: Transfer Line Dispersion
Due to the lack of time, measurements were done at 2 locations, upstream of the medical cave.
Reconstructed dispersion shows large amplitudes along the transfer line. Need to be measured again (+) in other locations along the transfer line.
In 2023, horizontal positions of He and C at isocenter were 1 – 2 mm apart. Most likely explanation – horizontal dispersion.
Measured :
17.4 m
6.7 m
Estimate at the end
~ -4 m

## Slide 31: Supplementary Material for Mixed Beam SX at MedAustron
Overshoot in BPSK signal
With PSK seed reproducible ripple in intensity and He:C ratio.

## Slide 32: Supplementary Material for Mixed Beam SX at MedAustron
Slow RFKO frequency sweep through waiting beam stack

## Slide 33: Supplementary Material for Mixed Beam SX at MedAustron
  200 MeV/u
  Broadband PSK with amplitude modulation
  He:C ratio tailored by adapting the 2nd injection bump amplitude.
Current measurement: only 1 measurement per setting
Mixing ratio estimate based on synchrotron RF frequency
Extraction He:C ratio throughout the spill
Beam current measurement in the synchrotron

## Slide 34: Supplementary Material for Mixed Beam SX at MedAustron
In this double-cycle configuration, the vertical beam size of He appears to be smaller than that of C.

## Slide 35: Single Ion Source in Clinical Facilities?
4He1+ and 12C3+
Source ✔ LINAC ❌ Synchrotron ✔
No stripping required
After stripping
No stripping; q/m=1/3
4He2+ and 12C6+
Source ❌ LINAC ✔ Synchrotron ✔
3He1+ and 12C4+
Source ✔ LINAC ✔ Synchrotron ❌
( < 400 MeV/u)
LINAC:
standard at e.g. MedAustron, CNAO, HIT
ECR ion sources: different source branches
4He2+
12C4+
Take away
Mixed beam generation within single ion source currently not possible in state-of-the-art medical synchrotron facilities.
Stripping foil

## Slide 36: Double Multi-Turn Injection: Technical Challenges @ MedAustron
Different injection energies due to in LINAC
  Mitigation measures (decelerate helium):
    Injector: debuncher cavity (allows to inject He into the synchrotron) and
    Synchrotron: deceleration prior to carbon inj. (using radial loop regulation; facilitates simultaneous capture)
S3: 4He2+
S2: 12C4+
[9] M. Kausel et al., submitted to PRAB ‘25
1) RL offset
-20 mm
2) RL offset
+20 mm
RL regulation
(1) Capture + decelerate helium prior to carbon injection.
Meas.
Measurement
Xsuite Simulation
(1)
(2)
(2) Inj.. C; capture und acc. He+C