## Slide 1: Stable islands and bent crystals for slow extraction
D. Veres, M. Giovannozzi, G. Franchetti
Acknowledgements: P. Arrutia, F. Asvesta, H. Bartosik, P. Bestmann, G. Franchetti, P. Hermes, K. Li, B. Lindström, G. Papotti, L. Pauwels, S. Redaelli, B. Salvant, R. Taylor, F. van der Veken, F. M. Velotti and SPS OP Crew

## Slide 2: Outline
Introduction
Proposed method
Simulation results
Proof-of-principle test at CERN SPS
Conclusions and outlook

## Slide 3: Introduction
Slow extraction is a well-established extraction method from circular accelerators
It exploits the third-order resonance
  Particles are driven to large amplitudes by the unstable dynamics generated by hyperbolic fixed points
  The expanding motion has an intrinsic stochastic character that prevents a full control of the dynamics
  Beam losses at the extraction septum are essentially unavoidable
  Is it possible to find alternative ways to push particles to large amplitude and reduce beam losses?

## Slide 4: Introduction
Since 2015, the CERN PS delivers beam to the SPS using Multi-turn Extraction (MTE)
  It is based on beam splitting by crossing the fourth-order resonance
  Particles are trapped and transported in stable islands
  The extraction is performed over five turns
Stable islands, instead of unbounded separatrices, allow for a regular dynamics and transport to large amplitudes.
Courtesy A. Huschauer

## Slide 5: Introduction
Bent crystals are becoming more and more popular in circular accelerators
  Collimation system in the CERN LHC
  Shadowing of extraction septum in the SPS
  Fixed-target experiment in the LHC

## Slide 6: Proposed method
We propose to combine
  Stable islands to trap and transport particles to large amplitudes
  Bent crystals to deflect particles and separate them from circulating beam

## Slide 7: Proposed method
Some considerations
  Stable islands imply a compact separatrix. The motion outside of the separatrix is regular. Hence, multiple interactions of the particle with the crystal are possible, which enhances the overall efficiency of the process.
  Particles are pushed from the triangular-shaped central region to the islands by a time variation of the system parameter. If the variation is adiabatic, then the process is described by a trapping probability that can be engineered by considering the time variation of the areas of the various phase-space regions.
  The time variation of the system parameters can be performed in various ways:
    Change the ring tune (this is what is done for MTE).
    Change the reference momentum by introducing a ramp of the magnetic flat top where the slow extraction takes place.
A. Neishtadt. “Passage through a separatrix in a resonance problem with a slowly-varying parameter”. J. Appl. Math. Mech. 39(4) (1975), pp. 594–605.
Neishtadt. “On the accuracy of conservation of the adiabatic invariant”. J. Appl. Math. Mech. 45(1) (1981), pp. 58–63.
A. Neishtadt. “Change of an Adiabatic Invariant at a Separatrix”. Fiz. Plasmy 12(992) (1986).
Region I
Region II
Region III

## Slide 8: Proposed method
Transport in stable islands
  Change of the reference momentum has been selected for compatibility with current SPS slow extraction process
    The beam is debunched prior to extraction
    Large negative chromaticity is used
    All magnetic elements are varied with the change of reference momentum
  This approach keeps the phase-space topology almost constant (Constant Optics Slow Extraction - COSE)

## Slide 9: Simulation results
Some considerations
  A simple 4D polynomial map (Hénon map with sextupoles and octupoles), with parameters inspired by the SPS case has been used.
  The Hamiltonian of the system is
The nonlinearities are varied too to control the trapping probability
Optimised variation of tune and nonlinearities for the two sides of the resonance

## Slide 10: Simulation results
Some considerations
  A simple 4D polynomial map (Hénon map with sextupoles and octupoles), with parameters inspired by the SPS case has been used.
Simulated performance vs crystal alignment (position and angle)
Typical spill. Addition of 50 Hz ripple and harmonics affects the spill similarly to a classic slow extraction

## Slide 11: Simulation results
Some considerations
  A lattice inspired by the CERN SPS has been built to perform 6D simulations
  Zero-dispersion straights are used to located key elements
  400 GeV protons, extracted over about 3.5 s
G. Iadarola et al., Xsuite: an integrated beam physics simulation framework, 2023.
G. Iadarola et al., Xsuite. Available at https://xsuite.readthedocs.io/en/latest/, 2023.
  2.8 mm long Si crystal bending 100 mrad
  500 mm septum thickness (pessimistic estimate from SPS)
  Xsuite and Xcoll used as tracking tools
Main parameters of the SPS-like ring

## Slide 12: Simulation results
Some considerations
  The shape of the stable islands can be used to control the beam spot on the crystal.
  The shape of the stable islands can be used to make the particles fall in the channelling acceptance of the crystal.
98.2% of first impacts in within channelling acceptance
Global performance analysis of the proposed extraction (without ripple or orbit jitter). Aperture limits are black absorbers.

## Slide 13: Simulation results
Some selected results
Typical spill structure
Distribution of extracted beam
Spill with orbit jitter
Orbit jitter along ring circumference

## Slide 14: Proof-of-principle test at CERN SPS
Experimental activities were carried out in 2024-25 SPS runs
  Preparatory tests in 2024
    Generation of stable islands
    Phase-space reconstruction
    Beam splitting by tune change.
    Promising but inconclusive proof-of-principle test
  Successful proof-of-principle test in 2025
    Demonstrate transport in stable islands to the crystal
    Demonstrate channelling onto a collimator
    No extraction to protect septa.
Phase-space reconstruction by kicking thew beam into one island
Beam splitting by crossing the third-order resonance

## Slide 15: Proof-of-principle test at CERN SPS
Experimental procedure
  General strategy
    The entire beam manipulation (beam is split using stable islands and a ramp of all magnetic elements) is implemented
    Three configurations are probed
      No crystal
      Crystal in amorphous condition
      Crystal in channelling condition
    Beam behaviour is probed by means of a collimator
      Scan of the inner jaw position
      Measurement of the beam intensity vs time and of local losses
    A wire scanner provide information about the transverse beam profile
Special orbit bumps are created around crystal and collimator
This island interacts with the crystal
This island interacts with the collimator jaw
Channelled particles land close to this island

## Slide 16: Proof-of-principle test at CERN SPS
SPS ring configuration
  Ring optics
    Qx →26.31, Qy →26.11, Q′x →−21.5
  Energy: 100 GeV
  Beam properties
    Four bunches
    Intensity: 1010 p/b
    Normalised emittance: about 0.56 mm
  Nonlinear elements
    One extraction sextupole (LSE.40602) to excite the resonance and control the orientation of islands
    LOF octupoles to generate the stable islands
  Ramp all magnetic elements
    0.33 GeV over 4 s
  Special orbit bumps
    Around crystal and collimator
Sequence of events in the SPS cycle for the proof-of-principle experiment

## Slide 17: Proof-of-principle test at CERN SPS
Observables and expectations
Stable islands visible in wire scanner profiles
  Beam intensity is steadily depleted
  Clear difference in the start of losses with and without crystal as a function of collimator jaw position
  Losses only at collimator(s) and crystal, magnitude consistent with crystal orientation
✓
✓
✓
TECA ➛ Crystal TCSM ➛ Collimator TIDP ➛ Momentum collimator
No crystal
Crystal in amorphous orientation
Crystal in channelling orientation

## Slide 18: Proof-of-principle test at CERN SPS
Observables and expectations
Stable islands visible in wire scanner profiles
  Beam intensity is steadily depleted
  Clear difference in the start of losses with and without crystal as a function of collimator jaw position
  Losses only at collimator(s) and crystal, magnitude consistent with crystal orientation
No crystal
Crystal in amorphous orientation
Crystal in channelling orientation
✓
✓
✓
✓
TECA ➛ Crystal TCSM ➛ Collimator TIDP ➛ Momentum collimator

## Slide 19: Proof-of-principle test at CERN SPS
Observables and expectations
Stable islands visible in wire scanner profiles
  Beam intensity is steadily depleted
  Clear difference in the start of losses with and without crystal as a function of collimator jaw position
  Losses only at collimator(s) and crystal, magnitude consistent with crystal orientation
✓
✓
✓
✓
TECA ➛ Crystal TCSM ➛ Collimator TIDP ➛ Momentum collimator

## Slide 20: Proof-of-principle test at CERN SPS
Comparisons with simulations
Profiles measured with collimator and crystal retracted. Losses are in momentum collimator (TIDP).
Good agreement between measurement and simulation results. The small discrepancies are probably linked to the details of the initial beam distribution.
The simulations detected a misalignment of the TIDP, confirmed a posteriori by survey measurements!
TECA ➛ Crystal TCSM ➛ Collimator TIDP ➛ Momentum collimator

## Slide 21: Proof-of-principle test at CERN SPS
Comparisons with simulations
Intensity evolution and losses around the ring as a function of the collimator jaw position. The crystal is in channelling mode.
Good agreement between measurements and simulation results.
Measurements
Simulations
TECA ➛ Crystal TCSM ➛ Collimator TIDP ➛ Momentum collimator

## Slide 22: Conclusions and outlook
A novel method of slow extraction from hadron accelerators combining stable islands and planar channelling by a bent crystal was developed
The use of stable islands to transport particles to the crystal allows for good control over the type of interactions with the crystal. This makes it possible to exploit the higher efficiency of multiple interactions with the crystal.
Successful proof-of-principle tests were conducted at the CERN SPS, which showed very good agreement with expectations and simulations results.

## Slide 23
Thank you for your attention!!!

## Slide 24: Selected references - I
M. A. Fraser et al. SPS Slow Extraction Losses and Activation: Challenges and Possibilities for Improvement. In Proc. IPAC’17, p. 611–614.
F. M. Velotti et al. Reduction of Resonant Slow Extraction Losses with Shadowing of Septum Wires by a Bent Crystal. In Proc. IPAC’17, p. 631–634.
M. A. Fraser et al. Slow Extraction Efficiency Measurements at the CERN SPS. In Proc. IPAC’18, p. 834–837.
M. A. Fraser et al. Demonstration of slow extraction loss reduction with the application of octupoles at the CERN Super Proton Synchrotron. Phys. Rev. Accel. Beams, 22:123501, 2019.
L. S. Esposito et al. Crystal for Slow Extraction Loss-Reduction of the SPS Electrostatic Septum. In Proc. IPAC’19, p. 2379–2382.
F. M. Velotti et al. Demonstration of Loss Reduction Using a Thin Bent Crystal to Shadow an Electrostatic Septum During Resonant Slow Extraction. In Proc. IPAC’19, p. 3399–3403.
F. M. Velotti et al. Septum shadowing by means of a bent crystal to reduce slow extraction beam loss. Phys. Rev. Accel. Beams, 22:093502, 2019.
V. Kain et al. Resonant slow extraction with constant optics for improved separatrix control at the extraction septum. Phys. Rev. Accel. Beams, 22:101001, 2019.
B. Goddard et al. Reduction of 400 GeV/c slow extraction beam loss with a wire diffuser at the CERN Super Proton Synchrotron. Phys. Rev. Accel. Beams, 23:023501, 2020.

## Slide 25: Selected references - II
D. E. Veres, M. Giovannozzi, and G. Franchetti. Exploring the potential of resonance islands and bent crystals for a slow extraction from circular hadron accelerators, Phys. Rev. Research 6, L042018, 2024.
D. E. Veres, G. Franchetti, M. Giovannozzi. An innovative method for slow extraction in circular hadron accelerators with resonance islands and bent crystals, Nucl. Instrum. & Methods A 1073, 170286, 2025.
D. E. Veres, H. Bartosik, G. Franchetti, M. Giovannozzi, K. Paraschou. Demonstrating Beam Splitting Through Stable Islands Formed by the Third-Order Resonance at the CERN Super Proton Synchrotron, J. Phys.: Conf. Ser. 3094, 012037, 2025.