## Slide 1: SX schemes for SIS100 in the presence of higher-order field errors
D. Ondreka, B. Galnander, S. Sorge, GSI
6th SX Workshop, Stony Brook 6 October 2025

## Slide 2: Contents
Recap of status from last WS
  Overview of SIS100
  Magnetic field measurements
  Effect of systematic errors
Modified multipole correctors
SX schemes with field errors
  Modified SX design
  Random error studies
Next steps
Summary

## Slide 3: SIS100: Overview
Workhorse of FAIR facility
  Primary heavy ion beams
  Factor 100 higher intensities than SIS18
Basic parameters
  Circumference 1083 m (= 5 x SIS18)
  Max. magnetic rigidity 100 Tm
  Max. ramp rate 4 T/s
  Super-ferric main magnets
Ion optical layout
  Super-periodicity 6, 14 cells per period
  DF focusing structure (charge separator lattice)
  Optimized for operation with intermediate charge state ions
Working modes
  Batch injection from SIS18
  Slow extraction to fixed targets
  Fast extraction to fixed targets or storage rings
Optical parameters (SX)` | 
Qh / Qv | 17.31 / 17.4
Q’h / Q’v | -17.5 / -22.7
αp | 0.005
γt | 14.2
SIS100
SX Experiments

## Slide 4: Magnetic Measurements: Field Errors
Measurements of SF main magnets
  Dipoles: all magnets measured (108 + 2)
  Quadrupoles: data from 53 magnets available
Analyzed data as function of current
  Variation of integral field
  Harmonics at Rref (dipole: n ≤ 7, quad: n ≤ 10)
  Unexpectedly large systematic components
    Dipoles: decapole (b5)
    Quadrupoles: dodecapole (b6)
Systematic components influence SX strongly
Systematic field errors in dipoles
Systematic field errors in quadrupoles

## Slide 5: SX: Effect of Systematic Errors
SX affected by ADTS bending separatrix
  Effects independent of momentum
    ADTS in first order of strengths: b6
    ADTS in second order of strengths:
      b3∙b3 (considered in baseline design)
      b5∙b3 (coupling with sextupoles)
  Effects depending on momentum
    Momentum-dependent ADTS by feed-down from dispersion in first order of strength:: b5∙δ
Effects on SX in SIS100
  Larger angular spread at ES through b5∙δ
  Strong bending by b6, larger for small tune distance
Compensation options in SIS100 (baseline)
  No b5 or b6 corrector magnets
  Two families of octupoles effecting ADTS by b4
    Baseline: compensate b3∙b3 from chroma sextupoles
    Can be used to mitigate effects of b6 and b5∙b3
  No compensation of b5∙δ in baseline lattice
b5∙δ
b5∙b3
b6
KO: b6 mitigated by octupoles
Tune-sweep: no compensation

## Slide 6: Multipole correctors
Baseline corrector
  Nested cos(θ) coils comprising b2, a3, b4
  Two families, six each (large and small βx / βy)
  Options for b5 and b6 coils studied
Constraints on modified corrector
  Only three types per magnet
  b5 corrector would need location with large βx∙D
  b6 corrector would need location with large βx
Final decision:
  Corrector with b5 at beginning of arc (b2, b4, b5)
  Baseline corrector at end of arc (b2, a3, b4)
  Mitigate b6 using baseline octupoles
Courtesy K. Sugita

## Slide 7: SX schemes with field errors
Requirements
  Separatrix sizes up to 25-30 um
  Extraction efficiency > 95% (activation)
  Losses on first wire ~ 1% (ES protection)
  Robustness against random magnet imperfections
  KO extraction plus one fallback scheme
  Avoid b5 compensation if possible (simplicity)
Constraints
  No major changes to lattice (under construction)
  Acceptance of ring limited by cryo catchers
  Small acceptance of extraction channel
Challenge
  Large emittance for separatrix shrinking schemes
Design horizontal emittances on flattop
x
x’
ES
Separatrix shrinking
LS
ES1
ES2
left margin
right margin
Beam transport from ES to LS
Particle trajectories over last three turns

## Slide 8: SX Schemes: KO
Specific challenges
  Small and large separatrix
    Different ion species and energies
    Power saving for KO exciter
Characteristics
  Small chromaticity for good separatrix overlap
  Bending by b6 mitigated with octupoles
  Usage of b5 correctors not necessary
    Increased spread through b5∙δ acceptable
  Total losses well within budget
  First wire losses a bit higher than expected (~1%) due to non-uniform distribution
Sepratrix size | 28 π∙μm | 8 π∙μm
Hor. chromaticity | -3 | -1
Sextupole amplitude | 0.70 m-2 | 0.45 m-2
Octupole strength | -1.0 m-3 | 1.9 m-3
Total losses | 2.2% | 1.8%
Losses first wire | 1.7% | 1.5%
B. Galnander
Distribution of extracted particles at ES

## Slide 9: SX Schemes: COSE
Specific challenges
  Large emittance difficult to handle
    ‘Linear’ Hardt condition for Q’x ≈ 0
    Small angular acceptance
Characteristics
  Usage of b5 correctors not necessary
    b5∙δ bending actually improves alignment
  Large chroma preferred due to smaller ΔBρ
    More δ selective  constant phase space at ES
  Strong octupoles for larger chromaticity
    ADTS cross-term axy must be removed
Preferred fallback scheme
Sepratrix size | 28 π∙μm | 10 π∙μm
Hor. chromaticity | -10 | -3.5
Sextupole amplitude | 0.40 m-2 | 0.32 m-2
Octupole strength | -/+9.2 m-3 | 1.5 m-3
Total losses | 3.5% | 2.1%
Losses first wire | 1.5% | 1.5%
B. Galnander
Momentum deviation vs. turn number

## Slide 10: SX Schemes: Tune-Sweep
Specific challenges
  Large emittance difficult to handle
  Large angular spread favors b5 compensation
Characteristics
  Chromaticity uncorrected
  Very large octupole strengths required
    ADTS cross-term axy must be removed
  Large angular spread due to shrinking separatrix
  Acceptable losses only for sepa size <= 15 π∙um
  Possibly useful as commissioning scheme
Sepratrix size | 15 π∙μm | 10 π∙μm
Hor. chromaticity | -17.5 (nat.) | -17.5 (nat.)
Res. sext. ampl. | 0.33 m-2 | 0.38 m-2
Octupole strength | -/+12.7 m-3 | -/+9.2 m-3
Total losses | 3.9% | 3.2%
Losses first wire | 1.5% | 1.2%
B. Galnander
Shrinking separatrices for different momenta

## Slide 11: Options for employing b5 correctors
Goal: better separatrix alignment
COSE: ‘anti-compensation’
  Amplify effect of b5 from dipoles
  Increased b5∙δ bending improves overlap
  Small losses (2.3%) even for large emittance
  Robustness yet to be checked
KO: limits for small separatrix
  Compensation of b5 not independent
  Better overlap at price of stronger size dependence
  Hard to get around acceptance limit at LS
Benefits to be investigated in further studies
COSE without and with b5 ‘anti-compensation’
KO extraction without and with b5 compensation

## Slide 12: SX with Magnet Imperfections: Random Error Studies
Goal: Verify robustness of SX schemes against magnet imperfections
  Magnet alignment errors
  Magnetic field errors (variations in integral field, harmonics)
Simulation procedure per scenario
  10 random error seeds chosen from Gaussian distribution truncated at 2σ
  Nelder-Mead optimizer to match separatrix
    Target parameters: separatrix size, spiral step, crossing angle
    Variables: tune distance, virtual sextupole, orbit bump, octupole strengths
  Tracking of 1000 particles over 25000 turns with MAD-X to evaluate performance
Preliminary results on SX without b5 compensation
  KO extraction and COSE robust against errors
Limitations
  Optimistic distributions for quadrupoles’ roll and variation of integral field
  Matching of separatrix can lead to non-optimal settings due to ignorance of distributions
    MAD-X tracking times not suitable for use of optimizer with multi-particle simulations
S. Sorge

## Slide 13: Magnet Imperfections: Alignment Errors
S. Sorge
Sources of alignment errors for SF magnets
  Mismatch between geometric and magnetic axis
  Tolerance for positioning magnet on girder
  Tolerance for positioning girder in cryostat
  Motion during cool-down
  Alignment tolerance of cryostat
Conservative values in simulations
  Lateral shifts of with σ = 1 mm
  Roll estimated from mechanical tolerances

## Slide 14: Magnet Imperfections: Model for Field Errors
S. Sorge
ΔB2/B2: magnetometer #2
ΔB2/B2: all magnetometers
Dipoles
  Systematic allowed components: b3, b5, b7
  Mean values of forbidden components discarded
    b2 artifact from measurement geometry
  Random components: standard deviation used as σ
  Integral field variation: σmod = 4∙10-3 > σmeas = 3∙10-4
    Kept for comparison with previous studies
Quadrupoles
  Systematic allowed components: b6, b10
  Mean values of forbidden components zero
  Random components: standard deviation used as σ
  Integral field variation: σmod = 5∙10-4 < σmeas > 7∙10-4
    Kept for comparison with previous studies
Calibration uncertainty for quadrupoles
  Systematic offsets between magnetometers
  Not fully removed by official cross-calibration
  Factor 2 difference in expected beta beating
Measured multipole errors in dipoles
Measured multipole errors in quadrupoles

## Slide 15: Random Error Studies: KO Extraction (U28+, 400 MeV/u)
S. Sorge
Target parameters | 
Separatrix size | 28 um
Spiral step | 10 mm
Crossing angle | 1.3 mrad
Tune distance
Sextupole amplitude
Sextupole phase
Octupole strength
Separatrix size
Crossing angle
Spiral step
Performance (errors / ideal) | 
Total losses | 2.3% / 2.2%
Losses 1st wire | 1.5% / 1.5%

## Slide 16: Random Error Studies: COSE (U28+, 1.5 GeV/u)
Performance (errors / ideal) | 
Total losses | 3.9% / 2.1%
Losses 1st wire | 1.3% / 1.5%
S. Sorge
Target parameters | 
Separatrix size | 11.5 um
Spiral step | 10 mm
Crossing angle | 1.3 mrad
Tune distance
Sextupole amplitude
Sextupole phase
Octupole strength
Separatrix size
Crossing angle
Spiral step
artefact from matching issues

## Slide 17: Next Steps
Continuation of error studies
  Schemes with b5 compensation
  Pessimistic quadrupole roll and field variation
  More statistics (larger number of seeds)
Studies for commissioning and operation
  Commissioning strategy
    Robust settings for design schemes
    Step-wise approach starting with simpler schemes
  Models for tuning of SX in operation
    ML for coupled, non-linear multi-parameter space
    Optimizers for fast tuning
Moving to Xsuite for faster tracking
  On GPU farm: 0.1Mpart * 0.6Mturns in few hours
  First runs (U28+, 1.5 GeV/u) by Ph. Niedermayer
  Benchmarked with Elegant for ideal machine
Courtesy Ph. Niedermayer
Phase space plots from Xsuite…
… and Elegant

## Slide 18: Summary
SX from SIS100 affected by systematic b5 and b6 errors from main magnets
Multipole corrector family modified to include b5 corrector
SX design adapted to account for b5 and b6
  KO SX and COSE work without b5 corrector
  Tune-sweep SX requires b5 corrector, COSE and KO may profit from it
Random error studies with MAD-X indicate robustness
  Optimizer used to determine settings based on single-particle tracking
  Some error estimates may be on the optimistic side, to be redone
Further studies will be based on Xsuite for faster tracking times
  Allows increased statistics and optimization using multi-particle simulations
Special thanks for their invaluable contributions go to: B. Galnander , Ph. Niedermayer, S. Sorge, and K. Sugita

## Slide 19: Thanks for your attention!
More info and media: https://www.gsi.de/en/researchaccelerators/fair/fair_civil_construction
Drone video of construction site: https://www.youtube.com/watch?v=tKuXUgJyirQ
Impressions from the ongoing installation of SIS100

## Slide 20: Reminder: SX schemes
Control of separatrix parameters required
  Size and orientation (crossing angle)
  Spiral step and pitch
Fixing chromaticity, parameters depend on
  Machine tune Qx,0
  Momentum deviation δ
Comparison of SX schemes
  Quad-driven SX
    2D dependence on Qx,0(t) and δ
    Parameters must be matched for each Qx,0 and δ
  Transverse knock-out SX
    Fixed Qx,0, matching for δ only
    Ideally small difference in separatrix sizes
  Momentum-driven SX
    Fixed Qx,0, matching for δ only
    Separatrix sizes must vary down to zero
Tune-sweep SX
For SIS100, KO and δ-driven SX are the only reasonable choices due to strong δ-dependence of separatrix parameters
KO SX
hor. excitation
Momentum-driven SX
δ-change