## Slide 1
Design of a resonant slow extraction from low-emittance electron booster rings using transverse resonance island buckets
Cristopher Cortés, I. Agapov and W. Hillert
6th slow extraction workshop (SX 2025)
Oct 6 - 9 , 2025 Stony Brook, NY, USA

## Slide 2
Contents
DESY.
Introduction
Future light sources
Electron booster rings
Theory overview
Transversal dynamics
Slow extraction
DESY IV layout
Slow extraction setting
Example: Extraction at 6 GeV
Summary

## Slide 3
Introduction
DESY.
Electron storage rings are science enablers for many photon users
PETRA III at DESY
2.3km circumference
6 GeV electron beam
Around 25 beamlines
Figure taken from https://synchrotron.royalsociety.org.nz/science/
Schematic of a synchrotron light source
Synchrotron light is produced with specialized insertion devices (undulators)
Notes: Success story -> proliferation of light sources

## Slide 4
Introduction
DESY.
Figure taken from https://doi.org/10.1142/S1793626810000361
Average brightness evolution of light sources in time
Photon beam brightness
Brightness increased by three orders of magnitude every 10 years since 1960s
Fourth-generation enabled by ultra-low emittances (electron beam sizes and divergences)
Photon beam
Electron beam

## Slide 5
Introduction
DESY.
Arc cells are hybrid six-bend achromats
New experimental hall to accommodate half of the beamlines
New low emittance booster based on multi-bend achromat cells
Will supply diffraction limited X-rays up to about 10 keV
Planned upgrade at DESY, Hamburg
New booster
New storage ring
(2.3 km)
[1] I. Agapov et al. Beam dynamics performance of the proposed PETRA IV storage ring. August 16, 2024. Pre-print: https://arxiv.org/pdf/2408.07995

## Slide 6
Introduction
DESY.
Optical functions for the new cells
[1] I. Agapov et al. Beam dynamics performance of the proposed PETRA IV storage ring. August 16, 2024. Pre-print: https://arxiv.org/pdf/2408.07995
Arc cells are hybrid six-bend achromats
New experimental hall to accommodate half of the beamlines
New low emittance booster based on multi-bend achromat cells
Will supply diffraction limited X-rays up to about 10 keV
Bending magnets
Quadrupole magnets
Sextupole magnets
Octupole magnets

## Slide 7
Introduction
DESY.
Optical functions for the new cells
[1] I. Agapov et al. Beam dynamics performance of the proposed PETRA IV storage ring. August 16, 2024. Pre-print: https://arxiv.org/pdf/2408.07995
Bending magnets
Quadrupole magnets
Sextupole magnets
Octupole magnets
Hybrid multi-bend achromats
Very low emittances achievable (< nm)
High quadrupole strengths
High natural chromaticity + Low dispersion
Strong sextupole strengths
Limited dynamic aperture
(< cm)
Low emittance booster is needed
(either LINAC, achromat synchrotron or plasma injector)

## Slide 8
DESY.
Off-axis injection
Injection and charge accumulation
PETRA IV will feature off-axis injection for initial charge accumulation and top-up
Horizontal aperture is limited by non-linear dynamics
Vertical aperture is limited by physical restrictions (Insertion Devices)
PETRA IV dynamic aperture
Stored beam
Injected beam

## Slide 9
DESY.
New booster is required!
Injection and charge accumulation
PETRA IV dynamic aperture
Stored beam
Injected beam
Specification:
20 nm rad eq. emittance @ 6 GeV
Requirements:
max. 50 nm rad (for off-axis injection)
1 nC single bunch charge

## Slide 10
Introduction
DESY.
Status of booster synchrotron
Specification:
20 nm rad eq. emittance @ 6 GeV
Structural analysis ruled out installation in the ceiling (mid-2023)
Design was revisited in winter 2023
Installation possibilities of DESY IV
in booster cave

## Slide 11
Introduction
DESY.
Optical functions of the possible DESY IV boosters
Eight-fold symmetric ring cell
Six-fold symmetric ring super-cell

## Slide 12
Introduction
DESY.
Status of booster synchrotron
Requirement:
20 nm rad eq. emittance @ 6 GeV
Structural analysis ruled out installation in the ceiling
Design was revisited in winter 2023
Test beam capabilities (?)
Multi-GeV positron and electron beams
1266 users from 2013-2017
R&D of detector technology
(mainly ATLAS & CMS)
J. Dreyling-Eschweiler, et. al. The DESY II test beam facility, NIM-A, Vol. 922, 2019,
https://doi.org/10.1016/j.nima.2018.11.133.
Sketch of the test beam facility at DESY

## Slide 13
Introduction
DESY.
Status of booster synchrotron
Requirement:
20 nm rad eq. emittance @ 6 GeV
Structural analysis ruled out installation in the ceiling
Design was revisited in winter 2023
Test beam capabilities (?)
Multi-GeV positron and electron beams
1266 users from 2013-2017
R&D of detector technology
(mainly ATLAS & CMS)
J. Dreyling-Eschweiler, et. al. The DESY II test beam facility, NIM-A, Vol. 922, 2019,
https://doi.org/10.1016/j.nima.2018.11.133.
Sketch of the test beam facility at DESY

## Slide 14
Contents
DESY.
Introduction
Future light sources
Electron booster rings
Theory overview
Transversal dynamics
Slow extraction
DESY IV layout
Slow extraction setting
Example: Extraction at 6 GeV
Summary

## Slide 15
Transversal dynamics
DESY.
Assume high sextupole strengths as in future electron booster rings
Sextupoles generate amplitude detuning (second order effect) extended Hamiltonian
Kobayashi part
extension (K.Symon, 1968)
Amplitude detuning

## Slide 16
Transversal dynamics
DESY.
Assume high sextupole strengths as in future electron booster rings
Unstable and stable fixed points can be estimated with formulas
Make use of this optics to extract
Kobayashi part
extension (K.Symon, 1968)

## Slide 17
Resonant slow extraction
DESY.
Quadrupole driven
Reduce the tune difference to shrink the stable triangle area
Picture taken from: PJ Bryant. Resonant Extraction. CAS-CERN Accelerator School: Beam injection, extraction and transfer. Italy, 2017.
M. Tomizawa, et. al.
Slow beam extraction
at TARN II. NIM-A, 1992.
Keep the optics constant. Blow-up the beam by exciting the betatron oscillations
RF-KO
RF-KO with TRIBs optics

## Slide 18
Contents
DESY.
Introduction
Future light sources
Electron booster rings
Theory overview
Transversal dynamics
Slow extraction
DESY IV layout
Slow extraction setting
Example: Extraction at 6 GeV
Summary

## Slide 19
DESY IV
DESY.
Less aggressive optics
Crossing of half-integer stop-band

## Slide 20
Setting up the slow extraction
DESY.
Two harmonic sextupole families
Stripline kicker for the emittance blow-up
Thin-electrostatic septum (ESS)
Magnetostatic septum (MSS)
Hardware necessary
Harm. sext.

## Slide 21
Setting up the slow extraction
DESY.
Functional dependency of amplitude detuning and virtual sextupole strength
Scan over tune distance to resonance and sextupole strength to determine optimal working point for extraction
Unstable fixed point determine the available area in phase-space for the “waiting beam”
For the 8-fold lattice the amplitude detuning is very sensitive to the virtual sextupole strength
Tune distance to resonance
Parameter scan for 8-fold lattice
Virtual sextupole strength
Working point

## Slide 22
Setting up the slow extraction
DESY.
Phase-space portrait at feasible working point
Tune distance to resonance
Parameter scan for 8-fold lattice
Virtual sextupole strength
Working point

## Slide 23
Setting up the slow extraction
DESY.
Phase-space portrait at feasible working point
Tune distance to resonance
Parameter scan for 8-fold lattice
Virtual sextupole strength
Working point
No islands were generated!

## Slide 24
Setting up the slow extraction
DESY.
Two harmonic sextupole families
Stripline kicker for the emittance blow-up
Thin-electrostatic septum (ESS)
Magnetostatic septum (MSS)
Add one harmonic octupole family
Hardware necessary
Harm. sext.
Harm. octupole

## Slide 25
Setting up the slow extraction
DESY.
Phase-space portrait at feasible working point with corrected amplitude detuning
Tune distance to resonance
Parameter scan for 8-fold lattice
Virtual sextupole strength
Working point
Now islands are generated

## Slide 26
Example: Extraction at 6 GeV
DESY.
Excitation waveform
Test for proof-of-concept
Diffusion rate
(diffusion region)
Escape rate
(extraction region)
Simulation performed with Xsuite

## Slide 27
Example: Extraction at 6 GeV
DESY.
Test for proof-of-concept
100 ms spill example
Extracted beam
Emittance -> 13 nm rad
Converging beam
(negative correlation between angle and position)

## Slide 28
Example: Extraction at 6 GeV
DESY.
Extraction efficiency
Tentative considerations:
5.5 m available length for ESS & MSS
2m-long ESS
30 - 100 micron wire/ribbon width (ESS)
4mm blade for the MSS
Extraction efficiency as function of the ESS tilt misalignment
Extraction efficiency (%)

## Slide 29
Summary
DESY.
New low-emittance booster ring is needed for efficient charge accumulation
Low emittances lattices have a considerable amplitude detuning term
Test beam facility should offer beams after upgrade
Setting slow extraction with resonant island buckets is possible
E. C. Cortés García, I. Agapov and W. Hillert. Design of a resonant slow extraction from low emittance electron booster rings using transverse resonance island buckets. PRAB, Jan 2025. DOI: 10.1103/PhysRevAccelBeams.28.011601
E. C. Cortés García et al. Design of a resonant slow extraction from the planned DESY IV booster synchrotron. IPAC25, June 2025. DOI: 10.18429/JACoW-IPAC25-TUPM053

## Slide 30
Cristopher Cortés
edgar.cristopher.cortes.garcia@cern.ch