## Slide 1: Extraction Bump Digital Twin for NSRL slow extraction
6th Slow Extraction Workshop
Oct 6-9, 2025
Weijian (Lucy) Lin, Trevor Olsen, Eiad Hamwi, Kevin Brown, et al.
wlin1@bnl.gov

## Slide 2: Introduction to NSRL

## Slide 3: NASA Space Radiation Laboratory (NSRL)
Understanding the risks and uncertainties from the space radiation environment is crucial for NASA missions:
“In space, astronauts are exposed to ionizing radiation that is quantitatively and qualitatively different from terrestrial radiation. This environment includes protons and high-Z, high-energy (HZE) ions together with secondary radiation, including neutrons and recoil nuclei that are produced by nuclear reactions in spacecraft materials or tissue.”
- Risk of Radiation Carcinogenesis (2016)
NASA HRP Space Radiation Element

## Slide 4: NSRL Users and Experiments:
Three main types of experiments
Radiobiology – Primary objective of NSRL and NASA interest in a synchrotron facility
  Users often from university biomedical research labs receiving grants from NASA HRP
Microelectronics – Little interest in early years, now represents majority of beam hours
  Users from space and defence industry
Scientific Measurements – a handful of experiments per year, usually detector testing
  Users often from university or national physics labs

## Slide 5: Sources & Synchrotron Complex
Booster
Target
NSRL
Tandem
Linac
LtB
TtB
Ebis
EtB
Source machines:
Linac (proton)
EBIS (ion)
Tandem Van de Graaffs (ion)
AGS Booster synchrotron:
Accelerate beam to KE between 50 and 2500 MeV/n
Slow Extraction

## Slide 6: Resonant Slow Extraction
Thin septum (0.76 mm) at D3 + thick septum (15.2 mm) at D6 in the Booster
Third-integer (13/3) resonance created by four sextupoles: C8, F8, B4, E4
Triangular stable region in horizontal phase space, brought closer to the septa via local extraction bump
Particles with turn-by-turn orbit deviation larger than D3 septum thickness are extracted and kicked into D6 aperture
See Eiad’s presentation on SciBmad simulation

## Slide 7: Extracted Beam Spill
6 sec
7
Beam is extracted over 400 ms, every 4 to 6 seconds (~10% duty cycle)

## Slide 8: Booster Extraction Bump

## Slide 9: Booster extraction bump
Local bump via back-leg windings on five Booster main magnets: C7, D1, D4, D7, E1
Each main magnet has 16 main windings and 2 back-leg windings:
Bring closed orbit close to septa at D3 and D6
Can be simulated in two ways:
  dipole field errors
  zero-length horizontal kicker in the middle of dipoles

## Slide 10: Orbit distortion via local bump
When a bump is excited, the main magnet field is changed, and the closed orbit solution experiences a kick angle :
The new orbit at location in the Booster with bump on at location is:
The new angle at location is the derivative:

## Slide 11: Design bump strength calculation
Strengths of the five bumps can be calculated for a design bump with
  desired location and angle at D3 and D6 septa:
  minimal residual orbit in the rest of the Booster ring:
Coefficients of for location and angle on previous slide

## Slide 12: Bump simulation vs. measurement
Single bump measurement (C7 bump = 80 Amp shown) show good agreement with simulation
Bump defined as horizontal kicker in MAD-X, dipole field error in Bmad
618 MeV/n Silicon

## Slide 13: Bump design vs. Reality
Surprise discovery: operational bump is miles away from design bump due to years of blind tuning
618 MeV/n Silicon

## Slide 14: Digital Twin interface

## Slide 15: What is digital twin (DT)?
"A digital twin is a set of virtual information constructs that mimics the structure, context, and behavior of a natural, engineered, or social system (or system-of-systems), is dynamically updated with data from its physical twin, has a predictive capability, and informs decisions that realize value. The bidirectional interaction between the virtual and the physical is central to the digital twin.”
- Foundational Research Gaps and Future Directions for Digital Twins (2024)
National Academies of Sciences, Engineering, and Medicine report

## Slide 16: Digital Twin for extraction bump
1 GeV/n Proton
Load live bump currents from real machine
Simulated D3 + D6 orbit info using live bumps
Simulated bump orbit using live bumps
Real bump orbit measured by beam position monitors

## Slide 17: Digital Twin for extraction bump
1 GeV/n Proton
Use Bmad to fit any design bump shape
Send calculated bump currents to real machine
Time stamps in Booster cycle used to measure bump orbit
Save simulated and measured data

## Slide 18: Digital Twin for extraction bump
Booster magnet currents are time-dependent
  Bump currents are only turned on during NSRL extraction
Full bump setting interface allows changes to both timing and current
For normal operation, timing stays the same, fast setting interface allows changes to only current
370 MeV/n Silicon

## Slide 19: DT-assisted bump tuning
1 GeV/n Proton
Optimize operational bump by minimizing the residual orbit across the Booster ring

## Slide 20: DT-assisted bump tuning
Minimal change in intensity and spill for optimized bump with minimal residual orbit
1 GeV/n Proton

## Slide 21
DT-assisted bump tuning
Difficulty in recovering original design bump
  Lack of BPMs around the two septa
  D3 has been moved away from design location
  D6 flag was not operational now fixed

## Slide 22: NSRL Beam Line

## Slide 23: NSRL beam line
Nine quadrupoles, three dipoles (20 degree), two octupoles, four multi-wires
Designed to be achromatic after the 20-degree bend
Two octupoles create uniform square beam at the target

## Slide 24: Uniform beam with octupoles
480 MeV/n Iron
Uniformity is defined as the RMS deviation from the average beam intensity in the center uniform region
Uniformity of is provided for NSRL experiments

## Slide 25: Digital Twin for NSRL line
Initial beam parameters used by model
Currents and polarities of quadrupoles from live machine
Simulated dispersion of NSRL line using live machine info
Simulated vs. real transverse beam profile at MW302
180 MeV/n Silicon

## Slide 26: Summary
NSRL is a unique facility that utilizes slow extraction to provide high quality heavy-ion beam for industry and academia to conduct space radiation testing
Booster extraction bump plays a key role in the slow extraction process, but years of empirical tuning has shifted the operational bump very far away from design
We developed and tested a complete digital twin system for the extraction bumps, with bidirectional interaction between physical and virtual machines.
Future bump tuning will be easier and more streamlined with the help of DT
DT for NSRL line also under development, will facilitate beam uniformity optimization