## Slide 1: Advances in Instrumentation Session SX Workshop 2025, NY
Aakaash Narayanan and Peter Forck
09 October 2025

## Slide 2: Federico’s talk - Slow-Spill-Fast-Monitor at the CERN SPS F.– Our impressions
Characterization of time-resolved spill measurement urgently demanded by users
Different time domain requires optimized instrumentation
OTR monitor with PMT readout is appropriate for SPS extraction
Monitors can be quite sensitive to radiation background which might hinder high-frequency measurements
Performant DAQ required for operational usage.
CORE IDEA
WHY IT MATTERS
Spill ‘quality’ should be characterized to serve users adequately
Beam properties for SX are very sensitive to small device parameters modifications (more than for other types of beams) .
Special efforts required for adequate instrumentation
Different technologies must be evaluated (e.g. broadband processing versus single-particle readout versus)
KEY TAKEAWAYS

## Slide 3: QUESTIONS (general, perhaps ambitious concerning general usage of instrumentation)
Requirements: What spill quality really required by the users? What is the related accelerator physics quantity?
At least at GSI: Sometimes ‘language problems’ between users and accelerator physicists
concerning problem definition!
Mitigation strategy: What instrument is needed for a proper measurement and what is an appropriate online display? What are the accelerator physics quantities using the measurement for improving the beam quality?
Integration: Is the instrument and the GUI display appropriate for daily operation without expert invention?

## Slide 4: Takashi’s talk - Precision Quadrupole Field-Error Diagnostics in the J-PARC Main Ring – Our impressions
Developed QCPLM (Quadrupole-error analysis by Closed-orbit Perturbation-based Linearized Model).
Achieves 0.1 % accuracy in detecting time-varying ΔK/K ~ 1% errors from eddy-current effects in beam-ducts.
Confirmed with 3D EM simulations → corrected via trim coils → 20 % beam-loss reduction.
CORE IDEA
WHY IT MATTERS
Demonstrates a direct feedback loop between measurement to model to correction.
Identifies hidden dynamic optics errors that conventional static calibrations miss.
Supports J-PARC’s 1.3 MW upgrade while keeping activation under control.
Establishes a framework adaptable to any high-intensity ring (FNAL DR, SPS, PS, etc.).
Orbit Response Matrix used as precision optics diagnostic.
Linearized perturbation model robust against BPM malfunctions.
Correlation of eddy-current signatures with magnet geometry (UFO ducts) → hardware-specific insight.
KEY TAKEAWAYS

## Slide 5: QUESTIONS (perhaps ambitious)
Applicability: Could QCPLM be extended or tweaked to time-varying sextupole or extraction-bump fields that affect separatrix stability during SX?
Coupling Effects: Do eddy-current-induced quadrupole errors couple differently into horizontal vs vertical spill diffusion?
Integration: Can this ORM-based correction loop run in-situ during a slow-spill cycle (closed-orbit feedback)?
Diagnostics Synergy: How can this interface with WCM- or tune-feedback data to provide real-time optics correction?

## Slide 6: Stephen’s talk – Poincaré friendly tracking using complex tune modulations – Our impressions
Build a tune-modulation probe element that can be inserted into a lattice to study how complex longitudinal-transverse coupling drives chaotic diffusion.
Restores Poincaré surface-of-section visualization to modern multi-RF, multi-sextupole lattices.
Identifies when a tune-modulation drive line (from RF, chromaticity, etc.) aligns with a resonance-island response line leading to onset of chaos.
CORE IDEA
WHY IT MATTERS
Provides a diagnostic bridge between theoretical nonlinear dynamics and realistic machine conditions (RHIC, HSR).
Quantifies how synchrotron harmonics × chromaticity create modulation sidebands that can enhance or suppress extraction resonances.
Offers a generic tracking framework—portable to codes like StarGirl (& hopefully to BMAD, Xtrack) for probing tune-modulation resilience.
Demonstrated how polynomial chromaticity + dual-RF buckets yield multiple modulation harmonics qn.
Showed spectral crossings between n Qs and QI that mark chaotic zones.
Clean, integer-synchrotron-period tracking enables crisp phase-space “movies” giving more insight to dynamics.
KEY TAKEAWAYS

## Slide 7: QUESTIONS (perhaps ambitious, again!)
How can this tune-modulation probe be applied to study slow-extraction spill microstructure driven by RF noise or magnet ripple?
Can Poincaré mapping be used to quantify extraction-island stability as a function of slow tune-ramp rate?
What is the role of cross-plane coupling (H ↔ V) in spill diffusion, and can this model capture it?
Could such a probe element become a standard diagnostic block in simulation chains (e.g., Mu2e DR, SPS SX)?
How can the framework tie into real-time tune-feedback systems for predictive control?
Are there similar lattice element probes that can be used to isolate and investigate other lattice performance issues?